## Slide 1: F341 – Decoder Performance Restrictions due to Merge/MVP Index Parsing
Tim Hellman

## Slide 2: The Problem…
Merge/MVP Index Parsing Requires MV Construction
  Candidate List Reduction: Checks for equal MVs, reduces the list size
  Changes the size of the syntax element
High-Performance decoders separate CABAC from the decoder pipeline
  In AVC: CABAC state only depends on CABAC-decoded elements
  Merge/MVP Index Parsing breaks this model
  CABAC decoder can run far ahead of pixel decode
<number>

## Slide 3: The Issues…
Increased CABAC Logic Area
  Have to do MV construction in two places
Replication of Collocated vector buffers
  Have to manage two sets of collocated vector buffers
  Have to do reference picture management twice
Loss of Picture-level Parallelism
  Can no longer work on two pictures in parallel
Loss of Error Resiliency
  Errors in one frame cause parsing errors in subsequent frames
  Small error in one frame can wipe out an entire subsequent frame
CABAC Performance
  Fixed processing time added to each block

## Slide 4: CABAC Performance Hit
Use Skip block as an example
Skip Decoding (w/o MV construction) = 3 cycles
Neighbor Computation & MV storage = 15 clocks
500% CABAC slowdown!
<number>

## Slide 5: Proposed Solution
Merge/MVP Syntax Size only depends on spatial availability
  No need to manage collocated vectors
  No need for MV construction in CABAC
Still do List Reduction
  Insert zero vector in extra spot

## Slide 6: Experimental Results
 | Y BD-rate
RA-HE | -0.5%
RA-LC | -0.8%
LD-HE | -1.2%*
LD-LC | -1.3%*
* = Skewed by Class E