## Slide 1: Evaluation of SDIP
Jun Xu, Ehsan Maani, Ali Tabatabai, Teruhiko Suzuki
SONY

## Slide 2: Outline
Introduction
Proposed solutions & results
Conclusion

## Slide 3: Problem statement
SDIP introduces non-square partitions
  16x16 CU can be split into four 4x16/16x4
    A 4x16/16x4 PU can be further split into four 1x16/16x1
    RQT to support 1x16/16x1
  8x8 CU can be split into 2x8/8x2
Problems
  Non-square RQT support for 1x16/16x1, only!
    Extra coding path needed
  Increased HW cost for 1x16/16x1 and 2x8/8x2
 | 16x1 and 1x16 | 8x2 and 2x8 | Other size in WD3
Gate size | + 36 Kgate | + 11 Kgate | 13 Kgate

## Slide 4: Proposals
Solutions
  Disable 1x16/16x1 prediction & transform in SDIP
    Reduced HW complexity
Results
  Anchor is HM3 SDIP Branch with 16x1/1x16
  Cross-check by Samsung JCTVC-F555
 | All intra HE |  |  | All intra LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.0 | 0.0 | 0.1 | -0.1 | -0.2 | -0.2
Class B | 0.1 | 0.1 | 0.2 | 0.0 | -0.2 | -0.1
Class C | 0.2 | 0.3 | 0.4 | 0.1 | 0.0 | 0.1
Class D | 0.1 | 0.2 | 0.2 | 0.1 | 0.1 | 0.1
Class E | 0.1 | 0.2 | 0.2 | -0.1 | -0.1 | -0.2
Overall | 0.1 | 0.2 | 0.2 | 0.0 | -0.1 | 0.0
Enc Time[%] | 97% |  |  | 96% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 

## Slide 5: More Results
Results of disabling 8x2/2x8 are also provided.
  Anchor is HM3 SDIP Branch with 8x2/2x8
 | All intra HE |  |  | All intra LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.1 | 0.0 | 0.0 | 0.2 | 0.1 | 0.1
Class B | 0.4 | 0.0 | -0.1 | 0.4 | 0.2 | 0.1
Class C | 1.1 | 0.4 | 0.4 | 1.1 | 0.6 | 0.5
Class D | 1.2 | 0.6 | 0.7 | 1.2 | 0.6 | 0.7
Class E | 0.4 | -0.1 | -0.1 | 0.3 | 0.0 | 0.0
Overall | 0.7 | 0.2 | 0.2 | 0.6 | 0.3 | 0.3
Enc Time[%] | 90% |  |  | 89% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 

## Slide 6: Conclusion
Investigated SDIP.
  Disable 16x1/1x16 in SDIP.
  Disable 8x2/2x8 in SDIP.
Minor degradation in coding efficiency and 3~4% decreasing in complexity.
Proposed to remove 16x1/1x16 in SDIP.