## Slide 1: Proposal for CDR Text
TK Tan and A. Fujibayashi
NTT DOCOMO, Inc
6th JCT-VC meeting
Torino, Italy
14 to 22 July 2011

## Slide 2: Summary
Background
  Clean Decoding Refresh (CDR) was accepted into the WD at the Daegu meeting.
  At the Geneva meeting there were some questions and comments about the definition of the CDR.
Proposal
  To provide an improved definition of the CDR.
    Define the CDR picture
      Entry point for decoding a random accessible bitstream from the middle of the bitstream.
      Contains only Intra slices.
      Not affected by reference pictures prior to the CDR reset picture in decoding order.
    Define the CDR reset picture
      First picture to be decoded with an output order greater than the CDR picture.
      Picture which refers only to the CDR picture
      Picture where the reference pictures with decode order or output order smaller than the corresponding value for the CDR picture are marked as “unused_for_reference”
  To clarify the implicit decoding process by adding an explicit decoding process to the WD.
    When the picture is the CDR reset picture, reference pictures with decode order or output order smaller than the corresponding value for the CDR picture are
      not used for inter prediction, and
      marked as “unused_for_reference”

## Slide 3: Figure 1: Pictures in decode and output order in normal decoding
Pictures in Decode Order:
CDR
Poc 0
Pictures in Output Order:
CDR
Poc 0
P
Poc 6
B
Poc -5
B
Poc -1
B
Poc 1
B
Poc 5
B
Poc 2
B
Poc 3
B
Poc 4
B
Poc -4
B
Poc -3
B
Poc -2
P
Poc -6
P
Poc 6
B
Poc 1
B
Poc 5
B
Poc 2
B
Poc 3
B
Poc 4
B
Poc -5
B
Poc -1
B
Poc -4
B
Poc -3
B
Poc -2
P
Poc -6
…..
…..
CDR reset picture
CDR picture
This is the order in which the decoder decodes the pictures
This is the order in which the decoder outputs the pictures
pictures with output order smaller than the output order of the CDR picture
pictures prior to the CDR reset picture in decode order
pictures with output order greater than the output order of the CDR picture
pictures that follows the CDR reset picture in decode order
CDR picture

## Slide 4: Figure 2: Pictures in decode and output order in random access decoding starting at the CDR picture
Decode Order:
CDR
Poc 0
Output Order:
CDR
Poc 0
P
Poc 6
B
Poc 1
B
Poc 5
B
Poc 2
B
Poc 3
B
Poc 4
P
Poc 6
B
Poc 1
B
Poc 5
B
Poc 2
B
Poc 3
B
Poc 4
CDR reset picture
CDR picture

## Slide 5: Proposed changes to the WD
Definitions
  CDR reset picture: The first coded picture in decode order with an output order greater than the output order of the CDR picture. The CDR reset picture shall only refer to the CDR picture for inter prediction. After the CDR reset picture is decoded, all reference pictures with decode order or output order smaller than the corresponding value for the CDR picture shall be marked as “unused for reference”.
  clean decoding refresh (CDR) picture: A coded picture containing only slices with I slice types that indicates a starting point for decoding from the middle of a bitstream. The CDR picture shall not be affected by the marking process of the coded pictures prior to the CDR reset picture in decode order.
Decoding Process
  Add to section 8.2.2 Decoding process for reference picture lists construction
    If the current picture is the CDR reset picture, then reference pictures with decode order or output order smaller than the corresponding value for the most recently decoded CDR picture shall be inferred to be marked as “unused_for_reference” in subclauses 8.2.2.2 through 8.2.2.3.
  Add to section 8.2.3 Decoded reference picture marking process
    If the current picture is the CDR reset picture, then reference pictures with decode order or output order smaller than the corresponding value for the most recently decoded CDR picture shall be marked as “unused for reference”.

## Slide 6: Comparison of current and proposed text
Current Definition | Proposed Definition (Editorial) | Proposed Decoding Process
 | CDR reset picture: The first coded picture in decode order with an output order greater than the output order of the CDR picture. | 
clean decoding refresh (CDR) picture: A coded picture containing only slices with I slice types that | clean decoding refresh (CDR) picture: A coded picture containing only slices with I slice types that indicates a starting point for decoding from the middle of a bitstream. | 
causes the decoding process to mark all reference pictures except the current CDR picture as "unused for reference" before the decoding of the first picture following the current CDR with an output order greater than the current CDR picture. | The CDR reset picture shall only refer to the CDR picture for inter prediction. | Add to section 8.2.2 Decoding process for reference picture lists construction: If the current picture is the CDR reset picture, then reference pictures with decode order or output order smaller than the corresponding value for the most recently decoded CDR picture shall be inferred to be marked as “unused_for_reference” in subclauses 8.2.2.2 through 8.2.2.3.
All coded pictures that follow a CDR picture in output order can be decoded without inter prediction from any picture that precedes the CDR picture in output order. | After the CDR reset picture is decoded, all reference pictures with decode order or output order smaller than the corresponding value for the CDR picture shall be marked as "unused for reference“. | Add to section 8.2.3 Decoded reference picture marking process: If the current picture is the CDR reset picture, then reference pictures with decode order or output order smaller than the corresponding value for the most recently decoded CDR picture shall be marked as “unused for reference”.
All coded pictures with output order smaller than the current CDR are not affected by the deferred marking process. | The CDR picture shall not be affected by the marking process of the coded pictures prior to the CDR reset picture in decode order. |