## Slide 1: CAVLC Adaptation using difference counter (JCTVC-F395)
JCT-VC 6th Meeting in Torino, 14-22 July , 2011
Tomoyuki Yamamoto
SHARP Corporation

## Slide 2: Introduction
Counter based CAVLC adaptation (HM-3.0 / JCTVC-E143)
  Decoding table swap: assign smaller codeNum to probable syntax value
  Counter: enable conditional swap by counting syntax value occurrences
   need sum counter and counter normalization to prevent overflow
Difference counter based CAVLC adaptation (Proposed)
  Count difference of occurrences of successive codeNum
   possible to achieve conditional swap similar to counter based method
  (same coding efficiency as counter based method)
   no normalization, no sum counter, no counter swap
<number>

## Slide 3: Counter and difference counter
s0
s1
s2
s3
cnt[0]
cnt[1]
cn=0
cn=1
cn=2
cn=3
codeWord
counter table
sum counter
sum
cntNum
cn: CodeNum
decoding table
s4
cnt[2]
cn=4
s0
s1
s2
s3
dcnt[0]
dcnt[1]
cn=0
cn=1
cn=2
cn=3
codeWord
difference
counter
cn: CodeNum
decoding table
s4
dcnt[2]
cn=4
cntNum
- cnt[cn]: count of scn
- increment cnt[cn] and sum
- swap scn and scn-1 when cnt[cn]>=cn[cn-1]
- values in cnt[] are periodically normalized
-dcnt[cn]: diff. of counts of scn and scn-1
- decrement dcnt[cn] and increment dcnt[cn+1]
- swap scn and scn-1 when dcnt[cn] == 0
Counter based CAVLC adaptation (HM-3.0)
Difference counter based CAVLC adaptation (Proposed)
Notes: <number>

## Slide 4: Decoding table adaptation
<number>
dcnt[cn]--
cn +1 < cntNum
swap decoding table
dcnt[cn] == 0
N
Y
dcnt[cn+1] = min (dcnt[cn+1]+1, 3)
swap decoding table
N
Y
0<cntNum && cn<cntNum
Y
N
count
swap
0<cntNum && cn <cntNum
sum ++
swap decoding table
swap counter table
swap decoding table
normarization (right shift every counter values)
sum == 15
cnt[cn] ++
cnt[cn] ≧ cnt[cn-1]
Y
N
N
Y
N
Y
sum = 0
count
swap
normalize
Counter based CAVLC adaptation (HM-3.0)
Difference counter based CAVLC adaptation (Proposed)
Check if counter is used
Check if counter exists
Check if sum counter is full

## Slide 5: Experimental result
<number>
 | All Intra LC |  |  | Random Access LC |  |  | Low delay B LC |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0 | 0.0 | 0.0 | -0.1 | 0.0 | 0.2 |  |  |  |  |  | 
Class B | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | 0.1 | 0.0 | 0.1 | 0.3 | 0.0 | 0.0 | 0.4
Class C | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | -0.1 | -0.1 | 0.0 | -0.1 | 0.0 | 0.0 | -0.2
Class D | 0.0 | 0.0 | 0.0 | 0.0 | -0.1 | -0.3 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | -0.6
Class E | 0.0 | 0.1 | 0.0 |  |  |  | 0.1 | 0.7 | -0.9 | 0.0 | 0.4 | -1.0
Overall | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.2 | -0.1 | 0.0 | 0.1 | -0.3
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  | 
Proposed method (difference counter) compared to HM-3.0 (counter)
- Almost no impact on coding efficiency
- No encoding / decoding time increase
Results are cross checked by Sony

## Slide 6: Conclusion
Difference counter for CAVLC adaptation
  Achieves as large coding efficiency gain as counter based method
  Simplified adaptation
    no normalization process
    no sum counter
    no counter swap
Recommendation
  Propose to adopt difference counter method in WD and HM.
<number>