## Slide 1: Improvement of Sample Adaptive Offset with modified bit accuracy and restricted offsets (JCTVC-F396)
Takanori Yamazaki
Tomohiro Ikai
Yukinobu Yasugi
Tomoyuki Yamamoto
6th JCT-VC Meeting, Torino, Italy, July 2011
Sharp Corporation
Notes: <number>

## Slide 2: Overall summary
<number>
Proposal
  Bit accuracy modification (up to 10 bits) in SAO offset
  Offsets range restriction (4 to 6 bits) in SAO offset
Benefit
  Performance gain, HE-AI / HE-RA / HE-LB =
    0.1 %, 0.2 %, 0.1% in qp 12-27
    0.1 %, 0.1 %, 0.0% in qp 17-32
      up to 0.2% gain on high bit-rate condition
    0.1 %, 0.0 %,-0.1% in qp 22-37
      almost negligible impact on common condition
  Memory reduction
    40 % to 56 % memory reduction when internal bit depth is 8 bit to10 bit case respectively
Propose to adopt the improvement into HM
Notes: <number>

## Slide 3: Contents
Motivation
Proposal1: bit accuracy modification
Proposal2: offset range restriction
Experimental result
WD Text changes
Conclusion
<number>
Notes: <number>

## Slide 4: Motivation
SAO uses offsets to compensate distortions
  offsets representation are important
    e.g. offset bit accuracy and offset range
We studied the following aspects
  bit accuracy modification
    to achieve high coding efficiency
  offset range restriction
    to reduce required memory size
      currently 40960 bits (= 256 units * 16 classes * 10bits) is needed
<number>

## Slide 5: Proposal1: bit accuracy modification
  Higher bit accuracy is used
  The bit accuracy is set to be
    MIN (Internal bit depth, 10)
  From our experiments, higher bit accuracy produces higher coding efficiency in lower qp range
    In HM3.0, it is set to be up to 9 bit
<number>
Internal bit depth [bit] | 8 | 9 | 10 | 11 | 12 | 13 | 14
Proposed | 8 | 9 | 10 | 10 | 10 | 10 | 10
HM3.0 | 8 | 8 | 9 | 9 | 9 | 9 | 9
Notes: <number>

## Slide 6: Experimental results for Proposal1
Higher bit accuracy(Proposal1) achieves up to 0.2% gain in lower qp range.
  10 bit and 12 bit of Internal bit depth is tested and the results are ok.
  Short frames is used.
    49 frames for Class A and B 150 frames for Class C,D and E
<number>
 | High Efficiency |  | 
 | qp12-27 | qp17-32 | qp22-37
AI | 0.0 % | -0.1 % | 0.0 %
RA | -0.2 % | 0.0 % | 0.0 %
LB | -0.1 % | -0.1 % | 0.0 %
# negligible impact on
 | High Efficiency |  | 
 | qp12-27 | qp17-32 | qp22-37
AI | 0.0 % | -0.1 % | 0.0 %
RA | -0.2 % | -0.1 % | 0.0 %
LB | -0.2 % | -0.1 % | 0.0 %
Internal bit depth is 10 bit
Internal bit depth is 12 bit

## Slide 7: Proposal2: offset range restriction
Offset range restriction is introduced.
  The range is set to be -16 to 15 in 8 bit.
  Memory usage can be reduced up to 40 % compared to HM-3.0 when internal bit depth is 10 bits
    11bit => 6bit in 10 bit case
<number>
SAO bit accuracy [bit] | 8 | 9 | 10
Proposed offset range [bit] | 4 | 5 | 6
SAO bit accuracy 8bit
SAO bit accuracy 10bit
-16
15
-64
63
4bit
6bit
255
1023
-256
-1024
0
0

## Slide 8: Experimental results for Proposal2
The restriction’s impact is negligible
  Common test condition (Full frames) is used.
<number>
 | High Efficiency | Low Complexity
AI | 0.0 % | 0.0 %
RA | 0.0 % | 0.0 %
LB | 0.0 % | 0.0 %

## Slide 9: Experimental results (Proposal1+2)
 | HE-AI Y BDRate |  |  | LC-AI Y BDRate
 | qp12-27 | qp17-32 | qp22-37 | qp22-37
Class A | 0.0 | 0.0 | 0.0 | 0.0
Class B | 0.0 | -0.1 | 0.0 | 0.0
Class C | -0.1 | -0.1 | 0.0 | 0.0
Class D | -0.1 | -0.1 | 0.0 | 0.0
Class E | -0.1 | -0.1 | 0.0 | 0.0
Overall | -0.1 | -0.1 | 0.0 | 0.0
 | HE-RA Y BDRate |  |  | LC-RA Y BDRate
 | qp12-27 | qp17-32 | qp22-37 | qp22-37
Class A | -0.1 | -0.1 | -0.1 | 0.0
Class B | -0.3 | -0.1 | 0.0 | 0.0
Class C | -0.2 | -0.1 | 0.0 | 0.0
Class D | -0.1 | 0.0 | 0.1 | 0.0
Class E |  |  |  | 
Overall | -0.2 | -0.1 | 0.0 | 0.0
 | HE-LB Y BDRate |  |  | LC-LB Y BDRate
 | qp12-27 | qp17-32 | qp22-37 | qp22-37
Class A |  |  |  | 
Class B | -0.1 | -0.1 | 0.0 | 0.0
Class C | -0.1 | 0.0 | 0.1 | 0.0
Class D | -0.1 | 0.0 | 0.0 | 0.0
Class E | -0.2 | -0.1 | 0.1 | 0.1
Overall | -0.1 | 0.0 | 0.1 | 0.0
<number>
In normal qp range,
the proposal doesn’t change coding efficiency.
In lower qp range,
the proposal achive up to 0.2 % coding gain.

## Slide 10: WD Text changes
The following highlighted text is added
<number>

## Slide 11: Conclusion
<number>
Proposal
  Bit accuracy modification (up to 10 bits) in SAO offset
  Offsets range restriction (4 to 6 bits) in SAO offset
Benefit
  Performance gain, HE-AI / HE-RA / HE-LB =
    0.1 %, 0.2 %, 0.1% in qp 12-27
    0.1 %, 0.1 %, 0.0% in qp 17-32
      up to 0.2% gain on high bit-rate condition
    0.1 %, 0.0 %,-0.1% in qp 22-37
      almost negligible impact on common condition
  Memory reduction
    40 % to 56 % memory reduction when internal bit depth is 8 bit to10 bit case respectively
Propose to adopt the improvement into HM
Notes: <number>

## Slide 12
<number>
Thank you
Notes: <number>

## Slide 13: Additional test for other internal bit depth
Proposal 1+ 2
.
  Short frames is used for 8bit and 12 bit case
    49 frames for Class A and B 150 frames for Class C,D and E
<number>
 | High Efficiency |  | 
 | qp12-27 | qp17-32 | qp22-37
AI | 0.0 % | -0.1 % | 0.0 %
RA | -0.2 % | 0.0 % | 0.0 %
LB | -0.1 % | -0.1 % | 0.0 %
 | High Efficiency |  | 
 | qp12-27 | qp17-32 | qp22-37
AI | 0.0 % | 0.0 % | 0.0 %
RA | 0.0 % | 0.0 % | 0.0 %
LB | 0.0 % | 0.0 % | 0.0 %
Internal bit depth is 8 bit
Internal bit depth is 12 bit
 | High Efficiency |  | 
 | qp12-27 | qp17-32 | qp22-37
AI | 0.1 % | -0.1 % | 0.0 %
RA | -0.2 % | -0.1 % | 0.0 %
LB | -0.1 % | -0.0 % | 0.1 %
Internal bit depth is 10 bit (Common test condition)
Notes: <number>