## Slide 1: CE5: Run and level mode coding improvement in CAVLC (JCTVC-F408)
Yonsei University
Samsung Co. Ltd.

## Slide 2: Contents
CAVLC – run mode, intra
Level coding methods
VLC modification
Combine with F407
Combined results

## Slide 3: E446:Intra run mode coding
Table modification
  Current : two tables for 4x4 and 8x8, 16x16, 32 x32
  8x8 and 16x16 has different distribution in run-level coding
    Make another [Tr1][max_run] table for 16x16, 32x32 blocks
    Original table is changed based on new training
  “vlcNum” table increment can be avoid (as combining with ‘vlc modification’)  100 byte increment (432 bytes in E446)

## Slide 4: E446:Intra run mode coding
 | HM 3.0 |  | Proposed | 
 | vlcNum Table | Parameter table | vlcNum Table | Parameter table
4x4 | 1x29 | 5x15 | 1x15 | 5x15
8x8 |  | 5x29 (same table) | 5x29 | 5x29
≥ 16x16 | 1x29 |  | 5x29 | 5x29
vlc modification (13 elements)

## Slide 5: Level coding methods
Modifications to VLC table selection in level mode
  Use different threshold set depends on block type (intra luma, P luma, B luma, or chroma)
  Threshold refinement using RQT depth.
    Intra Luma, Th = τ – RQTdepth
    Inter Luma, Th = τ – RQTdepth – (RQTdepth>0?1:0)
    Chroma, Th = τ

## Slide 6: vlc modification
Parameterized vlc
  Extends vlcNum 0~5 and 8
  Make “transition prefix length” to variable from constant, “6”.
  Extends vlcNum 8 to Unary-Max coding  most of cases ‘vlcNum 0’ might be merged to unary-max coding
vlcNum == 5
cn < param x 1<<vlcNum
START
END
Unary-Max
coding
Coding
Methods1
Coding
Methods 2

## Slide 7: Vlc modification
Run mode vlcNum parameterization
  Four modes are available.
  In very low maxrun( < th1), unary-max,
  In low maxrun (< th2), vlcNum = 1 & parameter = maxrun+1
  In high maxrun(< th3), vlcNum = 2 & parameter = (maxrun+1)>>1
  In very high maxrun, constant vlcNum and parameter
Level mode vlcNum parameterization
  In first parameter, vlcNum is same as before
  Parameter is defined for luma and chroma, separately

## Slide 8
Proposal
  For mapping {lev, run} pairs to code number cn, formula and parameter tables for cn1 & cn2 are used instead of run-level table.
  Parameter tables for cn1 & cn2 are determined according to tr1s(=0 / ≠0) and trSize(=4x4 / ≥8x8)
  cn1 is cn for {lev=0, run=maxrun+1}.
  cn2 is cn for {lev=1, run=0}.
Run-mode coding improvement with table reduction in CAVLC (JCTVC-F407)

## Slide 9: Combined results
Table | Features | HM3.0 | Proposal | Diff
INTRA(E446) | 4x4 | 5*15 | 5*15 | 145
 | 8x8 | 5*29 | 5*29 | 
 | 16x16 |  | 5*29 | 
 | all | 220 | 356 | 
threshold for level | I | 1*5 | 1*6 | 19
 | P |  | 1*6 | 
 | B |  | 1*6 | 
 | Chroma |  | 1*6 | 
 | all | 5 | 24 | 
vlcNum | INTRA | 1*29 | 4*4 (13 elems) | -68 (-73 elems)
 |  | 1*29 |  | 
 | INTER | 1*29 | 2*4 (8 elems) | 
 |  | 1*29 |  | 
 | Chroma | 0 | 3*4 (10 elems) | 
 | level | 0 | 2*6 | 
 | all | 116 | 48 | 
INTER (F407) | run-level table | 28*29 | 0 | -636 (-258 elems)
 | tables for cn0 & cn1 | x | 4*1*29+4*1*15 | 
 | all | 812 | 176 | 
sum |  | 1153 | 614 | -540 (-167 elems)

## Slide 10: Combined results
All Intra LC |  |  | Random Access LC |  |  | Low delay B LC |  | 
Y | U | V | Y | U | V | Y | U | V
-0.5 | -0.2 | -0.1 | -0.2 | 0.3 | 0.5 |  |  | 
-0.6 | -0.1 | -0.2 | -0.2 | 0.1 | 0.1 | -0.1 | 0.3 | 0.0
-0.7 | -0.4 | -0.4 | -0.4 | -0.2 | -0.2 | -0.2 | 0.1 | -0.2
-0.9 | -0.5 | -0.5 | -0.4 | -0.3 | -0.3 | -0.2 | 0.1 | -0.1
-0.6 | -0.2 | -0.2 |  |  |  | -0.2 | 0.6 | -0.5
-0.7 | -0.3 | -0.3 | -0.3 | 0.0 | 0.0 | -0.2 | 0.3 | -0.2
103% |  |  | 100% |  |  | 100% |  | 
100% |  |  | 100% |  |  | 100% |  | 
F408 only.

## Slide 11: Combined results
Combined with F407
All Intra LC |  |  | Random Access LC |  |  | Low delay B LC |  | 
Y | U | V | Y | U | V | Y | U | V
-0.5 | -0.2 | -0.2 | -0.4 | 0.2 | 0.4 |  |  | 
-0.6 | -0.4 | -0.4 | -0.4 | 0.3 | 0.1 | -0.1 | 1.5 | 0.7
-0.8 | -0.7 | -0.7 | -0.5 | -0.2 | -0.3 | 0.0 | 0.6 | 0.5
-0.9 | -0.8 | -0.9 | -0.6 | -0.4 | -0.3 | 0.0 | 0.7 | 0.5
-0.6 | -0.1 | -0.2 |  |  |  | 0.2 | 0.3 | -0.8
-0.7 | -0.5 | -0.5 | -0.4 | 0.0 | 0.0 | 0.0 | 0.8 | 0.3
105% |  |  | 101% |  |  | 101% |  | 
100% |  |  | 99% |  |  | 99% |  | 

## Slide 12: Conclusion
The proposed run and level mode coding scheme considers various context models based on block size, prediction mode and RQT depth.
Table size increase 91 bytes (without F407), and decrease 176 bytes (with F407), achieving the performance improvement.
Therefore, we recommend the proposed method to adopt HM
The proposed method is cross-verified by SHARP (JCTVC-F404)

## Slide 13: END
- Thank you !