## Slide 1: Joint coding of CU splitting flag and inter modes based on HM 3.1 JCTVC-F418
ZTE Corporation
Wen Zhang

## Slide 2: Outline
Acknowledgement
Introduction
Experimentation
Conclusion

## Slide 3: Acknowledgement
MediaTek and LGE were invited to cross check this proposal.
Cross check results were reported in JCTVC-F117(LGE) and JCTVC-F279(MediaTek).

## Slide 4: Introduction
In JCTVC-D275 and JCTVC-E072, slice-based adaptive representing methods of syntax elements related to inter modes were proposed.
In JCTVC-E258, a context-dependent classification method was introduced as supplementary part of CU-depth dependent while coding CU splitting flag and inter modes.
In this proposal, above two basic ideas were harmonized together and further studied.

## Slide 5: summary of CU splitting flag and inter modes

## Slide 6: CU splitting flag and inter modes coding in 16 types
CU-depth | Prediction mode-top CU | Prediction mode-left CU | Coding Type
CU size > 8x8 (min) | SKIP | SKIP | 0
 | INTER | SKIP | 1
 | SKIP | INTER | 
 | INTRA | SKIP | 2
 | SKIP | INTRA | 
 | CU Splitting | SKIP | 3
 | SKIP | CU Splitting | 
 | INTER | INTER | 4
 | INTRA | INTER | 5
 | INTER | INTRA | 
 | CU Splitting | INTER | 6
 | INTER | CU Splitting | 
 | INTRA | INTRA | 7
 | CU Splitting | INTRA | 8
 | INTRA | CU Splitting | 
 | CU Splitting | CU Splitting | 9
CU size==8x8(min) | SKIP | SKIP | 10
 | INTER | SKIP | 11
 | SKIP | INTER | 
 | INTRA | SKIP | 12
 | SKIP | INTRA | 
 | INTER | INTER | 13
 | INTRA | INTER | 14
 | INTER | INTRA | 
 | INTRA | INTRA | 15

## Slide 7: Solution
Codeword tables of all 16 coding types were updated for each inter slices
  It’s based on statistical results of previous coded slices, and all counter results of each type were sorted to refresh codeword tables for next slice with same slice QP.
Codeword tables here were maintained to be same both in encoder and decoder
  Thus, there is no need to transmit explicit coding types which were described in JCTVC-D275 and JCTVC-E072.
Unified representing method of CU splitting flag and inter modes had been implemented both in CABAC and CAVLC
  The motivation is to reduce flags / bins needed to code these syntax elements.

## Slide 8: IPCM Mode
It had been adopted into HM 3.1 which was disabled by default.
Two methods to enable IPCM were tested in this proposal.
It was proposed that IPCM could be enabled in intra slice while CU size greater than 16x16 and in inter slice while CU size greater than 8x8 (min).
  The impact on coding efficiency was observed only in AI-LC configuration, with a loss of 0.1% BD-rate.

## Slide 9: Pred_split_flag
Pred_split_flag was defined while CU-depth equals to 0 or 1.
  If this flag equals to 1, it means not only CU of current depth with split_flag equals to 1 but also all CUs here of current depth plus one with split_flags equal to 1.
In order to avoid worse coding result, constrained conditions were added to control the presence of pred_split_flag in each slice.
0.1% BD-rate gain was achieved by Pred_split_flag for AI-LC and RA-LC configurations.

## Slide 10: Test Results-1
Version A (without Pred_split_flag, default with IPCM disabled) [anchor HM 3.1]

## Slide 11: Test Results-2
Version A (without Pred_split_flag, IPCM enabled while CU size > 8x8)
[anchor HM 3.1]

## Slide 12: Test Results-3
Version A (without Pred_split_flag, IPCM enabled in intra slice while CU size > 16x16 and in inter slice while CU size > 8x8) [anchor HM 3.1] ---proposed

## Slide 13: Test Results-4
Version B (with Pred_split_flag, default with IPCM disabled) [anchor HM 3.1]
Version B (with Pred_split_flag, IPCM enabled while CU size > 8x8) [anchor HM 3.1]

## Slide 14: Results Analysis-1
Joint coding Method for CU splitting flag and inter modes
It improved about 0.5% BD-rate for CAVLC configurations comparing to HM 3.1.
CABAC itself did good job coding these syntax elements. There is almost no gain observed for coding efficiency (with 0.1% BD-rate deviation, some became worse).

## Slide 15: Results Analysis-2
Proposed IPCM mode (in intra slice CU size > 16x16 and in inter slice CU size > 8x8)
Two methods to enable IPCM were tested.
It has more impact on intra slice than inter slice.
Proposed method was observed have impact only on AI-LC configuration, with a loss of 0.1% BD-rate.

## Slide 16: Results Analysis-3
Pred_split_flag while CU-depth equals to 0 or 1
There is some redundancy existed in current CU splitting flag signaling.
Pred_split_flag can bring us 0.1% BD-rate gain for AI-LC and RA-LC configurations.
All intra LC |  | 
-0.1 | -0.1 | -0.1
Random access LC |  | 
-0.1 | -0.1 | -0.1
Low delay (B) LC |  | 
0.0 | 0.0 | 0.0
Low delay (P) LC |  | 
0.0 | -0.2 | -0.2

## Slide 17: Conclusion
The best choice to enable IPCM mode should be Intra Slice with CU size greater than 16x16, Inter Slice with CU size greater than 8x8 (min).
  It’s suggested to adopt this into HM.
Joint coding of CU splitting flag and inter modes could improve about 0.5% BD-rate for CAVLC, pred_split_flag brought further 0.1% BD-rate gain for AI-LC and RA-LC.
  It’s suggested to adopt both of them or the first part.
It’s proposed to unify representing method of CU splitting flag and inter modes both in CAVLC and CABAC.
  CABAC itself did good job while coding these syntax elements.
  Unification can help us to simplify spec text of splitting flag and inter modes.

## Slide 18: Revised Spec Text

## Slide 19: Revised Spec Text

## Slide 20: Revised Spec Text