## Slide 1: JCTVC-F459:Parsing friendly intra mode coding
Wei-Jung Chien, Xianglin Wang, and Marta Karczewicz
Qualcomm

## Slide 2: Introduction
HM3.0 intra mode decoding diagram

## Slide 3: Introduction
Chroma intra prediction mode
intra_chroma_pred_mode | IntraPredMode[ xB ][ yB ], X |  | 
 | 0 | 1 | X (X>1)
0 | N\A | 0 | 0
1 | 1 | N\A | 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
4 | 0 | 1 | X
Note: mode 2 could be DC mode or Planar mode

## Slide 4: Introduction
In current intra mode coding, different binerization are used depends on the intra prediction mode of the neighboring blocks.
  Affecting parsing throughput for CABAC (E-118).
  Two set of VLC tables are used.
Suggestions
  Fixed number of candidate modes (same suggestions in F340 and F378)
  Separate Planar mode and DC mode
  Removing codeword pruning in the coding of chroma intra prediction mode.
Advantages
  No line buffer needed for parsing
  Increase parsing throughput for CABAC by separate parsing and decoding
  Reducing VLC tables from 2 sets to 1 set

## Slide 5: Proposed method (luma intra prediction mode)
Fixed number of MPMs. 4 MPMs are currently used.
Separate Planar mode and DC mode in MPM coding
Use closest intra modes as additional MPMs.
One context for each bin of rem_intra_pred_mode
MPM1=10
MPM3=3, MPM4=4, if 18 intra modes are allowed
MPM3=18, MPM4=19, if 35 intra modes are allowed

## Slide 6: Luma intra mode
If candIntraPredModeA = candIntraPredModeB
  MPM1 = candIntraPredModeA
  MPM2 = Planar mode or DC mode (if candIntraPredModeA is Planer mode)
  MPM3 and MPM4 are assigned with two closest intra modes respect to MPM1.
If candIntraPredModeA != candIntraPredModeB
  MPM1 = min(candIntraPredModeA, candIntraPredModeB)
  MPM2 = max(candIntraPredModeA, candIntraPredModeB)
  If MPM2/MPM1 is equal to Planar mode, MPM3 and MPM4 are assigned with two closest intra modes respect to MPM1/MPM2.
  Otherwise, MPM4 = Planer mode, MPM3 is assigned with one of the closest intra modes respect to MPM1 or MPM2, or DC mode.

## Slide 7: Proposed method (luma intra prediction mode)
Fixed number of chroma intra prediction modes. 6 modes are currently used.
Replace horizontal, vertical, and DC prediction with two closest modes and one perpendicular mode.
Luma intra prediction mode =10
{3, 4, 8} are used if 18 intra modes are allowed
{18, 19,8} are used if 35 intra modes are allowed

## Slide 8: Simulation results
 | Intra |  |  | Intra LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.3 | 0.0 | 0.1 | -0.2 | 0.0 | -0.1
Class B | -0.3 | -0.3 | -0.2 | -0.2 | -0.4 | -0.3
Class C | -0.3 | -0.5 | -0.5 | -0.3 | -0.5 | -0.5
Class D | -0.4 | -0.4 | -0.5 | -0.3 | -0.4 | -0.6
Class E | -0.4 | -0.1 | -0.1 | -0.2 | -0.5 | -0.4
All | -0.33 | -0.3 | -0.3 | -0.22 | -0.4 | -0.4
Enc Time[%] | 102% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 9: Conclusions
Fixed number of candidate mode are proposed to improve parsing throughput.
0.3% and 0.2% BR-rate reduction are observed.
Thanks to Samsung for performing crosscheck (JCTVC-F721)