## Slide 1
<number>
JCTVC-F468: eBrisk’s Adaptive Interpolation Filtering Technique Using Samsung’s Newly Proposed Fixed Filters
Michael Horowitz, eBrisk Video
6th JCTVC Meeting in Torino
14-22 July 2011

## Slide 2: HM 3.0 Interpolation Filtering
<number>
¼ 8-tap | -1, 4, -10, 57, 19, -7, 3, -1
½ 8-tap | -1, 4, -11, 40, 40, -11, 4, -1
Sub-sample position | Vertical | Horizontal
ai.j | None | F_1/4
bi.j | None | F_1/2
ci.j | None | F_3/4
di.j | F_1/4 | None
ei.j | F_1/4 | F_1/4
fi.j | F_1/4 | F_1/2
gi.j | F_1/4 | F_3/4
hi.j | F_1/2 | None
ii.j | F_1/2 | F_1/4
ji.j | F_1/2 | F_1/2
ki.j | F_1/2 | F_3/4
ni.j | F_3/4 | None
pi.j | F_3/4 | F_1/4
qi.j | F_3/4 | F_1/2
ri.j | F_3/4 | F_3/4

## Slide 3: Proposed AIF Technique (Luma)
<number>
Same as proposed technique in JCTVC-F216.
Configuration | Sub pel | Tap length | Filter coefficients
All configurations | 1/4 pel | 7 | -2, 5, -11, 58, 18, -6, 2
 | 1/2 pel | 6 | 2, -9, 39, 39, -9, 2
Samsung’s filters (JCTVC-F247) are used as default filters
Configuration | Sub pel | Tap length | Filter coefficients
All configurations | 1/4 pel | 7 | a0, a1, a2, a3, a4, a5, a6
 | 1/2 pel | 6 | b0, b1, b2, b2, b1, b0
AIF filters

## Slide 4: Simulation Results (Luma)
<number>
 | Low delay (P) HE |  |  | Low delay (P) LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0 | -0.2 | -0.5 | -2.7 | 0.3 | 0.1
Class C | 0.1 | 0.1 | -0.1 | -0.8 | 0.2 | 0.3
Class D | 0.9 | 0.9 | 0.5 | 0.4 | 0.7 | 0.8
Class E | -0.4 | -0.3 | -0.7 | -5.3 | -0.9 | -1.4
Overall | 0.1 | 0.2 | -0.2 | -1.9 | 0.1 | 0.0
Enc Time[%] | 101% |  |  | 105% |  | 
Dec Time[%] | 98% |  |  | 99% |  | 

## Slide 5: Simulation Results (Luma)
<number>
 | Low delay (B) HE |  |  | Low delay (B) LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.1 | 0.0 | -0.1 | -1.4 | 0.2 | 0.0
Class C | 0.1 | 0.1 | 0.0 | -0.4 | 0.3 | 0.3
Class D | 0.5 | 0.9 | 0.8 | 0.5 | 0.9 | 0.4
Class E | -0.3 | -0.6 | -0.4 | -2.8 | -0.6 | -0.4
Overall | 0.1 | 0.1 | 0.1 | -0.9 | 0.3 | 0.1
Enc Time[%] | 98% |  |  | 98% |  | 
Dec Time[%] | 98% |  |  | 97% |  | 

## Slide 6: Simulation Results (Luma)
<number>
 | Random Access HE |  |  | Random Access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.3 | -0.4 | -0.5 | -1.3 | 0.0 | -0.2
Class B | 0.0 | -0.1 | -0.1 | -0.1 | 0.0 | -0.1
Class C | 0.1 | 0.1 | 0.1 | 0.2 | 0.1 | 0.1
Class D | 0.1 | 0.1 | 0.2 | 0.5 | 0.2 | 0.3
Class E |  |  |  |  |  | 
Overall | 0.0 | -0.1 | -0.1 | -0.2 | 0.1 | 0.0
Enc Time[%] | 98% |  |  | 98% |  | 
Dec Time[%] | 98% |  |  | 97% |  | 

## Slide 7: Proposed AIF Technique (Chroma)
<number>
Same technique proposed in JCTVC-F216
(using the HM 3.0 default Chroma filters)
Notes: <number>

## Slide 8
<number>
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.1 | -0.4 | -1.0 | -2.7 | -2.5 | -2.6
Class C | 0.1 | 0.0 | -0.2 | -0.8 | -0.5 | -0.4
Class D | 1.0 | 0.1 | 0.5 | 0.6 | 0.1 | 0.5
Class E | -0.1 | -2.0 | -3.6 | -4.9 | -13.5 | -8.8
Overall | 0.2 | -0.5 | -0.9 | -1.8 | -3.4 | -2.4
Enc Time[%] | 98% |  |  | 104% |  | 
Dec Time[%] | 97% |  |  | 98% |  | 
Simulation Results (Luma + Chroma)

## Slide 9
<number>
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.1 | 0.0 | -0.4 | -1.4 | -1.3 | -1.2
Class C | 0.1 | 0.1 | -0.1 | -0.5 | 0.0 | -0.2
Class D | 0.6 | 0.6 | 0.8 | 0.6 | 0.7 | 0.6
Class E | 0.1 | -1.0 | -2.1 | -2.4 | -9.0 | -6.6
Overall | 0.2 | 0.0 | -0.3 | -0.8 | -1.9 | -1.5
Enc Time[%] | 98% |  |  | 98% |  | 
Dec Time[%] | 97% |  |  | 98% |  | 
Simulation Results (Luma + Chroma)

## Slide 10
<number>
 | Random Access HE |  |  | Random Access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.3 | -0.4 | -0.5 | -1.2 | -0.5 | -0.5
Class B | 0.1 | 0.1 | 0.2 | -0.1 | 0.1 | 0.1
Class C | 0.1 | 0.1 | 0.1 | 0.2 | 0.1 | 0.1
Class D | 0.1 | 0.1 | 0.2 | 0.5 | 0.2 | 0.3
Class E |  |  |  |  |  | 
Overall | 0.0 | 0.0 | 0.0 | -0.1 | 0.0 | 0.0
Enc Time[%] | 98% |  |  | 98% |  | 
Dec Time[%] | 97% |  |  | 97% |  | 
Simulation Results (Luma + Chroma)

## Slide 11: Conclusion
<number>
The proposed combination yields good trade-offs between BD-rate performance and complexity:
  AIF (Luma): 0.5% gain for 97% average decoding complexity and 99% encoding complexity
  AIF (Luma + Chroma): 0.4% / 1.0% / 0.9% Y/U/V gains for 97% average decoding complexity and 99% average encoding complexity
Proposed combination provides a significant gain over HM 3.0 while using shorter filters (6-tap and 7-tap instead of 8-tap).
Notes: <number>