## Slide 1: JCTVC-F470: Parsing Robustness for Merge/AMVP

## Slide 2
Parsing problem on temporal motion vector predictor was reported last meeting
It is caused by dependency between deriving process for Merge/AMVP candidates list and parsing process for Merge/AMVP indices
It also causes performance issue on CABAC/CAVLC.
Introduction
Derive Merge candidates list
Get list size
Decode Merge indices
by using list size
Merge_idx | bin
0 | 0
1 | 10
2 | 110
3 | 1110
4 | 1111
Merge_idx | bin
0 | 0
1 | 1
List size=5
List size=2
CABAC/CAVLC
Decoding process in HM3.0 (Merge)
Check availability for mv of neighbor and co-located block
Reduce duplicate candidate by checking InterDir, mv, refIdx
・
・
Decouple creating list process and parsing index process
Add Merge/AMVP candidates to compensate coding loss
Parsing and performance problem
When list size is unknown, it becomes impossible to decode all bit stream (in the case that colPic is lost and temporal motion vector becomes unknown )
During parsing, it is needed to create list. It affects performance of CABAC/CAVLC

## Slide 3
Modify a decoding process for Merge/AMVP indices to use fixed list size
  Use truncated unary codes of fixed maximum length 5 for Merge, 3 for AMVP
   Decouple creating list process and parsing index process
Disable adaptive switching method for CABAC/CAVLC
  To avoid the parsing problem, following two adaptive switching methods are disabled
    Adaptive context selection for inter_pred_flag and ref_idx_lx (CABAC)  ctxIdx is fixed to 0
    Adaptive combined coding for inter_pred_flag and ref_idx_lx (CAVLC)  use_combined_inter_pred_ref is fixed to true in B slice
  Upper methods refer neighbor inter_pred_flag and ref_idx_lx, which become incorrect by occurrence of error, such as packet loss
Proposed method ( Fixed list size method )
Derive Merge candidates list
Decode Merge indices by using fixed list size
Merge
Fixed list size method
CABAC/CAVLC
(anchor HM3.0+bugfix146)

## Slide 4
Experimental result for fixed list size method
About 1.4% loss
Merge_idx | bin
0 | 0
1 | 10
2 | 110
3 | 1110
4 | 1111
List size=5
amvp_idx | bin
0 | 0
1 | 10
2 | 11
List size=3
Evaluate proposed method in which Merge/AMVP indices are coded in truncated unary codes of fixed maximum length
Truncated unary codes
(anchor: HM3.0+bugfix146)
Fixed list size method can solve parsing and performance problem, but its coding loss is large
 Proposed candidates are added to compensate coding loss

## Slide 5
Encoding process
Remove duplicate candidates
Add proposed candidates
following original ones
Select candidate
for encoding
Encode index
by using fixed list size
index | candidate
0 | Left
1 | Co-located
2 | New one
3 | New one
4 | New one
fixed list size=5
Original candidate after removing duplicate candidate
added proposed candidate
Decode index
by using fixed list size
Derive candidate list
Remove duplicate candidates
Add proposed candidates
following original ones
Derive candidate list
Decoding process
Use candidate [index]
for decoding
index
Creating bi-prediction Merge candidate
Fixed list size method with additional proposed candidates
CABAC/CAVLC
Merge/AMVP

## Slide 6
Additional proposed candidates
Consideration about Merge mode:
Prediction type of Merge mode is based on Merge candidates.  If all Merge candidates are uni-directional, prediction type of Merge mode can’t select bi-directional, even though a situation which bi-directional saves a lot of bits
Concept:
Bi-directional Merge candidates are created by using original Merge candidates, and then added to Merge candidate list
Proposed candidate list:
Combined bi-directional Merge candidate (candidate 1)
Scaled bi-directional Merge candidate (candidate 2)
Zero vector Merge/AMVP candidate (candidate 3)

## Slide 7
Merge_idx | L0 | L1
0 | mvL0_A, ref0 | -
1 | - | mvL1_B, ref0
2 |  | 
3 |  | 
4 |  | 
Merge_idx | L0 | L1
0 | mvL0_A, ref0 | 
1 |  | mvL1_B, ref0
2 | mvL0_A, ref0 | mvL1_B, ref0
3 |  | 
4 |  | 
mvL0_A(uni)
mvL1_B(uni)
Candidate 1: combined bi-directional Merge candidate
mvL0_A(bi)
mvL1_B(bi)
Original Merge candidate list
Merge candidate list after adding combined candidates
combine
L0R0
L1R0
Cur
Bi-directional Merge candidates are created by combining original Merge candidates
Two candidates in original candidates, which have mvL0 and refIdxL0 or mvL1 and refIdxL1, are used to created bi-directional Merge candidates
combine

## Slide 8
Candidate 2: scaled bi-directional Merge candidate
Merge_idx | L0 | L1
0 | mvL0_A, ref0 | -
1 | - | mvL1_A, ref1
2 |  | 
3 |  | 
4 |  | 
Merge_idx | L0 | L1
0 | mvL0_A, ref0 | -
1 | - | mvL1_A, ref1
2 | mvL0_A, ref0 | mvL0’_A, ref0’
3 | mvL1’_A, ref1’ | mvL1_A, ref1
4 |  | 
mvL0_A(ref0)
mvL0’_A(ref0)
mvL1_A(ref1)
mvL1’_A(ref1)
L0R0
Cur
Bi-directional Merge candidates are created by scaling original Merge candidates
One candidate in original candidates, which have mvLX and refIdxLX, is used to created bi-directional Merge candidates
Original Merge candidate list
Merge candidate list after adding scaled candidates
scaling
L0R1
L1R0
L1R1

## Slide 9
Merge_idx | L0 | L1
0 | mvL0_A, ref0 | -
1 | - | mvL1_B, ref0
2 | mvL0_A, ref0 | mvL1_B, ref0
3 | - | -
4 | - | -
Merge_idx | L0 | L1
0 | mvL0_A, ref0 | 
1 |  | mvL1_B, ref0
2 | mvL0_A, ref0 | mvL1_B, ref0
3 | (0,0), ref0 | (0, 0), ref0
4 | (0,0), ref1 | (0, 0), ref1
Candidate 3: Zero vector Merge/AMVP candidate
Original Merge candidate list
Merge candidate list after adding new ones
Add zero vector
Zero vector Merge/AMVP candidates are created by combining zero vector and refIdx
amvp_idx | L0
0 | mvL0_A
1 | mvL0_B
2 | -
amvp_idx | L1
0 | mvL1_A
1 | -
2 | -
amvp_idx | L0
0 | mvL0_A
1 | mvL0_B
2 | (0, 0)
amvp_idx | L1
0 | mvL1_A
1 | (0, 0)
2 | -
Original AMVP candidate list
AMVP candidate list after adding new ones
Add zero vector

## Slide 10
Experimental result
Fixed list size method
Proposed method
About 1.4% loss
About 0.3% gain
Evaluate a proposed method in which the candidate 1,2 and 3 are applied to fixed list size method
A proposed method compensates coding loss of fixed list size method
(anchor HM3.0+bugfix146)
Cross checked by TI (JCTVC-F090)
Proposed method solves parsing and performance. Moreover, it compensates coding loss of fixed list size method

## Slide 11
Experimental result for proposed candidate 1 and 2 (no parsing issue)
Evaluate combined and scaled bi-directional Merge candidate in HM3.0
Proposed candidates improve coding efficiency relative to HM3.0
(anchor HM3.0+bugfix146)
Proposed candidate 1, 2
Cross checked by TI (JCTVC-F090)

## Slide 12
Additional investigation on complexity reduction
An additional experiment was conducted to address of concerns about complexity raised in cross check report (JCTVC-F090)
Some limitations on complexity reduction are applied to proposed method
  combined bi-directional Merge candidate (candidate1)  The maximum number is limited to 5
  scaled bi-directional Merge candidate (candidate 2)  The maximum number is limited to 1
    It is limited that only candidate, which don't need scaling calculation, are added to Merge candidates list
  zero vector Merge candidate (candidate 3)  The maximum number is limited to 2
Cross checked by TI (JCTVC-F090)
(anchor HM3.0+bugfix146)
Proposed method with complexity reduction
A proposed method with complexity reduction compensates coding loss of fixed list size method

## Slide 13
Proposed method solves parsing and performance problem
  It’s related to JCTVC-F347
Moreover , it compensates coding loss of fixed list size method by adding proposed candidates ( about 0.3% gain )
We recommend that a proposed approach for the parsing robustness be adopted in the next version of HM/WD as a basis for further study in a CE
Conclusion