## Slide 1: JCTVC-F471: Picture Adaptive 1/8-pel Motion Compensation Method

## Slide 2
A low delay P setting was defined as an optional test condition last meeting
The difference of coding efficiency between low delay B and P is about 6%
  Large difference for BQTerrace, BQSquare and PartyScene
  Small difference for Basketball, Racehorses (class D) and Kimono
This difference is caused by GPB off
  not only the number of reference list is restricted to one, but also bi-predictive reference to one single picture cannot be used
However, low delay P is beneficial in terms of memory bandwidth and memory capacity
Introduction
Evaluate picture adaptive 1/8-pel motion compensation for low delay P
RD performance drop of low delay P (GPB off)

## Slide 3
Concept
  B slice can refer one single reference picture with two 1/4-pel mv  derive 1/8-pel accuracy prediction samples by bi-linear interpolation using bi- prediction
  P slice can refer one single reference picture with only one 1/4-pel mv  To improve coding efficiency, to use 1/8-pel motion vector is expected to be helpful
Picture adaptive 1/8-pel motion compensation
  1-bit flag is introduced into PPS (1/8pel_active_flag)
  Two parameters are introduced into slice header (num_ref_idx_lX_1/8pel_active)
  Encoder can select
    which slice should be applied 1/8-pel MC by 1/8pel_active_flag
    which reference picture should be referred in 1/8-pel mv by num_ref_idx_lX_1/8pel_active
Recommend setting
  For P slice
    1/8-pel MC is enabled
    All reference pictures are referred in 1/8-pel mv
  For B slice
    1/8-pel MC is enabled
    All reference pictures are referred in 1/4-pel mv in order not to increase overhead of mvd
Picture adaptive 8-pel motion compensation method
Notes: Indicate whether 1/8-pel motion compensation is enabled or not
Indicate the maximum reference index for which all of motion information is referred in 1/8-pel precision except for collocated motion vector “mvCol”

## Slide 4
Relationship between syntax elements and accuracy of motion parameters
  mvLX (ME): motion vector, to be derived by a motion estimation in encoder
  mvLX (internal): motion vector, to be used to derive spatial/temporal MVP candidate and to determine strength of deblocking filter
  To avoid increasing memory bandwidth and memory capacity for co-located picture
    if 1/8pel_active_flag = 1  mvCol = mvLX >> 1
Proposed syntax elements | mvdLX | pmvLX | mvLX (ME) | mvLX (internal) | mvCol
1/8pel_active_flag=0 | 1/4-pel | 1/4-pel | 1/4-pel | 1/4-pel | 1/4-pel
1/8pel_active_flag=1 num_ref_idx_lX_1/8pel_active=0 | 1/4-pel | 1/8-pel | 1/4-pel | 1/8-pel | 1/4-pel
1/8pel_active_flag=1 num_ref_idx_lX_1/8pel_active=N | if refIdxLX<N 1/8-pel otherwise 1/4-pel | 1/8-pel | if refIdxLX<N 1/8-pel otherwise 1/4-pel | 1/8-pel | 1/4-pel
Accuracy of motion parameters
Notes: If 1/8pel_active_flag = 0
  all precisions for parameters on motion vector are 1/4-pel.
If 1/8pel_active_flag = 1 and num_ref_idx_lX_1/8pel_active = 0,
  precisions for mvdLX, mvLX(ME) and mvCol are 1/4-pel
  precisions for pmvLX and mvLX(internal) are 1/8-pel.  It indicates that only precisions for parameters on motion vector, which is used internally, are expanded to 1/8-pel, so overhead bits such as mvdLX and computation time for ME are not increased.
If 1/8pel_active_flag = 1 and num_ref_idx_lX_1/8pel_active = N
  precision for mvCol is 1/4-pel, and precisions for pmvLX and mvLX(internal) are 1/8-pel, and precisions for mvdLX and mvLX(ME) is decided as below.
    If refIdxLX < N then, precisions for mvdLX and mvLX(ME) is 1/8-pel
    Otherwise, precisions for mvdLX and mvLX(ME) is 1/4-pel

## Slide 5
1/8-pel | -1, 2, -6, 62, 9, -4, 2, 0 | 
1/4-pel | -1, 4, -10, 57, 19, -7, 3, -1 | Same as HM3.0
3/8-pel | -2, 5, -11, 50, 29, -10, 5, -2 | 
1/2-pel | -1, 4, -11, 40, 40, -11, 4, -1 | Same as HM3.0
5/8-pel | -2, 5, -10, 29, 50, -11, 5, -2 | 
3/4-pel | -1, 3, -7, 19, 57, -10, 4, -1 | Same as HM3.0
7/8-pel | 0, 2, -4, 9, 62, -6, 2, -1 | 
1/16-pel | -2, 63, 4, -1 | 
1/8-pel | -3, 60, 8, -1 | Same as HM3.0
3/16-pel | -4, 57, 12, -1 | 
1/4-pel | -4, 54, 16, -2 | Same as HM3.0
5/16-pel | -5, 50, 22, -3 | 
3/8-pel | -5, 46, 27, -4 | Same as HM3.0
7/16-pel | -5, 41, 32, -4 | 
1/2-pel | -4, 36, 36, -4 | Same as HM3.0
9/16-pel | -4, 32, 41, -5 | 
5/8-pel | -4, 27, 46, -5 | Same as HM3.0
11/16-pel | -3, 22, 50, -5 | 
3/4-pel | -2, 16, 54, -4 | Same as HM3.0
13/16-pel | -1, 12, 57, -4 | 
7/8-pel | -1, 8, 60, -3 | Same as HM3.0
15/16-pel | -1, 4, 63, -2 | 
Fractional interpolation filter for 1/8-pel and 1/16-pel
Interpolation filters for 1/8-pel (Luma) and 1/16-pel (Chroma) are added in HM3.0
Fractional prediction sample values for luma and chroma are derived in the same way as HM3.0
It is designed based on 12-tap filter which is included in TMuC1.0 software
1/8-pel for Luma
1/16-pel for Chroma

## Slide 6
Experimental result of proposed method for low delay P
A proposed method was implemented on HM3.0 software and tested for low delay P condition
Encoding setting A is as below
  1/8_active_flag = 1
  num_ref_idx_l0_1/8pel_active = 4, num_ref_idx_l1_1/8pel_active = 0
   1/8-pel MC is enabled, and all reference pictures (L0) are referred in 1/8-pel mv
 | mvdL0 | pmvL0 | mvL0 (ME) | mvL0 (internal) | mvCol
1/8pel_active_flag=1 num_ref_idx_l0_1/8pel_active=4 | 1/8-pel | 1/8-pel | 1/8-pel | 1/8-pel | 1/4-pel
Cross checked by Samsung (JCTVC-F682)

## Slide 7
Experimental result for common test condition
A proposed method was evaluated below setting B for common test condition
  1/8_active_flag = 1
  num_ref_idx_l0_1/8pel_active = 0, num_ref_idx_l1_1/8pel_active = 0
   1/8-pel MC is enabled, all reference pictures are referred in 1/4-pel mv
 | mvdLX | pmvLX | mvLX (ME) | mvLX (internal) | mvCol
1/8pel_active_flag=1 num_ref_idx_lX_1/8pel_active=0 | 1/4-pel | 1/8-pel | 1/4-pel | 1/8-pel | 1/4-pel
Cross checked by Samsung (JCTVC-F682)

## Slide 8
Picture adaptive 1/8-pel motion compensation method is proposed
It saves 2.5% bits for HE in low delay P
  encoding time is 19% increased relative to HM3.0
  decoding time increase is not obvious
It can be configurable to achieve 1.1% bits reduction for HE in low delay P without obvious difference in encoding and decoding time
It also saves 0.4% bits for HE RA, and 0.1% bits HE LD
We suggest to consider the future adoption of the proposed method based on the study in a CE
Conclusion