## Slide 1: KANG Lijuan, MA Yanzhuo LIN Sixin Xidian University Huawei Tech. Ltd. (Presented by Haitao Yang)
2x2 block-based reference
frame compression

## Slide 2: Background
Existing methods in the last meeting: fixed rounding,E133,E432
  Memory access benchmark: access bandwidth of the fixed rounding method (pixel based compression) at align/burst parameters 8bit/8bit, where there is no redundant memory access.
  4x4-block-based memory compression method: E133/E432 methods
    Bandwidth increased by 40%~70% compared with the benchmark.
    Even higher than No compress one when align/burst are 8/8.
  Fixed rounding:
    is the benchmark at 8/8, however, when align/burst be higher, the bandwidth increased quickly.
    can be reorganized to 4x4-block-based memory to decrease its access bandwidth.
    Fixed rounding is not perfect for RFC due to the low RD performance.
Normalized bandwidth of the three methods

## Slide 3: Where comes the redundant bandwidth access?
An example
(a) Orange area: 8x8 block for access, which is not aligned with 4x4 blocks
(b) When align/burst parameters are 8/8, and compression unit is 4x4 block, the area shown in blue will be accessed unnecessarily, and redundant bandwidth access is introduced
(a)
(b)

## Slide 4: Where comes the redundant bandwidth access?
Notes: <number>

## Slide 5
So, without cache
  Better to use smaller compression unit when align/burst are small.
  Better to use larger compression unit when align/burst are large.
However, Small compression unit can be reorganized to larger ones.
  Considering all the circumstances, small compression unit is the better solution: access unit flexible granularity

## Slide 6: FIFO Cache: avoid some of the repeat access

## Slide 7
Cache is the best option if cost allows (expensive).
  Better to use larger compression unit, due to the large cache refresh unit.
Still, however, Small compression unit can be reorganized to larger ones.
  Considering all the circumstances, small compression unit is the better solution.

## Slide 8: Proposed method
We propose a RFC method based on 2x2 blocks instead of 4x4 blocks or single pixel
  Compared with 4x4 block based methods, 9%~17% of bandwidth is decreased for RA_HE and LD_HE, when burst parameter is lower than or equal to 128bits.
  Bandwidth is almost the same compared with E432 and E133, when burst parameter is higher than 128bits or with cache, by reorganizing four 2x2 units into 4x4 unit, which is a simple nor-normative implementation trick.
  The coding efficiency is close to the 4x4 block bsed ones.

## Slide 9: Proposed method
Scheme Describe for 10-bit/pixel to 8-bit/pixel
The scaling process
  Obtain the minimum (min) and maximum (max) pixel values in the 2x2 block
  Calculate the range of pixels’ values in the 2x2 block, as R=max-min.
  Decide the scaling value S so that R becomes less than (64 << S) and no less than (0, if S=0; 64 << (S-1), if S=1,2), where the max value of S is 3, which means R>=(64<<2)
  If S is less than 3, then the position of min in the block (minIdx) is stored, and P (=(pixel_value[i]-min)>>S, where i!=minIdx) will be represented by 6 bits. At the same time, min, S are stored, too.
  Else if S equals to 3, then the P(=pixel_value[i]>>3) and offset (=(sum(pixel_value[i]&0x7)+2)>>3) are stored.

## Slide 10: Proposed method
The de-scaling process
Read the first 2 bits, got the flag of scaling
If the flag denotes the case of S=3, the reconstruct pixel value D[i] (=P[i]<<3+(offset<<1)) is obtained.
Else if the flag denotes the case of S<3, the reconstruct pixel value D[i](=(P[i]<<S)+min) is calculated.

## Slide 11: Proposed method
The value of R | Precision Losses | Number of Bits to be used
R<64 | Lossless | 2(flag)+10(min)+2(minIdx)+6*3(differences)=32
R>=64 && R<128 | 1 bit * 3 | 2(flag)+10(min)+2(minIdx)+6*3(differences)=32
R>=128&& R<256 | 2 bits * 3 | 2(flag)+10(min)+2(minIdx)+6*3(differences)=32
R>=256 | 3 bits * 4 - compensated by two bits of offset | 2(flag)+ 7*4(Pixel rightshift 3 bits)+2(offset)=32
Table. 1 The scaled data for reference pictures compression

## Slide 12: Results
Encoding efficiency comparison (all compared with No-compression, HM3.0)
  Better than the Fixed rounding method: 0.07%/1.16% BD-rate vs. 0.68%/4.01%.
  A little better than E133 (BD-rate: 0.09%/1.16% vs. 0.12%/1.62
  A litter worse than E432 schemes (BD-rate: 0.09%/1.16% vs. 0.07%/0.77%).

## Slide 13
Memory access bandwidth comparison
  Without memory reorganization
    Reduced bandwidth comparing with E133 , E432 and Fixed rounding, when burst parameter is smaller than or equal to 128 bits.
    While burst parameter higher than 128bits ,it cause more memory access bandwidth than the 4x4 block based methods.
Results

## Slide 14: Results
Memory access bandwidth comparison
  With reorganized memory
    The proposed method access bandwidth is always the smallest one when burst parameter is larger than 8bits.
    The fixed rounding is the smallest one with align/burst parameters 8/8, as the benchmark.

## Slide 15: Conclusions
Lower memory access bandwidth with the proposed scheme
  When burst parameter is lower than or equal to 128 bits
  Decreased by 9~17% comparing to the 4x4 ones.
  When burst parameter is higher than 128 bits
  Memory access bandwidth is not increased, Similar to the 4x4 ones.
  Access bandwidth lower than 4x4-block-based schemes in all circumstances, and lower than fixed rounding scheme in most of the cases.
Encoding efficiency of the proposed scheme
  Better than fixed rounding method by 0.59%/2.85% BD-rate
  Close the 4x4 block based methods
Better tradeoff between RD performance and access bandwidth is obtained.
Other benefits of the proposed method:
  With smaller granularity, the memory storage format alignment between the RFC and display processing problem is alleviated.
  Smaller compression unit is good for parallel processing.
Can also implement other compression schemes to 2x2 blocks
Considering above factors, we propose to evaluate 2x2 RFC method through comparison with existing 4x4 based methods in a core experiment.

## Slide 16
Thank you !