## Slide 1: JCTVC-F503 Results on slice header modification
N.Ouedraogo, P.Onno
<number>
Jul 30, 2026
JCT-VC 6th Meeting, Torino 14-22 July, 2011
Notes: <number>

## Slide 2: Concept introduced in JCTVC-E222
Concept proposed in JCTVC-E222
1. Creation of a new Slice Common Parameters (SCP) NALU:
  Formerly named Slice Parameter Sets but not appropriate
  Basic principle
    Move current Slice parameters from Slice Header to this new NAL unit defined at picture level
  Motivation
    Avoid redundant coding of slice parameters
Slice Common Parameters (SCP)
HM2.0
Proposal
<number>
Notes: <number>

## Slide 3: Concept introduced in JCTVC-E222
2. Define boundaries in that new SCP NAL unit
  For Intra and inter prediction processes
    Signaled by the LCU address
    Can be defined independently of slice boundaries dedicated to entropy coding process
  For Loop filter process
    Signaled by the LCU address
    Independent of other boundaries
  Motivation
    Independent partitioning in slices for each process
07/30/26
<number>
Slice Common Parameters

## Slide 4: Experiment configuration of proposal
Implemented in HM3.1:
  Slice Header are limited to two syntax elements
    Address of first CU in the entropy slice
    QP parameter since may vary from slice to slice
  Slice Common Parameters NAL unit gathers all other slice header parameters
  Define Reconstruction slices boundaries in SCP NAL unit
  Loop filter slices are not used
    ALF & SAO parameters are defined in first entropy slice
Specific experiment conditions (targeting streaming)
  Reference is HM3.1 with
    NAL units size is limited to MTU size (typically 1500 bytes)
  2 LCU rows per slice
    Use slices to limit error propagation
07/30/26
<number>
Class | Slice size in LCU (64x64)
A | 80
B | 60
C | 26
D | 13
E | 40

## Slide 5: Experiment 1: Single SCP NAL unit per frame
07/30/26
<number>
Dedicated to reliable networks
Use a single SCP NAL unit per frame
  No redundancy of slice header parameters
Coding gain about 1% in average with our current testing conditions
  Much Higher for class E sequences

## Slide 6: Experiment 1: Results
07/30/26
<number>

## Slide 7: Experiment 1: Analysis
Why coding gain ?
  Reduction of slice header redundancy
  Indicating a new slice HM3.1 implies a new NAL unit
    New NAL units signaling overhead is saved with our proposal
    Significant at low bitrate
  Encoded data is below MTU size in common testing conditions
<number>
HM3.1
Proposal

## Slide 8: Experiment 2: Multiple SCP NAL units per frame
07/30/26
<number>
In error prone network, redundancy of slice parameters is needed to enable a resilient decoding of slice data.
Use multiple SCP NAL units per frames
  As many SCP NAL unit as entropy slice NAL units
  Aggregation of SCP NAL units and entropy slice in a single network packet same level of redundancy as in HM 3.1 is attainable

## Slide 9: Experiment 2: Results
 |  | Random access |  |  | Random access LC | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0,2 | -0,1 | 0,2 | -0,1 | 0,1 | 0,0
Class B | -0,3 | -0,3 | -0,4 | -0,3 | -0,2 | -0,2
Class C | -0,2 | -0,3 | -0,2 | -0,3 | -0,3 | -0,2
Class D | -1,3 | -1,1 | -1,2 | -1,2 | -1,2 | -1,1
Class E |  |  |  |  |  | 
All | -0,5 | -0,4 | -0,4 | -0,5 | -0,4 | -0,4
Enc Time[%] | 102% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
Results below show coding loss for high bitrate classes
  Due to the slightly bigger size of the SCP NAL unit compared to current Slice header.
Coding gain for Classes D & E
  The bitrate is low and the number of NAL units per frame is reduced in comparison to the reference.
  Additional SCP NAL units is not exceeding the overhead introduced in HM3.1
07/30/26
<number>
 | Intra |  |  | Intra LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0,5 | 0,8 | 0,7 | 0,4 | 0,4 | 0,4
Class B | 0,5 | 0,6 | 0,6 | 0,4 | 0,4 | 0,4
Class C | 0,4 | 0,5 | 0,5 | 0,4 | 0,4 | 0,4
Class D | 0,3 | 0,4 | 0,4 | 0,3 | 0,3 | 0,3
Class E | 0,4 | 0,6 | 0,6 | 0,3 | 0,3 | 0,4
All | 0,5 | 0,6 | 0,5 | 0,4 | 0,4 | 0,4
Enc Time[%] | 107% |  |  | 101% |  | 
Dec Time[%] | 109% |  |  | 100% |  | 
 | Low delay |  |  | Low delay LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0,4 | -0,7 | -0,4 | -0,3 | -0,4 | -0,2
Class C | -0,2 | -0,4 | -0,1 | -0,2 | -0,5 | -0,2
Class D | -1,4 | -1,5 | -0,7 | -1,1 | -1,3 | -0,7
Class E | -5,7 | -4,8 | -6,1 | -4,5 | -3,9 | -4,1
All | -1,6 | -1,6 | -1,5 | -1,3 | -1,3 | -1,1
Enc Time[%] | 102% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 99% |  | 

## Slide 10: Comparison with HM3.1 without slices
07/30/26
<number>
Low coding loss is observed for class E and D.
No loss for other classes
When a single slice is used within each frame, SCP NAL unit is not very efficient
A flag at PPS or SPS level could be defined to disable SCP NAL unit

## Slide 11: Loop filter slices
JCTVC-E045 proposes to move ALF parameters to PPS and defines activation flags for each CU at the beginning of slice.
Other contributions, such as JCTVC-F143, define deblocking filter parameters in slice headers
  Thus, these parameters may change at each slices
  A complex encoder may be able to adapt these parameters within a frame
  It seems reasonable that defining independent slices for Deblocking filter provide gains in comparison of creating new reconstruction slice with new parameters
Defining loop filter slices independently of slice or entropy slices seems advantageous
07/30/26
<number>

## Slide 12: Benefits of the proposal for streaming
Slices partitioning for network requirements and coding efficiency is separately defined
  The slice partitioning process can be adapted according to the network characteristics
    Entropy slices partitioning for network transport
    Reconstruction virtual slices for error propagations limitation
    Loop filter virtual slices for accurate loop filtering
  Same partitioning as with slices and entropy slices is permitted
Availability of Slice Common Parameters prior to slice data enables
  Identification of coding boundaries even in case of slice loss
  Adaptation of error concealment and video quality estimation strategy
Adaptation of slice parameter redundancy in function of the network reliability
<number>

## Slide 13: Conclusion
Goal of this proposal
  Validate the benefits of concept introduced in JCTVC-E222 for streaming environment.
Main points of this proposal
  Creation of a Slice Common Parameter NAL unit
  Introduction of coding dependencies and filtering boundaries/parameters in the proposed Slice Parameter Set.
Main advantages
  Coding efficiency is improved for streaming environment
  Redundancy of Slice parameters can be adapted to the network reliability .
Recommendation
  We propose to consider this proposition in a “Slice/High level syntax” Ad-Hoc Group or in a CE.
07/30/26
<number>

## Slide 14: Slice Common Parameter Syntax
07/30/26
<number>
Former slice header syntax
Inter/intra boundaries signalling
syntax