## Slide 1
A chroma coding scheme for SDIP mode (JCTVC-F505)
Jin Song, Haitao Yang, Mingyuan Yang, Haoping Yu, Changcai Lai (Huawei)
Jizheng Xu (Microsoft)

## Slide 2: Proposed scheme - overview
Part 1 Assign LM with the shortest codeword in SDIP case, which is the same as the method in JCTVC-F110.
Part 2 Introduce a new prediction mode, SDM (SDIP Direct Mode) as a candidate mode for chroma component in SDIP case
Part 3 Prune candidate mode set

## Slide 3: Proposed scheme – Part 2
SDM (SDIP Direct Mode)
  the chroma component share the same PU partition of the luma component
  The prediction mode of each chroma partition is the same as the mode of the corresponding luma partition.

## Slide 4: Proposed scheme – Part 3
Prune candidate mode set : prediction mode used by only one of the four SDIP luma partitions is excluded from the candidate mode set of chroma component

## Slide 5: Proposed scheme – codeword table
LumaModeNum denotes the number of different prediction modes of the four SDIP luma partitions, for example
  LumaModeNum equals 1 means that all four SDIP luma partitions use the same prediction mode.
  LumaModeNum equals 4 means that the prediction modes of the four SDIP luma partitions are different from each other.
LumaMode(x) denotes the prediction mode that is selected by x out of the four luma partitions.
With different LumaModeNum, all possible candidate chroma mode sets and corresponding codeword assignment are shown in the next slides

## Slide 6: Proposed scheme – codeword table
Candidiate chroma prediction modes | Codeword
LM | 0
LumaMode(3) | 10
SDM | 110
DC/planar | 111
when LumaModeNum is 2 (3 + 1)
Candidiate chroma prediction modes | Codeword
LM | 0
LumaMode(2) | 10
SDM | 110
DC/planar | 111
when LumaModeNum is 3
Candidiate chroma prediction modes | Codeword
LM | 0
SDM | 10
Vertical | 110
Horizontal | 1110
DC/planar | 1111
when LumaModeNum is 4
Candidiate chroma prediction modes | Codeword
LM | 0
LumaMode(4) | 10
SDM | 110
DC/planar | 111
when LumaModeNum is 1
Candidiate chroma prediction modes | Codeword
LM | 0
LumaMode(2)-1 | 10
LumaMode(2)-2 | 110
SDM | 1110
DC/planar | 1111
when LumaModeNum is 2 (2 + 2)

## Slide 7: Simulation
Based on issued SDIP software with revision number 866
The performance of the proposed scheme is evaluated
The performance of just the SDM technique is also evaluated

## Slide 8: Performance – SDM
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.0 | -0.1 | -0.1 | 0.0 | -1.4 | -0.8
Class B | 0.0 | -1.1 | -0.9 | 0.1 | -1.7 | -1.7
Class C | 0.0 | -0.2 | -0.3 | 0.1 | -0.8 | -0.8
Class D | 0.0 | -0.3 | -0.3 | 0.1 | -0.8 | -0.6
Class E | 0.0 | -0.8 | -0.7 | 0.1 | -1.6 | -1.4
Overall | 0.0 | -0.5 | -0.5 | 0.1 | -1.3 | -1.1

## Slide 9: Performance – whole scheme
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.0 | -0.3 | -0.2 | 0.0 | -1.6 | -1.0
Class B | 0.0 | -1.4 | -1.3 | 0.1 | -2.0 | -1.9
Class C | -0.1 | -0.8 | -0.7 | 0.0 | -1.0 | -1.0
Class D | -0.1 | -0.8 | -0.7 | 0.0 | -0.9 | -0.8
Class E | 0.1 | -1.4 | -1.5 | 0.1 | -2.0 | -1.8
Overall | 0.0 | -0.9 | -0.9 | 0.0 | -1.5 | -1.3
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.0 | -0.8 | -0.2 | 0.0 | -2.0 | -1.0
Class B | 0.0 | -1.4 | -1.0 | 0.0 | -2.0 | -1.8
Class C | -0.1 | -0.6 | -0.4 | 0.0 | -1.1 | -1.0
Class D | 0.0 | -0.3 | -0.5 | 0.1 | -0.8 | -0.6
Class E |  |  |  |  |  | 
Overall | 0.0 | -0.8 | -0.5 | 0.0 | -1.5 | -1.1
Enc Time[%] | 100% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 102% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0 | -0.4 | 0.0 | 0.0 | -1.0 | -0.7
Class C | -0.1 | -0.2 | -0.5 | 0.0 | -0.4 | -0.5
Class D | 0.0 | 0.3 | -0.2 | 0.0 | -0.5 | -0.7
Class E | -0.1 | -2.8 | -2.6 | -0.1 | -3.2 | -1.2
Overall | 0.0 | -0.6 | -0.7 | 0.0 | -1.1 | -0.7
Enc Time[%] | 100% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 100% |  | 

## Slide 10: Conclusion
The RD performance of the three parts are additive in Intra-HE case, and are almost additive in Intra-LC case
The proposed new chroma intra prediction mode, SDM contributes most of the coding gain
The whole scheme can achieve U/V component BD-rate of -0.9%/-0.9% and -1.5%/-1.3% under AI_HE and AI_LC conditions (Thanks Samsung for the crosschecking efforts, JCTVC-F629)
Based on the above conclusions, we suggest adopting the proposed prediction scheme along with SDIP.

## Slide 11
Thank You
www.huawei.com
Notes: 26/7/29
<number>