## Slide 1
CE6.b: Harmonization of SDIP and MDDT (JCTVC-F506)
Haitao Yang, Jiantong Zhou, Haoping Yu, and Changcai Lai

## Slide 2: Background & proposed harmonization
MDDT in HM3.0
  Applied to luma component of 4x4 blocks
  For each one dimensional transform, either DCT or DST is selection according to the intra prediction direction
Transforms in the issued SDIP software
  For the MxN TU, M-point and N-point DCT are applied to the row and the column vector, respectively.
Proposed harmonization
  MDDT is applied as either the row transform or the column transform if the dimension of the non-square TU in row or column direction equals 4
  The dependency of intra prediction mode and transform mode is the same as that for MDDT in HM3.0

## Slide 3: Simulation
Test case 1: SDIP OFF, MDDT_4x4 OFF
  The RD data of this test case is compared with HM3.0 anchor data to see the performance of MDDT in HM3.0.

## Slide 4: Simulation
Test case 2: SDIP ON, MDDT_4x4 OFF
  The RD data of this test case is compared with SDIP anchor data to see the performance of MDDT on top of SDIP.

## Slide 5: Simulation
Test case 3: SDIP ON, MDDT_4x4 ON
  This test case is actually the SDIP anchor. The SDIP anchor data is compared with HM3.0 anchor data to see the performance of SDIP on top of MDDT.

## Slide 6: Simulation
Test case 4: SDIP ON, MDDT_4x4 ON, HARMONIZATION_4x4 ON
  The RD data of this test case is compared with SDIP anchor data to see the performance of the harmonization solution.

## Slide 7: Simulation
Test case 5 (additional): SDIP OFF, MDDT_8x8 ON
  The RD data of this test case is compared with HM anchor data to see the performance of additional 8x8 MDDT for square TUs.

## Slide 8: Simulation
Test case 6 (additional): SDIP ON, MDDT_8x8 ON, HARMONIZATION_8x8 ON
  The RD data of this test case is compared with test case 4 to see the performance of additional 8x8 MDDT for both square and non-square TUs.

## Slide 9: Simulation
Test case 3 is the RD performance of the issued SDIP software
Test case 1, 2, 4 are specified in CE description JCTVC-E706, and are crosschecked by BBC, NEC, Orange Lab, and TI in JCTVC-F630, JCTVC-F349, JCTVC-F139, JCTVC-F239.
Test 5 and 6 are provided for information, and they are crosschecked by I2R in . JCTVC-F155.

## Slide 10: Conclusion
Based on the results of test case 1 and 2, most of the coding gain of MDDT can be retained when SDIP is enabled
The proposed harmonization (test case 4) is a straightforward extension of HM3.0 MDDT to SDIP, and show consistent coding performance improvement though not very big
Test case 5 and 6 show provide the information that combined with 8x8 MDDT, further coding gain can be obtained.
Based on the above conclusions, we suggest adopting the proposed harmonization (case 4) along with SDIP.

## Slide 11
Thank You
www.huawei.com
Notes: 26/7/30
<number>