## Slide 1: Improvements of SPS syntax
Virginie Drugeon, Thomas Wedi
Panasonic Corporation
6th JCT-VC meeting, Torino 14.-22. July 2011

## Slide 2: Outline
Introduction on Sequence Parameter Set syntax problems
Transmission of pictures size
Results
Conclusion

## Slide 3: Problems in Sequence Parameter Set syntax
The SPS syntax in the working draft and in the software needs to be harmonised: WD section 7.3.2.1 TEncCavlc::codeSPS TDecCavlc::parseSPS
The following types of differences between working draft and software can be observed:
  Syntax elements present in the working draft, but not in the software
  Syntax elements present in the software, but not in the working draft
  Syntax elements present both in working draft and software, but coded differently
  Syntax elements present both in working draft and software, but coded in another order
Implementation to solve third and fourth types of problems is very easy and can be provided
compared to

## Slide 4: Transmission of picture size: current status
In HEVC, the size of the coded pictures must be a multiple of the minimum coding unit size
In working draft: no syntax element to signal padding / cropping
In HM3.2:
  A number of padding pixels is present in SPS to enable coding of all picture sizes
  All values are provided in number of luma samples  confusing and redundant, because only some values of picture size and padding pixels are allowed
seq_parameter_set_rbsp( ) { | Descriptor
… | 
pic_width_in_luma_samples | u(16)
pic_height_in_luma_samples | u(16)
… | 
} | 
coding_tree( x0, y0, log2CUSize ) { | Descriptor
if( x0 + ( 1 << log2CUSize ) <= PicWidthInSamplesL && y0 + ( 1 << log2CUSize ) <= PicHeightInSamplesL && cuAddress( x0, y0 ) >= SliceAddress ) { | 
… | 
} | 
} | 

## Slide 5: Transmission of picture size: proposed solution
Automatic calculation of necessary number of padding pixels in order to have a coded picture size that is a multiple of the minimum CU size:
Give a number of additional padding minimum CUs at boundaries:
  Keep current software possibility to pad more than necessary
  Enable the best trade-off between padding and size of CUs at boundaries

## Slide 6: Results
As an example, for a sequence of size 1908x1076 with minimum CU size 8x8:
   At least two bytes are saved
With additional clean-up work, three of four bytes can be saved in SPS depending on the amount of padding pixels
HM3.2 |  |  | Proposed solution |  | 
Name | Value | Number of bits | Name | Value | Number of bits
pic_width_in_ luma_samples | 1920 | 21 | pic_width_in_ luma_samples | 1908 | 16
pic_height_in_ luma_samples | 1080 | 21 | pic_height_in_ luma_samples | 1076 | 16
PadX | 12 | 7 | horizontal_padding_ in_number_of_SCU | 1 | 3
PadY | 4 | 5 | vertical_padding_ in_number_of_SCU | 0 | 1

## Slide 7: Conclusion
The SPS syntax in the working draft and the software needs to be harmonized
First harmonization work is proposed in this contribution
Furthermore, this contribution proposes to solve the current problems for transmission of picture size in the SPS:
  Transmission of input/output picture size in number of luma samples
  Transmission of additional padding in number of minimum CU size
  Automatic calculation of coded pictures size
Proposal: integrate changes in next software release