## Slide 1: JCTVC-F543 Tabless run-length coding for transform coeffcients in CAVLC Antti Hallapuro, Jewon Kang, Jani Lainema, Kemal Ugur (Nokia)

## Slide 2: Background
Current run-length coding in CAVLC uses a table to store the run values for 28 lowest scan positions
This run-length table increases cost of hardware implementation
Mapping run value directly to codeword number captures the probability distribution rather well except for the longest run

## Slide 3: Algorithm
Longest run is mapped to a position between the shortest and second longest run
This is done with a simple equation that estimates roughly the probability distribution
A simple linear equation work quite well
  longest_run_pos = (maxrun + 1) >> K
  K = 0 for intra, 3 otherwise

## Slide 4: Source code
if(cn<maxrun+2)
{
level = 0; // next non-zero level is 1
thr = (maxrun + 1) >> scale;
if (cn >= thr)
run = (cn == thr) ? (maxrun+1) : (cn-1);
else
run = cn;
}
else
{
level = 1; // next non-zero level is larger than 1
run = cn-maxrun-2;
}

## Slide 5: Results
 | Intra LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -0,1 | -0,3 | -0,2
Class B | -0,1 | -0,4 | -0,3
Class C | -0,2 | -0,8 | -0,9
Class D | -0,2 | -0,8 | -1,0
Class E | -0,1 | 0,3 | 0,0
All | -0,1 | -0,4 | -0,5
Enc Time[%] | 99 % |  | 
Dec Time[%] | 100 % |  | 
 | Random access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0,0 | 0,1 | 0,2
Class B | -0,1 | 0,3 | 0,3
Class C | -0,1 | -0,3 | -0,4
Class D | -0,1 | -0,4 | -0,4
Class E |  |  | 
All | -0,1 | 0,0 | -0,1
Enc Time[%] | 99 % |  | 
Dec Time[%] | 99 % |  | 
 | Low delay LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 0,1 | 0,4 | 0,1
Class C | 0,1 | 0,2 | 0,1
Class D | 0,1 | 0,3 | 0,5
Class E | 0,4 | 2,1 | -0,9
All | 0,1 | 0,6 | 0,0
Enc Time[%] | 100 % |  | 
Dec Time[%] | 100 % |  | 

## Slide 6: Comparison with other proposals
Proposal | Memory in bytes | Intra LC | RA LC | LD LC
JCTVC-F543 | 0 | -0.1 | -0.1 | 0.1
JCTVC-F160 | 104 | 0.0 | 0.0 | 0.0
JCTVC-F298 | 148 | 0.0 | -0.1 | 0.0
JCTVC-F408 | 220 | 0.0 | -0.2 | 0.0

## Slide 7: Conclusions
Proposed method replaces run-length table in CAVLC saving 434 bytes memory
Performance on average is slightly improved compared to HM3