## Slide 1: JCTVC-F550 Removal of the parsing dependency of residual coding on intra mode
Joel Sole, Yunfei Zheng, Wei-Jung Chien, Rajan Joshi, Xianglin Wang, Marta Karczewicz

## Slide 2: Summary
Parsing issue
  Currently, decoding of intra mode is required to be able to parse residual data
  Mappings from 1-D data to 2-D block are necessary to parse
Goal: Separate parsing from decoding process in the residual coding in HE
Three parts have to be modified to solve the parsing issue
  Coefficient level coding
  Last coefficient coding
  Significance map coding
BD-rate | AI – HE | RA – HE | LB – HE
A | -0.05% | 0.07% | -0.01%
A + B | -0.03% | 0.06% | 0.01%
A + B + C | 0.13% | 0.18% | 0.05%

## Slide 3: Background
HEVC uses 3 scans for significance map coding
  Forward zig-zag, vertical and horizontal
  Scan depends on prediction mode
Coefficient level coding uses a different scan
  Forward-backward zig-zag scan on 4×4 sub-blocks
  Problem: need to know the significance map scan in order to derive the contexts for coefficient level
Significance map contexts depend on block position
Last significant coding depends on the block position
Solution: Make residual entropy coding independent of the intra mode

## Slide 4: Residual Coding Independent of the Intra Mode
Use the scan applied to the significance map for coefficient level coding
  Scan follows backward direction (as in JCTVC-F288 part 1)
  Context sets: set consists of 16 consecutive coefficients in scan order
    Instead of 4x4 sub-blocks in HEVC
    Less scan patterns, less processing, easier harmonization with non-square blocks
Last coefficient position is coded assuming that the scan is the zig-zag
Significance map coding
  For small blocks (4x4 and 8x8) the context currently depends on the 2-D position of the coefficient within the block
  Context is made dependant on the position of the coefficient within the scan order

## Slide 5: BD-rate
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.11 | 0.10 | 0.15 | 0.27 | 0.06 | 0.41 |  |  | 
Class B | -0.10 | 0.05 | 0.03 | 0.02 | -0.18 | 0.04 | 0.05 | -0.58 | -0.97
Class C | -0.14 | -0.04 | -0.01 | 0.02 | -0.03 | -0.20 | -0.02 | -0.72 | -0.79
Class D | -0.18 | -0.10 | -0.10 | -0.03 | -0.27 | -0.33 | -0.11 | -1.52 | -1.34
Class E | 0.08 | 0.11 | 0.23 |  |  |  | 0.04 | -0.99 | -2.88
All | -0.05 | 0.02 | 0.05 | 0.07 | -0.11 | -0.02 | -0.01 | -0.93 | -1.38
Enc T[%] | 99% |  |  | 99% |  |  | 99% |  | 
Dec T[%] | 97% |  |  | 98% |  |  | 99% |  | 
Coefficient level (A)

## Slide 6: BD-rate
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.18 | -0.03 | 0.07 | 0.23 | 0.13 | -0.23 |  |  | 
Class B | -0.07 | -0.07 | -0.11 | 0.02 | -0.26 | -0.04 | 0.05 | -0.50 | -1.16
Class C | -0.16 | -0.07 | -0.09 | 0.02 | 0.02 | -0.30 | 0.00 | -0.70 | -0.79
Class D | -0.15 | -0.20 | -0.19 | -0.02 | -0.30 | -0.43 | -0.09 | -1.48 | -1.33
Class E | 0.12 | 0.23 | 0.22 |  |  |  | 0.09 | -1.07 | -1.00
All | -0.03 | -0.04 | -0.04 | 0.06 | -0.11 | -0.24 | 0.01 | -0.90 | -1.08
Enc T[%] | 95% |  |  | 98% |  |  | 97% |  | 
Dec T[%] | 98% |  |  | 98% |  |  | 99% |  | 
Coefficient level + last coefficient coding (A + B)

## Slide 7: BD-rate
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.39 | 0.01 | -0.08 | 0.44 | -0.01 | 0.45 |  |  | 
Class B | 0.10 | -0.07 | -0.12 | 0.13 | -0.29 | 0.00 | 0.09 | -0.55 | -0.92
Class C | 0.03 | -0.10 | -0.11 | 0.12 | -0.19 | -0.22 | 0.06 | -0.72 | -0.70
Class D | -0.04 | -0.28 | -0.31 | 0.05 | -0.52 | -0.83 | -0.04 | -1.15 | -1.00
Class E | 0.21 | 0.19 | 0.17 |  |  |  | 0.07 | -1.60 | -1.75
All | 0.13 | -0.06 | -0.11 | 0.18 | -0.25 | -0.14 | 0.05 | -0.94 | -1.04
Enc T[%] | 94% |  |  | 97% |  |  | 97% |  | 
Dec T[%] | 99% |  |  | 100% |  |  | 99% |  | 
Coefficient level + last coefficient + significance map (A + B + C)

## Slide 8: Conclusions
Proposed making parsing independent of the decoded intra mode
Residual coding based on scan position, not on 2-D block position
Changes in elements
  Coefficient level
  Last significant position
  Significance map
BD-rate | AI – HE | RA – HE | LB – HE
A | -0.05% | 0.07% | -0.01%
A + B | -0.03% | 0.06% | 0.01%
A + B + C | 0.13% | 0.18% | 0.05%

## Slide 9
Thank you!

## Slide 10: Context sets for coefficient level
Set consists of 16 consecutive coefficients in scan order
  Instead of 4x4 sub-blocks in HEVC
Same contexts derivation for all blocks sizes
  Same number of contexts as in HEVC
Context Set (for 4x4 sub-blocks) | 
0 | For block size 4x4 only
1 | 0-3 LargerT1 in previous sub-block
2 | 4-7 LargerT1 in previous sub-block
3 | 8-11 LargerT1 in previous sub-block
4 | 12-15 LargerT1 in previous sub-block
5 | First 4x4 sub-block (for blocks>4x4) 16 LargerT1 in previous sub-block
HEVC
Proposal
Context Set (inverse 16 scan) |  | 
0 | Sub-set 0 | 0 LargerT1 in previous sub-set
1 |  | 1-3 LargerT1 in previous sub-set
2 |  | >3 LargerT1 in previous sub-set
3 | Other sub-sets | 0 LargerT1 in previous sub-set
4 |  | 1-3 LargerT1 in previous sub-set
5 |  | >3 LargerT1 in previous sub-set