## Slide 1: JCTVC-F552 Parallel Processing of Residual Data in HE
Joel Sole, Rajan Joshi, Marta Karczewicz

## Slide 2: Summary
Two methods are proposed to enhance parallelization processing of residual data in HE configuration
Sub-set processing of residual data
  Four scans passes for each set: significance, bin 1 of level, remaining of coefficient level and sign
Delayed state update for CABAC
  Probability update delayed by one context for residual data
BD-rate | AI – HE | RA – HE | LB – HE
A | -0.25% | -0.21% | -0.05%
A + B | -0.15% | -0.13% | 0.00%

## Slide 3: Scans in HEVC
Forward scan on the whole TU for significance map coding
  Zig-zag, horizontal or vertical
Different scan for coefficient level
  Zig-zag scan on 4×4 sub-blocks
  Passes in each sub-block
    Bin 1 of coefficient level
    Remaining of coefficient level
    Sign of coefficient
Complexity issues
  Different scan patterns imply different optimum data ordering
  Better to work on the most local set of data possible at any one time

## Slide 4: Parallel processing
Interleave all the scans within a TU divided in sets
  Reordering of the coding process in JCTVC-E335/F288
  Four scans within each set of 16 consecutive coefficients
    Significance
    Bin 1 of coefficient level
    Remaining of coefficient level
    Sign of coefficient
Parallelization
  Easier computation of contexts of following passes and sets
    Process one set while pre-calculating contexts of the next sets
  More local processing

## Slide 5: Delayed State Update in CABAC
Feedback loop in CABAC
  Context for the next bin may depend on the current bin
  Wait to update the state prior to processing next bin
Proposal: delay the state update by 1
  Allows the arithmetic coder to process the next bin without waiting for the state update to be completed
  Useful when the context for the next bin to be processed is already known
  Applied to residual coding
    Significance map and coefficient level

## Slide 6: Delayed State Update in CABAC
Highlighted parts are not computed for the current bin
  Separated process for previous bin update
  Computation can be done in parallel

## Slide 7: Delayed State Update in CABAC
Better pipelining (as in JCTVC-E226)
Current HEVC
Proposal (context update is for the previous bin model)

## Slide 8: BD-rate of (A) 4 set scans
  * Thanks to Panasonic for the cross-check
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.47 | -0.52 | -0.57 | -0.68 | -1.04 | -1.21 |  |  | 
Class B | -0.20 | -0.59 | -0.60 | -0.13 | -0.80 | -0.66 | 0.03 | -1.48 | -1.55
Class C | -0.21 | -0.42 | -0.43 | 0.00 | -0.66 | -0.58 | 0.03 | -1.44 | -1.58
Class D | -0.18 | -0.50 | -0.48 | -0.04 | -0.69 | -0.91 | -0.17 | -2.27 | -2.00
Class E | -0.19 | -0.91 | -0.78 |  |  |  | -0.11 | -2.43 | -3.17
All | -0.25 | -0.57 | -0.56 | -0.21 | -0.79 | -0.83 | -0.05 | -1.84 | -1.97
Enc T[%] | 98% |  |  | 99% |  |  | 97% |  | 
Dec T[%] | 97% |  |  | 98% |  |  | 98% |  | 

## Slide 9: BD-rate of (A + B) scans + delayed update
  * Thanks to Panasonic for the cross-check
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.32 | -0.34 | -0.39 | -0.60 | -1.19 | -1.41 |  |  | 
Class B | -0.09 | -0.49 | -0.45 | -0.05 | -0.72 | -0.49 | 0.08 | -1.24 | -1.37
Class C | -0.13 | -0.34 | -0.34 | 0.09 | -0.60 | -0.62 | 0.08 | -1.46 | -1.32
Class D | -0.11 | -0.43 | -0.37 | 0.01 | -0.76 | -0.81 | -0.05 | -1.75 | -1.54
Class E | -0.09 | -0.80 | -0.64 |  |  |  | -0.17 | -2.14 | -2.31
All | -0.15 | -0.46 | -0.43 | -0.13 | -0.81 | -0.81 | 0.00 | -1.59 | -1.58
Enc T[%] | 97% |  |  | 96% |  |  | 98% |  | 
Dec T[%] | 98% |  |  | 98% |  |  | 98% |  | 

## Slide 10: Conclusions
Proposed two methods to enhance parallelization of HE entropy coding
  Parallel context processing
  Delayed state update
Better performance

## Slide 11
Thank you!

## Slide 12: Context for significance map
Less contexts
Simpler derivation
HEVC
Proposal

## Slide 13: Context sets for coefficient level
Set consists of 16 consecutive coefficients in scan order
  Instead of 4x4 sub-blocks in HEVC
Same contexts derivation for all blocks sizes
  Same number of contexts as in HEVC
Context Set (for 4x4 sub-blocks) | 
0 | For block size 4x4 only
1 | 0-3 LargerT1 in previous sub-block
2 | 4-7 LargerT1 in previous sub-block
3 | 8-11 LargerT1 in previous sub-block
4 | 12-15 LargerT1 in previous sub-block
5 | First 4x4 sub-block (for blocks>4x4) 16 LargerT1 in previous sub-block
HEVC
Proposal
Context Set (inverse 16 scan) |  | 
0 | Sub-set 0 | 0 LargerT1 in previous sub-set
1 |  | 1-3 LargerT1 in previous sub-set
2 |  | >3 LargerT1 in previous sub-set
3 | Other sub-sets | 0 LargerT1 in previous sub-set
4 |  | 1-3 LargerT1 in previous sub-set
5 |  | >3 LargerT1 in previous sub-set