## Slide 1: JCTVC-F556: SDIP Harmonization With Deblocking, HE Residual Coding
Geert Van der Auwera, Joel Sole, Yunfei Zheng,
Xianglin Wang, In Suk Chong, Rajan Joshi,
Marta Karczewicz
Qualcomm Inc.

## Slide 2: HE Residual Coding

## Slide 3: Introduction
SDIP uses non-square transforms
  Block sizes: 32×8, 8×32, 16×4, 4×16, 8×2, 2×8, 16×1 and 1×16
Issue: in SDIP new mappings are introduced between non-square transforms and ‘square-based’ entropy coders
  This adds extra computational complexity
  The mapping ‘breaks’ neighborhood relationship between coefficients
Harmonization: modify HE entropy coding to deal in the same way with square and non-square blocks and without intermediate mapping
  Scans for SDIP blocks
  Modification of last coefficient coding and coefficient level
  New contexts for significance map

## Slide 4: Harmonization For HE Residual Coding
Scans
  Horizontal, vertical, and fixed diagonal scan starting at the long side
Last significant position coding
  Context depends on the length of the side of the block
  New context for the sides of length 2
Significance map coding
  New contexts for non-square blocks
    Blocks with same sizes share (transposed) contexts
  Small blocks (<= 64 coefficients) use contexts based on position
  Blocks 32×8 and 8×32 use the method for square blocks of 16×16 and 32×32
Coefficient level coding
  Same algorithm for all block types and sizes
  Based on 16 consecutive coefficients in scan order instead of 4×4 sub-blocks
    Method described in JCTVC-E335/F288

## Slide 5: Results
Running time reduction of ~7% compared to HM3-SDIP anchor
BD-rate | All Intra HE |  | 
 | Y | U | V
Class A | -0.15 | 0.35 | 0.21
Class B | -0.29 | -0.08 | -0.19
Class C | -0.26 | -0.16 | -0.16
Class D | -0.22 | -0.05 | -0.06
Class E | -0.09 | 0.14 | 0.16
All | -0.21 | 0.03 | -0.03
Enc T[%] | 92% |  | 
Dec T[%] | 98% |  | 

## Slide 6: SDIP Harmonization with Deblocking

## Slide 7: Artifact Examples

## Slide 8: Deblocking of Narrow SDIP Partitions
Block edges are near each other, for example:
Deblocking decisions and filters should be such that no additional edges are included in the support region, because deblocking result can become unreliable
Breaks the current deblocking filter design (8x8 based)
8×8 CUs
8×2 SDIP PU
Current edge
Filter and decision support region
CU 32×32 | 8×32, 32×8
CU 16×16 | 4×16, 16×4, 1×16, 16×1
CU 8×8 | 2×8, 8×2

## Slide 9: Proposal for reduction of SDIP blocking artifacts
  Direction of SDIP partitions with respect to CU edge determines HM3 deblocking or special SDIP deblocking
  Deblocking decision and filter adaptation based on SDIP partition type
  Support for deblocking parallellism of HM3
    Horizontal and vertical decisions based on reconstructed data
    Independent filtering

## Slide 10: SDIP Partition Orientation
When partition orientations are perpendicular to CU edge, HM3 deblocking filter can be used, other cases require adaptation depending on partition types
P
Q

## Slide 11: CU Boundary Edges
Block A | Block B | Filter Type | Decision Conditions
32x8 | Not SDIP type or perpendicular SDIP-PU | Strong or Weak4 | Deblock edge on/off Strong or weak filter
32x8 | 32x8 | Strong or Weak4 | Deblock edge on/off Strong or weak filter
32x8 | 16x4 | Weak2 | Deblock edge on/off
32x8 | 16x1 | Weak1 | Deblock edge on/off
32x8 | 8x2 | Weak1 | Deblock edge on/off
16x4 | Not SDIP type or perpendicular SDIP-PU | Weak2 | Deblock edge on/off
16x4 | 16x4 | Weak2 | Deblock edge on/off
16x4 | 16x1 | Weak1 | Deblock edge on/off
16x4 | 8x2 | Weak1 | Deblock edge on/off
8x2 | Not SDIP type or perpendicular SDIP-PU | Weak1 | Deblock edge on/off
8x2 | 16x1 | Weak1 | Deblock edge on/off
8x2 | 8x2 | Weak1 | Deblock edge on/off
16x1 | Not SDIP type or perpendicular SDIP-PU | Weak1 | Deblock edge on/off
16x1 | 16x1 | Weak1 | Deblock edge on/off
Not SDIP type or perpendicular SDIP-PU | Not SDIP type or perpendicular SDIP-PU | HM3 deblocking filters | HM3 deblocking decision conditions

## Slide 12: Internal CU Edges
Block A | Block B | Filter Type | Decision Conditions
32x8 | 32x8 | Strong or Weak4 | Deblock edge on/off Strong or weak filter
16x4 | 16x4 | Weak2 | Deblock edge on/off
16x4 | 16x1 | Weak1 | Deblock edge on/off
16x1 | 16x1 | Weak1 | Deblock edge on/off
8x2 | 8x2 | Weak1 | Deblock edge on/off
SDIP Level 2: 16x1 partitions
Only processing along level 1 edge of 16x4 partition
Preservation of texture

## Slide 13: SDIP Deblocking Filters
Strong Filter (HM3) | p0’ = ( p2 + 2*p1 + 2*p0 + 2*q0 + q1 + 4 )/8 p1’ = ( p2 + p1 + p0 + q0 + 2 )/4 p2’ = ( 2*p3 + 3*p2 + p1 + p0 + q0 + 4 )/8 q0’ = ( p1 + 2*p0 + 2*q0 + 2*q1 + q2 + 4 )/8 q1’ = ( p0 + q0 + q1 + q2 + 2 )/4 q2’ = ( p0 + q0 + q1 + 3*q2 + 2*q3 + 4 )/8
Weak4 Filter [1] |  = ( 9*(q0-p0) - 3*(q1-p1) + 8 )/16  = Clip( -tc, tc,  ) (tc is HM3 deblocking threshold, depending on QP) p0’ = p0 +  q0’ = q0 -  p = Clip( - (tc/2), tc/2, ( (p2 + p0 + 1)/2 - p1 +  + 1 )/2 ) p1’ = p1 + p q = Clip( - (tc/2), tc/2, ( (q2 + q0 + 1)/2 - q1 -  + 1)/2 ) q1’ = q1 + q
Weak2 Filter [1] |  = ( 9*(q0 - p0) - 3*(q1 - p1) + 8)/16  = Clip( -tc, tc,  ) (tc is HM3 deblocking threshold, depending on QP) p0’ = p0 +  q0’ = q0 - 
Weak1 Filter |  = ( 5*(q0 - p0) + 8)/16  = Clip( -tc, tc,  ) (tc is HM3 deblocking threshold, depending on QP) p0’ = p0 +  q0’ = q0 - 
[1] Norkin, K. Andersson, R. Sjoberg, “CE12.1: Ericsson Deblocking Filter,” 5th JCT-VC Meeting, Geneva, CH, March 2011, Doc. JCTVC-E276
Filter | Compute | Replace
Strong | 4L, 4R | 3L, 3R
Weak4 | 3L, 3R | 2L, 2R
Weak2 | 2L, 2R | 1L, 1R
Weak1 | 1L, 1R | 1L, 1R

## Slide 14: SDIP Deblocking Decisions
Deblock edge on/off | ¦p0i – q0i¦ < α2 ¦p1i – p0i¦ < β2 ¦q1i – q0i¦ < β2 For i=2 and i=5 If all conditions are true, then edge is deblocked α2 = (3*α+2)>>2 β2 = (3*β+2)>>2 (α and β are thresholds specified in [1], depending on QP)
Strong or weak filter | ¦p0 – q0¦ < δ ¦q1 – q0¦ + ¦q2 – q0¦ + ¦q3 – q0¦ + ¦p1 – p0¦ + ¦p2 – p0¦ + ¦p3 – p0¦ < μ Conditions tested on pixel line basis If conditions are true, then strong filter is applied to the line, else weak filter δ = ( α2 >> 2 ) – (α2 >> 4) μ = (β – 4) << 2
[1] J. An, Q. Huang, X. Guo, Y.-W. Huang, S. Lei, “CE12 Subtest1: Improved Deblocking Filter,” 5th JCT-VC Meeting, Geneva, CH, March 2011, Doc. JCTVC-E079

## Slide 15: Results
Encoding and decoding times are similar to HM3-SDIP
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.1 | 0.0 | 0.0 | -0.1 | 0.0 | 0.0
Class B | 0.0 | 0.0 | 0.0 | -0.1 | 0.0 | 0.0
Class C | -0.1 | 0.0 | 0.0 | -0.2 | 0.0 | 0.0
Class D | -0.1 | 0.0 | 0.0 | -0.1 | 0.0 | 0.0
Class E | -0.1 | -0.1 | -0.1 | -0.2 | -0.2 | -0.1
Overall | -0.1 | 0.0 | 0.0 | -0.1 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 101% |  |