## Slide 1
Near Lossless Coding for Screen Contents
July 14,2011
Wen Gao, Gregory Cook, Mingyuan Yang, Jin Song, Haoping Yu
Notes: <number>
<number>

## Slide 2
Motivation
Interactive video communications are becoming a major feature in many application scenarios
  E-Conference or web-conference: Screen Sharing
  Virtual desktop infrastructure (VDI), and Online Gaming
  Potentially new major application for HEVC
Common requirements related to video include
  High compression efficiency
  Low delay
  High quality texts and graphics  prevent eye fatigue
Major issues in existing Solutions
  Non-standard proprietary solutions
  Poor quality
Page <number>
Notes: <number>

## Slide 3
State of HEVC WD/HM
Many tests have been done by using HM for screen content coding
We observed the following:
  Rather efficient inter-frame encoding: Skip and direct mode
  Less efficient intra-frame encoding at low QP, such as QP=0
Unique characteristics of screen content
  Compound video: mixture of cameral captured contents, computer generated graphics, texts, etc.
  Contents are either static or contain fast motion but without optical motion blurring,
    Such as identical content with simple displacement
It’s desirable to have (near) lossless encoding tool
  Avoid eye fatigue
  facilitate efficient inter coding
Page <number>
Notes: <number>

## Slide 4
Current HEVC Architecture
Page <number>
Notes: <number>

## Slide 5
Near Lossless Encoding
Transform bypass lossless coding
  Remove the transform and quantization module
  Use DPCM when horizontal or vertical intra prediction mode is used
    Prediction based on adjacent pixels
  Slightly modify the CABAC coding due to the new characteristics of the prediction residuals
Transform without quantization (near) lossless coding
  Only the quantization module is removed
  Can achieve near lossless coding due to the nature of existing transforms
    We observe +1 or -1 difference in original and reconstructed pixels
Page <number>
Notes: <number>

## Slide 6
Syntax modification (1)
Add luma and chroma transform bypass flags at PU level
  Flag =1  transform bypass coding
  Flag =0  transform without quantization coding
Modify vertical and horizontal intra prediction mode
  Prediction based on previous lines in vertical or horizontal directions
  For example, in vertical prediction mode
    Denote P(I,J) as prediction version of Z(I,J)
    P(0,J) = X(J) for J=0..,3 and P(I,J)=Z(I-1,J) for I=1,2,3 and J=0,..3
Page <number>
Notes: <number>

## Slide 7
Syntax modification (2)
Luma prediction residual encoding
  Significant portion of luma prediction residuals has large levels
  Change the binarization scheme for level-3 to Fixed length coding: B0 and B1 are CABAC coded while bypass CABAC coding for B2-B9
Page <number>
Level | B0 | B1 | B2 | B3 | B4 | B5 | B6 | B7 | B8 | B9
1 | 0 |  |  |  |  |  |  |  |  | 
2 | 1 | 0 |  |  |  |  |  |  |  | 
3 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
4 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
… |  |  |  |  |  |  |  |  |  | 
255 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
signs of luma and chroma prediction residuals encoding
  Use CABAC coding to replace the bypass coding
Notes: <number>

## Slide 8
Test Results (1)
Baseline: HM3.0
Near lossless coding modifications are integrated into HM3.0-SDIP branch
Test Conditions:
  All Intra, HE
  8-bit internal depth
  RDOQ, De-blocking filtering, Alf and SAO are all turned off
Test Sequences:
  ScreenCaptureWinMoving_1280x720_30.yuv
  ScreenCaptureSlideEditing_1280x720_30.yuv
Page <number>
Notes: <number>

## Slide 9
Test Results (3)
Page <number>
QP=14
Notes: <number>

## Slide 10
Test Results (4)
Page <number>
QP=9
Notes: <number>

## Slide 11
Test Results (2)
Use HM3.0 as the anchor, BD performance of HM3.0-dev-SDIP
Page <number>
Use HM3.0-dev-SDIP QP=0 as the anchor, rate performancee of near lossless coding software
Sequence | BD-Y rate | BD-U rate | BD-V rate
ScreenCaptureWinMoving_1280x720_30.yuv | -13.5 | -12.1 | -11.9
ScreenCaptureSlideEditing_1280x720_30.yuv | -13.0 | -10.8 | -10.6
Sequence | total rate
ScreenCaptureWinMoving_1280x720_30.yuv | -53.0%
ScreenCaptureSlideEditing_1280x720_30.yuv | -41.7%
Notes: <number>

## Slide 12
Conclusion
Recommend to create a CE group to exam this (near) lossless coding mode
Page <number>
Notes: <number>

## Slide 13
Page <number>
Thank You
www.huawei.com
Notes: <number>
<number>