## Slide 1: CE6.c: Differential Coding of Intra Modes
Sony, Sharp, Panasonic, and Toshiba
July. 12, 2011
<number>
JVTVC-F566

## Slide 2: DCIM Technology
DCIM Proposal
DCIM Key Features
HM Proposal
Enhances current UIP
Efficient signaling of directional information
Significant Coding & Visual Improvements
Notes: <number>

## Slide 3: DCIM -- summary
Summary of Changes
- Additional luma intra modes (dcim modes, bipred modes)
- Luma Intra mode coding
- Edge derivation using reconstructed neighbor pixels
- Modified directional prediction … use 4-tap filter
- Simplified Bidirectional prediction
Luma intra mode in HM-3.0 + DCIM
- 64x64: 3 UI + 1 Planar
- 32x32,16x16: 34 UI + 1 planar + 5 dcim + 2 bipred
- 8x8: 34 UI + 1 planar + 1 dcim + 2 bipred
- 4x4: 17 UI + 1 planar + 1 dcim + 2 bipred
Performance
- HE: 0.8% gain (entT: 113%, decT: 103%)
- LC: 0.7% gain (encT: 124%, decT: 105%)

## Slide 4: Edge derivation
Stage I:
  Find neighbors’ suggested direction
    Filter reconstructed area to find local gradients
    Calculate σ and ρ
    Use the ratio and a look-up table (size 32) to find the index of edge direction
      Signs of σ and ρ are also important in finding the index.
      128 values are possible for the index (all possible directions between integer locations in the boundary and the center of a 32x32 block)
    The index of the edge direction is directly used in the function that computes the prediction
      This function is the same as UI prediction function for the most part (no additional computation for finding the prediction compared to UI modes)
<number>
,

## Slide 5: DCIM modes signaling
Stage II:
  Encode the actual prediction direction differentially with respect to neighbors’ suggested direction
  That is, code the sign and magnitude of the value
<number>

## Slide 6: Luma intra mode signaling

## Slide 7: Prediction Interpolation
Interpolation
    Since DCIM modes generally have higher precision they perform better when used with Cubic interpolation
    4-tap interpolation filters are generated based on Cubic interpolation
      Main DCIM mode always uses the 4-tap filters
      The rest of the modes switch between 4-tap filters and 2-tap (linear) interpolation based on the mode direction
        Decision is based on a table (currently based on mode Intra smoothing table)
Fractional-pel location | Filter coefficient |  |  | 
0/32 | 0 | 256 | 0 | 0
1/32 | -3 | 252 | 8 | -1
2/32 | -5 | 247 | 17 | -3
3/32 | -7 | 242 | 25 | -4
4/32 | -9 | 236 | 34 | -5
5/32 | -10 | 230 | 43 | -7
6/32 | -12 | 224 | 52 | -8
7/32 | -13 | 217 | 61 | -9
8/32 | -14 | 210 | 70 | -10
9/32 | -15 | 203 | 79 | -11
10/32 | -16 | 195 | 89 | -12
11/32 | -16 | 187 | 98 | -13
12/32 | -16 | 179 | 107 | -14
13/32 | -16 | 170 | 116 | -14
14/32 | -17 | 162 | 126 | -15
15/32 | -16 | 153 | 135 | -16
16/32 | -16 | 144 | 144 | -16
Interpolation Filters

## Slide 8: BD-Rate Compared to HM 3.0
<number>
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.2 | 0.0 | 0.1 | -0.2 | 0.0 | 0.0
Class B | -0.7 | -1.0 | -1.1 | -0.5 | -0.4 | -0.5
Class C | -1.2 | -1.1 | -1.1 | -1.4 | -0.7 | -0.8
Class D | -0.7 | -0.4 | -0.4 | -0.6 | -0.1 | -0.2
Class E | -1.0 | -1.3 | -0.9 | -0.8 | -1.0 | -0.7
Overall | -0.8 | -0.7 | -0.7 | -0.7 | -0.4 | -0.5
Enc Time[%] | 113% |  |  | 124% |  | 
Dec Time[%] | 103% |  |  | 105% |  | 

## Slide 9
BD-Rate Compared to HM 3.0
All Intra HE

## Slide 10: Result by different configuration
 |  | Configuration |  |  |  | Performance (vs HM-3.0) |  | 
 |  | DCIM | subdir | bipred | 4tap | Y Bdrate | Enc T | Dec T
Test 1 | DCIM | x | X | X | x | -0.8 | 113% | 103%
Test 2 | DCIM sdir0 | x |  | X | x | -0.4 | 106% | 103%
Test 3 | DCIM bip0 | x | x |  | x | -0.7 | 110% | 103%
Test 4 | DCIM 4tap0 | x | x | X |  | -0.4 | 111% | 103%
 |  | Configuration |  |  |  | Performance (vs HM-3.0) |  | 
 |  | DCIM | subdir | bipred | 4tap | Y Bdrate | Enc T | Dec T
Test 1 | DCIM | x | x | x | x | -0.7 | 124% | 105%
Test 2 | DCIM sdir0 | x |  | x | x | -0.4 | 114% | 106%
Test 3 | DCIM bip0 | x | x |  | x | -0.5 | 119% | 104%
Test 4 | DCIM 4tap0 | x | x | x |  | -0.1 | 121% | 105%
All Intra HE
All Intra LC

## Slide 11
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.6 | -1.1 | -1.3 | -0.6 | -0.6 | -1.2
Class B | -1.5 | -2.7 | -3.1 | -1.7 | -1.5 | -2.3
Class C | -2.6 | -3.0 | -3.4 | -2.8 | -2.1 | -2.6
Class D | -2.1 | -2.2 | -2.3 | -2.0 | -1.7 | -1.8
Class E | -2.4 | -4.3 | -3.7 | -2.5 | -4.6 | -3.4
Overall | -1.8 | -2.6 | -2.7 | -1.9 | -1.9 | -2.2
Enc Time[%] | 141% |  |  | 173% |  | 
Dec Time[%] | 105% |  |  | 107% |  | 
(Information) SDIP + DCIM
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.1 | 0.3 | 0.4 | 0.2 | 0.6 | 0.7
Class B | -0.3 | -0.2 | -0.2 | 0.2 | 0.4 | 0.4
Class C | -0.7 | -0.4 | -0.4 | -0.2 | 0.4 | 0.4
Class D | -0.3 | 0.0 | -0.2 | 0.3 | 0.5 | 0.5
Class E | -0.4 | 0.3 | 0.3 | 0.4 | 0.7 | 0.8
Overall | -0.4 | 0.0 | 0.0 | 0.2 | 0.5 | 0.5
Enc Time[%] | 107% |  |  | 112% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
Compared to HM-3.0
Compared to SDIP

## Slide 12: Conclusion
DCIM: Differential Coding of Intra Modes
- Additional luma intra modes (dcim modes, bipred modes)
- Luma Intra mode coding
- Edge derivation using reconstructed neighbor pixels
- Modified directional prediction … use 4-tap filter
- Simplified Bidirectional prediction
Performance
- DCIM compared to HM-3.0
- HE: 0.8% gain (entT: 113%, decT: 103%)
- LC: 0.7% gain (encT: 124%, decT: 105%)
- Impact by changing each DCIM aspect
- Performance with SDIP