## Slide 1: Simplification of MVP design for HEVC JCTVC-F575
Yue Yu, Krit Panusopone and Limin Wang
Motorola Mobility

## Slide 2: MV coding for bi-predictive mode in HM-3.0
2 MVs are used for each PU, one for list 0 and one for list 1
Each MV is coded independently with its own MVP
MVP is computed using AMVP scheme
Hence, 2 MVP candidate lists are formed and 2 MVP indices may be required

## Slide 3: Proposed change
For list 0, compute MVP using AMVP scheme
  MVP index for list 0 may be used
For list 1, compute MVP using MV0
  No need to form MVP candidate list for list 1
Scaling may be required for list 1 MVP calculation
MVP_list1 = (sign)(TR2/TR1)*MV0
  Sign is set based on prediction direction of MV0 and MV1
Alternately, MVP, for list 1, can be computed using MVP0
  Similar scaling process applies

## Slide 4: Example of MVP scaling (1)
Both MV0 and MV1 point to past reference pictures

## Slide 5: Example of MVP scaling (2)
MV0 points to a past reference picture and MV1 point to future reference picture

## Slide 6: Experimental results (1)
MVP of list 1 derived from MV0
 | Low delay low complexity |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 0.2 | 0.2 | 0.0
Class C | 0.1 | 0.3 | 0.0
Class D | 0.0 | 0.1 | -0.2
Class E | 0.1 | -0.5 | 0.4
All | 0.1 | 0.1 | 0.1
Enc Time[%] | 103% |  | 
Dec Time[%] | 99% |  | 

## Slide 7: Experimental results (2)
MVP of list 1 derived from MVP0
 | Low delay low complexity |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 0.1 | 0.2 | -0.4
Class C | 0.0 | 0.0 | -0.2
Class D | 0.0 | -0.2 | -0.3
Class E | 0.0 | -0.1 | -0.4
All | 0.0 | 0.0 | -0.3
Enc Time[%] | 102% |  | 
Dec Time[%] | 99% |  | 

## Slide 8: Conclusions
Simplification of MVP design for bi directional prediction.
MVP of list 1 is set to either MV0 or MVP0.
Only 1 candidate list required, lower complexity in decoder.
No overhead required for MVP index of list 1.
No significant impact on coding performance.