## Slide 1: RQT with rectangular transform unit support JCTVC-F578
Krit Panusopone, Xue Fang, Vivian Kung and
Limin Wang
Motorola Mobility

## Slide 2: Residual Quadtree (RQT) in HM-3.0
QT for TU representation to allow flexible partitioning
RQT is applied to each CU (inter mode), PU (intra mode)
Leaf of QT becomes TU
RQT defined by 4 parameters; CU size, max TU size, min TU size, max RQT depth
TU split flag required for each RQT node (except node for min TU size)
Implicit TU partition used when max RQT depth = 1

## Slide 3: RQT for rectangular PU in HM-3.0
Rectangular PU, 2NxN and Nx2N, allowed
If RQT max depth = 1, NxN TU is selected
If RQT max depht > 1, RQT root at CU (2Nx2N)
Rectangular TU proposed in previous meetings
Harmonization between rectangular TU and RQT for rectangular PU may be beneficial

## Slide 4: Proposed residual tree
Only for rectangular PU
Root level of tree set to PU, instead of CU
Only first level node is rectangular, other level node is square
Joint splitting decision at the first level node
  To ensure normal RQT after first level
Minimize change to current RQT syntax

## Slide 5: Proposed residual tree for PU type Nx2N

## Slide 6: Experiment configuration
Implemented in HM-3.0-dev-Motorola
Max RQT depth set to 1
TU size ranges from 32x32 to 4x4, similar to common test condition

## Slide 7: Experimental results (1)
 | Random access high efficiency |  |  | Random access low complexity |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.2 | 0.7 | 0.2 | -0.5 | 1.8 | 1.6
Class B | -0.3 | 0.4 | 0.1 | -0.4 | 1.0 | 0.8
Class C | -0.4 | 0.2 | 0.2 | -0.4 | 0.4 | 0.5
Class D | -0.3 | -0.2 | -0.3 | -0.4 | 0.4 | -0.2
Class E |  |  |  |  |  | 
All | -0.3 | 0.0 | 0.1 | -0.4 | 0.9 | 0.7
Enc Time[%] | 89% |  |  |  | 89% | 
Dec Time[%] | 90% |  |  |  | 90% | 

## Slide 8: Experimental results (2)
 | Low delay high efficiency |  |  | Low delay low complexity |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.1 | 0.0 | -0.1 | -0.2 | 0.5 | 0.2
Class C | -0.3 | 0.2 | 0.0 | -0.2 | -0.1 | 0.1
Class D | -0.3 | -0.3 | 0.2 | -0.3 | -0.2 | 0.5
Class E | 0.0 | -0.1 | 0.0 | -0.1 | 0.9 | 2.5
All | -0.2 | -0.1 | 0.0 | -0.2 | 0.3 | 0.7
Enc Time[%] | 89% |  |  |  | 89% | 
Dec Time[%] | 91% |  |  |  | 89% | 

## Slide 9: Conclusions
Rectangular TU for rectangular PU improves coding efficiency
Simplified residual tree is proposed
Rectangular TU allowed only in the first level of RQT
Joint split flag used for first level
Normal RQT operation after the first level
Recommend creating experiment in CE to study harmonization of rectangular TU and RQT