## Slide 1
<number>
eBrisk and InterDigital Communications
6th JCT-VC Meeting: Torino, IT
July 14-22, 2011
The effect of LCU size on coding efficiency in the context of MTU size matching
Notes: <number>

## Slide 2: Introduction
<number>
Some applications transport coded video on networks with maximum transmission unit (MTU)size constraints (e.g., 1500 bytes for Ethernet v2)
MTU size matching
  Coded slice size > MTU size
    Network fragments oversize packet carrying slice or
    Application uses multiple MTU-sized packets for 1 slice
    Both cases: loss of one fragment  loss of large slice
  Coded slice << MTU size
    Packet header overhead “steals” coding efficiency
  Ideally: coded slice size == MTU size
Notes: <number>

## Slide 3: Experiment
Explore the effect of LCU size on coding efficiency in the context of a 1500-byte MTU size constraint
  Compare single slice per picture to 1500-byte slice partition
  Compare single slice per picture to 1500-byte slice + tiles partition
    Widths selected to produce square-ish slices
LCU sizes: 16x16, 32x32, and 64x64
<number>

## Slide 4: Results
<number>
Notes: <number>
Observation: losses for slices grow with decreasing LCU size
Hypothesis: Coding efficiency loss results from smaller LCU sizes creating longer and narrower slices -> Narrower slices have more slice boundary for a given unit of slice area -> more broken dependencies per unit area -> lower coding efficiency
Observation: Slices and Tiles losses do not increase with decreasing LCU size (and are generally smaller than slices alone)

## Slide 5: Summary
Relative to one slice per picture anchor
  For 1500-byte slices, coding efficiency loss grows with decreasing LCU size
  For 1500-byte slices + tiles, coding efficiency loss somewhat decoupled from LCU size
Simulations using slices + tiles showed higher coding efficiency compared to those where only slices were used
<number>
Notes: <number>