## Slide 1: CE11: Hardware complexity of large zig-zag scan for level-coding of transform coefficients
Cheung Auyeung
Sony
July 14, 2011
<number>
JCTVC-F134

## Slide 2: Level Scanning in HM3 HE Coding
4x4 blocks
  Uses zig-zag scan in reverse order.
Blocks larger than 4x4
  Divide block in to 4x4 sub-blocks.
  Levels in each 4x4 subblocks are scanned with zig-zag but in reverse order.
  Each 4x4 sub-block are scanned with forward zig-zag scan order
4x4 scan patterns have lower complexity property for HW addressing.
<number>

## Slide 3: Level Scanning in JCTVC-E335
Use mode dependent scan as in significance map coding but in the reverse order
  Divide the mode dependent scan order into subsets of 16 consecutive coefficients but in reverse order.
Scan patterns larger than 4x4 do not have lower complexity property for HW addressing.
<number>

## Slide 4: Level Coding in JCTVC-F612
4x4 and 8x8 blocks
  uses new VLC table mapping and no changes in the CAVLC algorithm.
16x16 and 32x32 blocks
  Add Horizontal and Vertical scan order for Intra block coding based on IntraPredMode.
  16x16 and 32x32 have different mapping of IntraPredMode to ScanOrder.
  Blocks are divided into 4x4 sub-blocks and coded separately with CAVLC after the last position is send.
    When condition is meet, a skipped/not skipped bit is send to indicate if a candidate 4x4 subblock is all zero or not.
<number>

## Slide 5: Hardware Complexity Comparison
HM3 CAVLC and JCTVC-E335 CABAC scan pattern is approximately twice as costly as HM3 CABAC scan pattern
HM3 CABAC and QualComm JCTVC-615 CAVLC level coding are based on 4x4 sub-blocks. Their scan patterns have lower gate count for hardware implementaton.
<number>
 | Transform size | Scan | HW size of scan
AVC | 8x8 | 4x4 scan | Reordering buffer 8x8x16 = 1,024bit + control logic 9kgate
HM3 CABAC | Upto 32x32 | 4x4 scan + zigzag | Reordering buffer 32x32x16 = 16,384bit + control logic 11kgate (+2kgate)
HM3 CAVLC and JCTVC‑E335 | Upto 32x32 | 32x32 zigzag scan | Reordering buffer 32x32x16 = 16,384bit + control logic 19kgate (+10kgate)