## Slide 1: JCTVC-F606:Memory and Parsing Friendly CABAC Context
Wei-Jung Chien, Marta Karczewicz, and Xianglin Wang
Qualcomm

## Slide 2: Introduction
In CABAC, information from neighboring blocks are often used in designing the context for certain syntax elements.
    Line buffer is required for context modeling
    This proposal is to reduce line buffer size while keeping similar coding performance.
LCU

## Slide 3: Contexts using neighboring information (HM3.0)
Syntax element | Number of contexts | Memory requirement (every 4x4 block)
split_coding_unit_flag | 4 | 2 bits (every 16x16 block)
skip flag | 4 | 1 bit
no_residual_data_flag | 4 | 1 bit (every 8x8 block)
cbp of luma block | 4 | 1 bit
cbp of intra chroma block | 4 | 2 bit
merge_flag | 4 | 1 bit
inter_pred_flag | 4 | 1 bit
ref_idx (bin0) | 4 | 2 bits
mvd(bin0) | 4 | 4 bits

## Slide 4: Propose method
Syntax element | Proposed method
split_coding_unit_flag | No changes
skip flag | No changes
no_residual_data_flag | 1 context
cbp of luma block | No changes
cbp of intra chroma block | Aligned with cbp of inter chroma block, 1 context for each transform depth
merge_flag | 1 context
inter_pred_flag | 1context for each CU depth
ref_idx (bin0) | 1 context
mvd(bin0) | 1 context

## Slide 5: Simulation Results
 | HE |  | 
 | Y | U | V
AI | 0.07 | -0.95 | -0.91
RA | -0.02 | -0.66 | -0.77
LB | 0.00 | -0.19 | -0.42

## Slide 6: Memory requirement comparison
Syntax element | Original memory needed (bit) | Proposed (bit)
split_coding_unit_flag | ((1920+64)/16-1)*2 = 246 | 246
skip flag | (1920+64)/4 - 1 = 495 | 495
no_residual_data_flag | (1920+64)/8 – 1 = 247 | 0
cbp of luma block | (1920+64)/4 - 1 = 495 | 495
cbp of intra chroma block | ((1920+64)/4 – 1)*2 = 990 | 0
merge_flag | (1920+64)/4 - 1 = 495 | 0
inter_pred_flag | (1920+64)/4 - 1 = 495 | 0
ref_idx (bin0) | ((1920+64)/4 – 1)*2= 990 | 0
mvd(bin0) | ((1920+64)/4 – 1)*4 = 1980 | 0
Total | 6433 | 1236
For a 1080p sequence
Memory requirement reduced by over 80%