## Slide 2
Advanced Sampling Filters for
Spatial Scalability And
Chroma Sampling Applications
Pankaj Topiwala
FastVDO
JCTVC-618

## Slide 3: Down Sampling
0 1/2 1
In the absence of other information, a
typical downsampler is a half-band filter
H
2
0 ½ 1

## Slide 4: Up Sampling
0 1/2 1
Similarly, in the absence of other information, a typical upsampler is also half-band filter
F
2
0 ½ 1

## Slide 5: Spatial Scalability
Interested in both directions
Caution: Concatenation of optimal filters may not be optimal!
2
H1
2
F1
Video
In
Video
Out

## Slide 6: Ignoring 2nd Channel In Perfect Rec Filter Bank
2
H1
2
F1
Video
In
Video
Out
….
2
H2
2
F2
….
- In 2-channel system, both at half-rate, keeping sample rate.
In PR FB (e.g., wavelets), aim for max regularity
In just one channel (lowpass), aim for maxflat

## Slide 7: Spatial Scalability
2
H1
2
F1
Video
In
Video
Out
In 2 and higher channels, PR is possible.
In spatial scalability, have only one channel.
PR is impossible.
That is why the Laplace Pyramid was invented.
- code downsampled lowpass (¼ sample rate)
- code the upsampled difference residual (full rate)
Spatial scalability is built on this.

## Slide 8: Laplace One Better
We can do better than the half-band
New optimization problem
  - max energy in lowpass
  - min error in recovered upsampled signal
No math (time..)
Show results

## Slide 9: Filters Under Test
Downsamplers
H11 = [1 0 -3 0 10 16 10 0 -3 0 1] / 32.
Svc13 = [ 2 0 -4 -3 5 19 26 19 5 -3 -4 0 2] / 64
Upsamplers
f7 = [-1 0 5 8 5 0 -1] / 8:
  Really a 4-tap, [-1 5 5 -1] / 8.
Svc4 = [ -3 19 19 -3] / 32.

## Slide 10: Spectral Response (Downsampler)

## Slide 11
Harbour

## Slide 12
Chart: RaceHorses
| 22 | 27 | 32 | 37
FV 11d 4u | 34.5072 | 33.4657 | 32.0577 | 30.2655
SVC 13d 4u | 33.5667 | 32.7272 | 31.5643 | 30.037

## Slide 13
Chart: BasketballDrill
| 22 | 27 | 32 | 37
FV 11d 4u | 34.845 | 33.9075 | 32.6325 | 31.0175
SVC 13d 4u | 34.0525 | 33.2925 | 32.2025 | 30.7475

## Slide 14: Chroma Sampling
Although spatial and chroma sampling are treated very differently (and very different filters are used), in principle they are quite similar
While not optimized for this application, we will show that these filters are also effective in chroma sampling

## Slide 15: RGB 4:4:4 to YUV 4:2:0 and Back
Just has color conversion as well
We introduce advanced color transforms
2
H1
2
F1
RGB
YUV
RGB
YUV

## Slide 17: Perf on Crowd Run, No Comp.
1. YcrCb. 2. YcoCg. 3. YfbFr. 4. YFbFrv2.

## Slide 18: Perf on Duck, No Comp.
1. YcrCb. 2. YcoCg. 3. YfbFr. 4. YFbFrv2.

## Slide 19: Color Spaces