## Slide 1: High level syntax for loop filter parameters

## Slide 2: Situation
In both SW and draft, loop filter parameters are created and remain constant picture, and can (and in the current SW typically will) change per picture
However, a lot of stuff is “per picture” although it ought to be per slice, or per tile, or per something else, because of history, loop filter work is mostly independent from high level syntax work, and often performed by other people
There are arguments in favor and against loop filters on sub-picture granularity.
No written contributions either way.
Parameter sets are designed to capture long-term constant properties, and not rapidly changing information.

## Slide 3: Option 1: PPS
Loop filter in PPS only
  Need to send PPSs every time loop filter params are updated
    + No major changes to draft or software
    - Some irrelevant data being sent
    - Problems for systems sending PPS out of band and certain architectures
    Asynchronous nature of parameter sets violated
    Loop filter per picture only

## Slide 4: Option 2: New APS
New APS as synchronous PPS, akin a persistent picture header
  Only one activation per picture, activated in first slice (like PPS)
  May stay constant between pictures (like PPS) or may change between pictures (like picture headers)
  Contains ONLY information that is expected to change frequently between pictures.
    + Only moderate changes to software, drafting work mostly done
    + PPS can be sent out of band, whereas new APS can be sent in-band—most architectural problems solved
    - Loop filter per picture only

## Slide 5: Option 3: Old APS
APS as a slice parameter set
  Allows activation of different APS in different slices of one given picture
  + Would allow changing loop filter parameters on a per slice level—flexibility, future proof
  Inadequate (for loop filter data) if long-term decision is to keep loop filters parameters per picture
  Until such time the former is agreed, we could create a Band-Aid by saying that loop filter data needs to be the same in all oldAPs activated in a given picture.

## Slide 6: Coding Efficiency
Option 1 needs more bits for the (redundant) transmission of PPS data other than frequently changing loop filters
Option 2 and 3, when designed correctly, should have the same overhead.

## Slide 7: Recommendation
If there is consensus in the group that loop filtering MAY move towards sub-picture granularity, go for option 3
If there is consensus that loop filtering stays in picture granularity, go for option 2
Option 1 not recommended.