## Slide 1
CRA
Poc 0
CRA
Poc 0
P
Poc 6
B
Poc -5
B
Poc -1
B
Poc 1
B
Poc 5
B
Poc 2
B
Poc 3
B
Poc 4
B
Poc -4
B
Poc -3
B
Poc -2
P
Poc -6
P
Poc 6
B
Poc 1
B
Poc 5
B
Poc 2
B
Poc 3
B
Poc 4
B
Poc -5
B
Poc -1
B
Poc -4
B
Poc -3
B
Poc -2
P
Poc -6
…..
…..
leading pictures:
Follow the CRA picture in decoding order but precede it in output order
normal pictures:
Follow the CRA picture in both decoding order and output order
Decoding order: from left to right, Poc: relative POC
Output order: from left to right, Poc: relative POC
B
Poc 7
B
Poc 8
B
Poc 9
B
Poc 7
B
Poc 8
B
Poc 9
P
Poc 10
P
Poc 10
lagging pictures: prior to the CRA in decoding order but follow it in output order
CRA picture:
I slices only
For each normal picture: inter prediction only from the CRA picture and/or other normal pictures (i.e., never from any picture other than the CRA picture or a normal picture)
Lagging pictures shall not exist
Concept

## Slide 2
clean random access (CRA) picture: A coded picture containing only I slices and for which each slice of the CRA picture has nal_unit_type equal to 4, all coded pictures that follow the CRA picture both in decoding order and output order shall not use inter prediction from any picture that precedes the CRA picture either in decoding order or output order; and any picture that precedes the CRA picture in decoding order also precedes the CRA picture in output order.
inter prediction: A prediction derived from decoded samples or data elements of reference pictures other than the current decoded picture.
prediction: An embodiment of the prediction process. (unchanged)
prediction process: The use of a predictor to provide an estimate of the sample value or data element currently being decoded. (unchanged)
predictor: A combination of specified values or previously decoded sample values or data elements used in the decoding process of subsequent sample values or data elements. (unchanged)
Text

## Slide 3
intra prediction: A prediction derived from the decoded samples or data elements of the same decoded slice.
B slice: A slice that may be decoded using intra prediction or inter prediction using at most two motion vectors and reference indices to predict the sample values of each block. (unchanged)
I slice: A slice that is decoded using intra prediction only. (unchanged)
P slice: A slice that may be decoded using intra prediction or inter prediction using at most one motion vector and reference index to predict the sample values of each block. (unchanged)
Text

## Slide 4
Summary and Discussion
The definitions of “inter prediction” and “intra prediction” are changed to cover also prediction of data elements, in addition to sample values (see the definition of prediction process and predictor). Thus this is equivalent to the “refer to” we wanted (to cover prediction of both sample values and data elements).
Actually, this changes also improves the definitions of “I slice”, “P slice”, and “B slice” (to be more generic).
If we keep the definitions of “inter prediction” and “intra prediction” unchanged but define the term “refer to” to cover sample values and data elements, then we may also additionally need to change the definitions of “I slice”, “P slice”, and “B slice”.
If it is acceptable to use the current definition of “inter prediction” and “intra prediction” for the definitions of “I slice”, “P slice”, and “B slice”, then using “inter prediction” (i.e., not “refer to”) is obviously also acceptable for the definition of “CRA picture”.