## Slide 1: CE8: Results of informal subjective viewing
The viewing was conducted
from 16:50 to 17:30
on Nov. 25 2011
at room T072

## Slide 2: Testing Environment
Playback: Dell Optiplex 790 (Core-i3)
  Linux
Monitor: Dell 3008 LCD
  30 inches, 2560x1600
  Due to playback capability of the PC, resolution was set to 1920x1080 (dot-by-dot display on center area)

## Slide 3: Viewing Procedure
Tests
  Test A: Slice boundary artifacts
    Anchor vs JCTVC-G207 (played back randomly)
    Kimono; HE-LDB, Qp37
  Test B: Line buffer reduction
    Anchor vs JCTVC-G212_option1 (played back randomly)
    BQMall, Cactus, Vidyo3, Vidyo4; HE-LDB, Qp37
Viewing
  5 to 6 persons per viewing session, sitting on two rows
  20 volunteers participated in the viewing
Voting
  Mark on “A” if A looks better  Add 2 points to A
  Mark on “B” if B looks better  Add 2 points to B
  Mark on both “A” and “B” if A and B looks similar  Add 1 point to both A and B

## Slide 4: Results (Scores)
Test A: SAO slice boundary artifact
  Anchor: 16
  Proposal (JCTVC-G207): 24
  Statistic analysis
    Even: 6, anchor: 5, test: 9
  Slice boundary artifact on anchor is likely to be recognized.  Recommend to conduct CE to address this issue
Test B: SAO and ALF line buffer reduction
  Anchor: 18.75
  Proposal: 21.25
  Statistic analysis (anchor/test)
    BQM: 18/22, Cactus 22/18, Vidyo3 15/25, Vidyo4 20/20
  No difference between the anchor and the proposal.  Recommend for adoption of JCTVC-G212 as tentatively agreed on at session A