## Slide 1
<number>
<number>
JCTVC-G056 (CE8 Subtest G):
Adaptive Loop Filtering of Chrominance Samples Using Luma Map
Hsan Guermazi
7th JCT Meeting in Geneva, November, 2011
Notes: This contribution presents a technique for the Adaptive Loop Filtering (ALF) of chrominance samples that employs the map used in ALF of the luminance samples.
In HM4.0, (1) ALF of the chrominance samples is applied only when ALF filtering is applied to the luminance samples and (2) CU-adaptive filtering is not applied for chrominance samples (i.e. ALF is applied to a whole frame of the chrominance samples, or it is not applied at all).
In the proposed technique, we apply either frame-based or CU-based ALF for chrominance samples as follows (see Figure 1):
<number>

## Slide 2: Proposed ALF of Chroma Samples
<number>
<number>
Notes: If ALF is not applied to the luminance samples, (a) it is also not applied to the chrominance samples.
If frame-based ALF is applied to the luminance samples, either (b) ALF is not applied at all, or (c) frame-based ALF is also applied to the chrominance samples.
If CU-based ALF is applied to the luminance samples, either (d) ALF is not applied at all, or (e) frame-based ALF is applied, or (f) CU-based ALF is also applied to the chrominance samples. When CU-based ALF is applied to the chrominance samples, we apply the same CU filter map generated for the luminance samples.
<number>

## Slide 3: Simulation Results (multi-pass)
<number>
 | Low Delay (P) HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 0.0% | -0.3% | -0.2%
Class C | 0.0% | -0.1% | -0.4%
Class D | 0.0% | -0.1% | -0.5%
Class E | 0.0% | -0.7% | -0.5%
Class F | -0.1% | -0.3% | -0.4%
Overall | 0.0% | -0.3% | -0.4%
Overall – F | 0.0% | -0.3% | -0.4%
Enc Time[%] | 100 % |  | 
Dec Time[%] | 98 % |  | 
Notes: . The proposed technique reduces the average decoding time (~1%) while also achieving better U/V BD-Rate (0.21%-0.19%) performance than those of HM4.0 [1].
<number>

## Slide 4: Simulation Results (multi-pass)
<number>
 | Low Delay (B) HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 0.0% | -0.4% | -0.1%
Class C | 0.0% | -0.3% | -0.4%
Class D | 0.0% | 0.0% | -0.2%
Class E | -0.1% | -0.7% | 0.2%
Class F | -0.1% | -0.4% | -0.4%
Overall | 0.0% | -0.3% | -0.2%
Overall – F | 0.0% | -0.3% | -0.1%
Enc Time[%] | 100 % |  | 
Dec Time[%] | 99 % |  | 

## Slide 5: Simulation Results (multi-pass)
<number>
 | Random Access HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0% | -0.2% | -0.2%
Class B | 0.0% | -0.1% | -0.1%
Class C | 0.0% | -0.2% | -0.2%
Class D | 0.0% | -0.2% | -0.2%
Class E |  |  | 
Class F | 0.0% | -0.1% | -0.1%
Overall | 0.0% | -0.2% | -0.1%
Overall – F | 0.0% | -0.2% | -0.2%
Enc Time[%] | 101 % |  | 
Dec Time[%] | 99 % |  | 

## Slide 6: Simulation Results (multi-pass)
<number>
 | Intra Only HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0% | 0.0% | -0.1%
Class B | 0.0% | -0.1% | -0.1%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.0% | -0.1% | -0.1%
Class F | 0.0% | -0.1% | -0.1%
Overall | 0.0% | -0.1% | -0.1%
Overall – F | 0.0% | -0.1% | -0.1%
Enc Time[%] | 101 % |  | 
Dec Time[%] | 100 % |  | 

## Slide 7
Summary
Average chroma BD-rate gain of 0.2 %
Average decoder complexity reduced by 1%.
 | Y BD-rate | U BD-rate | V BD-rate
All | -0.01 % | -0.21 % | -0.19 %
All – Class F | 0.00 % | -0.22 % | -0.18 %
Enc Time[%] | 101 %
Dec Time[%] | 99 %