## Slide 1
<number>
JCTVC-G057 (CE3): eBrisk’s Adaptive Interpolation Filtering Technique
Hsan Guermazi
7th JCTVC Meeting in Geneva
21-30 November 2011
Notes: <number>

## Slide 2: HM 4.0 Interpolation
<number>
¼ | -1, 4, -10, 57, 19, -7, 3, -1
½ | -1, 4, -11, 40, 40, -11, 4, -1
Sub-sample position | Vertical | Horizontal
ai.j | None | F_1/4
bi.j | None | F_1/2
ci.j | None | F_3/4
di.j | F_1/4 | None
ei.j | F_1/4 | F_1/4
fi.j | F_1/4 | F_1/2
gi.j | F_1/4 | F_3/4
hi.j | F_1/2 | None
ii.j | F_1/2 | F_1/4
ji.j | F_1/2 | F_1/2
ki.j | F_1/2 | F_3/4
ni.j | F_3/4 | None
pi.j | F_3/4 | F_1/4
qi.j | F_3/4 | F_1/2
ri.j | F_3/4 | F_3/4
Notes: <number>

## Slide 3: Proposed AIF Technique
<number>
For each referenced video slice, select between the ½-pel default and new filters. and between the ¼-pel default and new filters.
Convey selected filters through luma_filter_mode as follows:
¼ | {a0, a1, a2, a3, a4, a5, a6, a7}
½ | {b0, b1, b2, b3, b3, b2, b1, b0}
Luma_filter_mode | F_1/4 | F_1/2
0 | Default | Default
1 | Default | AIF (New)
2 | AIF (New) | Default
3 | AIF (New) | AIF (New)
Same HM 4.0 Filtering Structure
Notes: Filter selection occurs at the slice level. Luma_filter_mode_flag is sent in slice header
<number>

## Slide 4: Proposed AIF Technique
<number>
AIF Filter Generation:
  Step 1: Estimate MVs using HM 4.0 filters
  Step 2: Estimate filter coefficient values by minimizing the energy of prediction errors after performing MC using MVs from Step 1
AIF Filter Transmission:
  Compute differences between the filter coefficient values and the corresponding HM 4.0 filter coefficient values
  Transmit differences
Notes: Coefficients sent in the the slice header
<number>

## Slide 5: Simulation Results
<number>
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.6% | -0.7% | -0.7% | -3.2% | -0.9% | -1.3%
Class C | -0.4% | -0.5% | -0.4% | -1.0% | -0.3% | -0.2%
Class D | -0.2% | -0.1% | -0.6% | -0.5% | -0.2% | -0.4%
Class E | -0.9% | 0.2% | -0.4% | -6.0% | -1.3% | -1.0%
Overall | -0.5% | -0.3% | -0.5% | -2.5% | -0.7% | -0.7%
 | -0.5% | -0.3% | -0.6% | -2.5% | -0.7% | -0.8%
Enc Time[%] | 105% |  |  | 106% |  | 
Dec Time[%] | 98% |  |  | 97% |  | 
Mult[%] | -6% |  |  | -6% |  | 
Adds[%] | -7% |  |  | -7% |  | 
Access[%] | 0% |  |  | 0% |  | 
MemBand(2D) Ave.[%] | -1% |  |  | 0% |  | 
MemBand(2D) Max.[%] | 5% |  |  | 7% |  | 
MemBand(1D) Ave.[%] | -1% |  |  | 0% |  | 
MemBand(1D) Max.[%] | 4% |  |  | 7% |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 6: Simulation Results
<number>
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.2% | -0.1% | -0.8% | -0.1% | -0.3%
Class C | -0.1% | -0.1% | 0.1% | -0.5% | 0.3% | 0.1%
Class D | 0.1% | 0.5% | 0.4% | -0.1% | 0.4% | 0.2%
Class E | 0.1% | 0.7% | 1.2% | -1.9% | 0.6% | 0.0%
Overall | 0.0% | 0.2% | 0.3% | -0.8% | 0.3% | 0.0%
 | 0.0% | 0.1% | 0.3% | -0.8% | 0.3% | 0.0%
Enc Time[%] | 104% |  |  | 105% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 
Mult[%] | -7% |  |  | -6% |  | 
Adds[%] | -9% |  |  | -7% |  | 
Access[%] | -1% |  |  | 0% |  | 
MemBand(2D) Ave.[%] | -1% |  |  | -1% |  | 
MemBand(2D) Max.[%] | 8% |  |  | 8% |  | 
MemBand(1D) Ave.[%] | -1% |  |  | -1% |  | 
MemBand(1D) Max.[%] | 7% |  |  | 7% |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 7: Simulation Results
<number>
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.6% | -0.9% | -1.3% | -1.7% | -0.2% | -1.1%
Class B | 0.2% | -0.1% | 0.0% | 0.0% | -0.2% | -0.3%
Class C | 0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.2% | 0.1% | 0.1% | 0.2% | -0.1% | -0.1%
Class E |  |  |  |  |  | 
Overall | 0.0% | -0.2% | -0.3% | -0.4% | -0.1% | -0.4%
 | 0.0% | -0.2% | -0.2% | -0.4% | -0.1% | -0.3%
Enc Time[%] | 102% |  |  | 102% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 
Mult[%] | -5% |  |  | -5% |  | 
Adds[%] | -7% |  |  | -6% |  | 
Access[%] | -1% |  |  | -1% |  | 
MemBand(2D) Ave.[%] | -1% |  |  | -1% |  | 
MemBand(2D) Max.[%] | 4% |  |  | 7% |  | 
MemBand(1D) Ave.[%] | -1% |  |  | -1% |  | 
MemBand(1D) Max.[%] | 5% |  |  | 6% |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 8: Visual Quality Check
<number>
Zoom on the 100th frame of PartyScene encoded with QP=37. LD(P)-LC. (HM4.0+SAO OFF) | Zoom on the 100th frame of PartyScene encoded with QP=37. LD(P)-LC. (G057 + SAO OFF)
Almost the same as HM4.0
Better than HM4.0 when SAO is disabled
Notes: We believe RA results are lower compared with the LD as a result of the use of future pictures in B slices
<number>

## Slide 9: Conclusion
<number>
BD-rate relative to HM 4.0
  0.70%, 0.15% and 0.27% average Y, U and V BD-rate reductions (respectively) compared to those of HM 4.0.
Complexity relative to HM 4.0
  Run times: 99% and 104% for decoder and encoder (respectively)
  Multiplications: -6% and 0% for average case and worst case (respectively)
  Additions: -7% and 0% for average case and worst case (respectively)
  Memory Access & Bandwidth: same as HM4.0
Visual quality relative to HM 4.0
  Almost the same relative to HM4.0
  Better than HM4.0 when SAO is disabled