## Slide 1
<number>
JCTVC-G058 (CE3): eBrisk’s Interpolation using different-length horizontal and vertical filters
Hsan Guermazi
7th JCTVC Meeting in Geneva
21-30 November 2011
Notes: <number>

## Slide 2: HM 4.0 Interpolation
<number>
Filtering stage | Filter | Taps | Filter coefficients
Horizontal & Vertical | F1/8 | 4 | {-3, 60, 8, -1}
 | F1/4 | 4 | {-4, 54, 16, -2}
 | F3/8 | 4 | {-5, 46, 27, -4}
 | F1/2 | 4 | {-4, 36, 36, -4}
Filtering stage | Filter | Taps | Filter coefficients
Horizontal & Vertical | F1/4 | 8 | {-1, 4, -10, 57, 19, -7, 3, -1}
 | F1/2 | 8 | {-1, 4, -11, 40, 40, -11, 4, -1}
Same filter set (F) is used during the horizontal and the vertical filtering stages
Fixed Luma filter coefficients
Fixed Chroma filter coefficients

## Slide 3: Proposed Interpolation Technique
<number>
Motivation
  Reduce number of vertical lines.
  Allow higher-accuracy interpolation in the horizontal direction.
Proposal
  Use shorter interpolation filters in the vertical direction than in the horizontal direction.
  Both filters are fixed (i.e., known coefficients).
  For horizontal filtering, we employ the variant B filters from the joint CE3 contribution JCTVC-G778.
  For vertical filtering, we employ the filters from the CE3 contribution JCTVC-G775.
Notes: Filter selection occurs at the slice level. Luma_filter_mode_flag is sent in slice header
<number>

## Slide 4: Proposed Interpolation Technique
<number>
Filtering stage | Filter | Taps | Filter coefficients
Horizontal | H_F1/4 | 7 | {-1, 3, -8, 60, 13, -4, 1, 0}
 | H_F1/2 | 8 | {-1, 4, -11, 40, 40, -11, 4, -1}
Vertical | V_F1/4 | 7 | {-2, 5, -11, 58, 18, -6, 2, 0}
 | V_F1/2 | 6 | { 0, 2, -9, 39, 39, -9, 2, 0}
Filtering stage | Filter | Taps | Filter coefficients
Horizontal | H_F1/8 | 4 | {-2, 61, 6, -1}
 | H_F1/4 | 4 | {-4, 54, 16, -2}
 | H_F3/8 | 4 | {-5, 44, 29, -4}
 | H_F1/2 | 4 | {-4, 36, 36, -4}
Vertical | V_F1/8 | 4 | {-2, 58, 10, -2}
 | V_F1/4 | 4 | {-4, 54, 16, -2}
 | V_F3/8 | 4 | {-6, 46, 28, -4}
 | V_F1/2 | 4 | {-4, 36, 36, -4}
Fixed Luma filter coefficients
Fixed Chroma filter coefficients
Notes: Filter selection occurs at the slice level. Luma_filter_mode_flag is sent in slice header
<number>

## Slide 5: Simulation Results
<number>
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.2% | -0.2% | -0.1% | -0.8% | -0.2% | -0.5%
Class C | -0.2% | 0.1% | 0.3% | -0.3% | 0.2% | 0.2%
Class D | 0.2% | -0.1% | -0.2% | 0.1% | 0.2% | 0.1%
Class E | -0.9% | -0.3% | -0.2% | -2.1% | -1.4% | -0.7%
Overall | -0.2% | -0.1% | 0.0% | -0.7% | -0.2% | -0.2%
 | -0.2% | -0.1% | -0.1% | -0.7% | -0.3% | -0.3%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Mult[%] | -5% |  |  | -5% |  | 
Adds[%] | -7% |  |  | -7% |  | 
Access[%] | 0% |  |  | 0% |  | 
MemBand(2D) Ave.[%] | 0% |  |  | 0% |  | 
MemBand(2D) Max.[%] | 5% |  |  | 6% |  | 
MemBand(1D) Ave.[%] | 0% |  |  | 0% |  | 
MemBand(1D) Max.[%] | 5% |  |  | 6% |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 6: Simulation Results
<number>
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.2% | -0.4% | -0.2% | -0.4% | -0.4% | -0.4%
Class C | 0.0% | 0.1% | 0.1% | 0.1% | 0.5% | 0.2%
Class D | 0.5% | 0.1% | 0.6% | 0.7% | 0.5% | 0.3%
Class E | -0.4% | 0.4% | 0.3% | -0.8% | -0.1% | -0.5%
Overall | 0.0% | 0.0% | 0.2% | -0.1% | 0.1% | -0.1%
 | 0.0% | 0.0% | 0.1% | -0.1% | 0.0% | -0.1%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Mult[%] | -5% |  |  | -5% |  | 
Adds[%] | -7% |  |  | -7% |  | 
Access[%] | 0% |  |  | 0% |  | 
MemBand(2D) Ave.[%] | 0% |  |  | 0% |  | 
MemBand(2D) Max.[%] | 11% |  |  | 5% |  | 
MemBand(1D) Ave.[%] | -1% |  |  | 0% |  | 
MemBand(1D) Max.[%] | 9% |  |  | 4% |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 7: Simulation Results
<number>
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | -0.1% | 0.6% | 0.5%
Class B | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | -0.1%
Class C | 0.1% | 0.1% | 0.2% | 0.3% | 0.2% | 0.3%
Class D | 0.1% | 0.3% | 0.2% | 0.7% | 0.2% | 0.2%
Class E |  |  |  |  |  | 
Overall | 0.0% | 0.1% | 0.1% | 0.2% | 0.2% | 0.2%
 | 0.0% | 0.1% | 0.1% | 0.2% | 0.2% | 0.2%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Mult[%] | -5% |  |  | -5% |  | 
Adds[%] | -7% |  |  | -7% |  | 
Access[%] | 1% |  |  | 0% |  | 
MemBand(2D) Ave.[%] | 0% |  |  | 0% |  | 
MemBand(2D) Max.[%] | 7% |  |  | 8% |  | 
MemBand(1D) Ave.[%] | 0% |  |  | 0% |  | 
MemBand(1D) Max.[%] | 7% |  |  | 8% |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 8: Visual Quality Check
<number>
Zoom on the 100th frame of PartyScene encoded with QP=37. LD(P)-LC. (HM4.0+SAO OFF)
Zoom on the 100th frame of PartyScene encoded with QP=37. LD(P)-LC. (G058 + SAO OFF)
Almost the same as HM4.0
Better than HM4.0 when SAO is disabled
Notes: We believe RA results are lower compared with the LD as a result of the use of future pictures in B slices
<number>

## Slide 9: Conclusion
<number>
BD-rate relative to HM 4.0
  0.13%, 0.00% and 0.00% average Y, U and V BD-rate reductions (respectively) compared to those of HM 4.0
Complexity relative to HM 4.0
  Multiplications: -5% and -5% for average case and worst case (respectively)
  Additions: -7% and -6% for average case and worst case (respectively)
  Memory Access & Bandwidth: Almost the same as HM4.0
Visual quality relative to HM 4.0
  Almost the same relative to HM4.0
  Better than HM4.0 when SAO is disabled