## Slide 1
<number>
JCTVC-G063 (CE3): eBrisk’s Adaptive interpolation using different-length horizontal and vertical filters
Hsan Guermazi, eBrisk Video
7th JCTVC Meeting in Geneva
21-30 November 2011
Notes: <number>

## Slide 2: HM 4.0 Interpolation
<number>
Filtering stage | Filter | Taps | Filter coefficients
Horizontal & Vertical | F1/8 | 4 | {-3, 60, 8, -1}
 | F1/4 | 4 | {-4, 54, 16, -2}
 | F3/8 | 4 | {-5, 46, 27, -4}
 | F1/2 | 4 | {-4, 36, 36, -4}
Filtering stage | Filter | Taps | Filter coefficients
Horizontal & Vertical | F1/4 | 8 | {-1, 4, -10, 57, 19, -7, 3, -1}
 | F1/2 | 8 | {-1, 4, -11, 40, 40, -11, 4, -1}
Same filter set (F) is used during the horizontal and the vertical filtering stages
Table 1: Fixed Luma filter coefficients
Table 2: Fixed Chroma filter coefficients

## Slide 3: Proposed AIF Technique
<number>
AIF technique based mainly on the technique in [CTVC-G057]
Differences
  Use of shorter filter for vertical and longer filter for horizontal interpolation
  Both filters can be default or newly-generated
  Default/newly-generated horizontal filters are 7Q8H
  Default/newly-generated vertical filters are 7Q6H
  Horizontal default filters correspond to variant B from joint CE3 contribution on solid interpolation filter [JCTVC-G778]
  Vertical default filters correspond to the tested variant in CE3 as solid (non-switchable) interpolation filter [JCTVC-G775 ]
Notes: Filter selection occurs at the slice level. Luma_filter_mode_flag is sent in slice header
<number>

## Slide 4: Proposed Interpolation Technique
<number>
Filtering stage | Filter | Taps | Filter coefficients
Horizontal | H_F1/4 | 7 | {-1, 3, -8, 60, 13, -4, 1}
 | H_F1/2 | 8 | {-1, 4, -11, 40, 40, -11, 4, -1}
Vertical | V_F1/4 | 7 | {-2, 5, -11, 58, 18, -6, 2}
 | V_F1/2 | 6 | {2, -9, 39, 39, -9, 2}
Table 1: Default Luma filter coefficients
Filtering stage | Filter | Taps | Filter coefficients
Horizontal | H_F1/4 | 7 | {a0, a1, a2, a3, a4, a5, a6}
 | H_F1/2 | 8 | {b0, b1, b2, b3, b3, b2, b1, b0}
Vertical | V_F1/4 | 7 | {c0, c1, c2, c3, c4, c5, c6}
 | V_F1/2 | 6 | {d0, d1, d2, d2, d1, d0}
Table 2: Newly-generated Luma filter coefficients
Notes: Filter selection occurs at the slice level. Luma_filter_mode_flag is sent in slice header
<number>

## Slide 5: Proposed Interpolation Technique
<number>
Filtering stage | Filter | Taps | Filter coefficients
Horizontal | H_F1/8 | 4 | {-2, 61, 6, -1}
 | H_F1/4 | 4 | {-4, 54, 16, -2}
 | H_F3/8 | 4 | {-5, 44, 29, -4}
 | H_F1/2 | 4 | {-4, 36, 36, -4}
Vertical | V_F1/8 | 4 | {-2, 58, 10, -2}
 | V_F1/4 | 4 | {-4, 54, 16, -2}
 | V_F3/8 | 4 | {-6, 46, 28, -4}
 | V_F1/2 | 4 | {-4, 36, 36, -4}
Table 3: Fixed Chroma filter coefficients
Notes: Filter selection occurs at the slice level. Luma_filter_mode_flag is sent in slice header
<number>

## Slide 6: Simulation Results
<number>
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.7% | -1.2% | -1.1% | -3.7% | -1.2% | -2.0%
Class C | -0.4% | -0.1% | -0.1% | -1.1% | 0.2% | 0.1%
Class D | 0.2% | -0.2% | -0.5% | -0.2% | 0.2% | -0.1%
Class E | -0.7% | 0.2% | 0.4% | -6.2% | -1.7% | -1.1%
Overall | -0.4% | -0.4% | -0.4% | -2.7% | -0.6% | -0.8%
 | -0.4% | -0.5% | -0.5% | -2.7% | -0.6% | -0.9%
Enc Time[%] | 104% |  |  | 105% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 
Mult[%] | -7% |  |  | -6% |  | 
Adds[%] | -9% |  |  | -9% |  | 
Access[%] | 1% |  |  | 1% |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 7: Simulation Results
<number>
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.4% | -0.3% | -1.0% | -0.4% | -0.5%
Class C | 0.0% | 0.2% | 0.2% | -0.3% | 0.6% | 0.3%
Class D | 0.8% | 0.6% | 0.5% | 0.6% | 0.7% | 0.4%
Class E | 0.8% | 1.4% | 1.7% | -1.6% | 1.0% | 0.5%
Overall | 0.3% | 0.3% | 0.4% | -0.5% | 0.4% | 0.1%
 | 0.4% | 0.3% | 0.4% | -0.5% | 0.3% | 0.1%
Enc Time[%] | 103% |  |  | 103% |  | 
Dec Time[%] | 100% |  |  | 99% |  | 
Mult[%] | -8% |  |  | -7% |  | 
Adds[%] | -11% |  |  | -10% |  | 
Access[%] | 0% |  |  | 0% |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 8: Simulation Results
<number>
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.9% | -1.1% | -1.5% | -2.2% | 0.0% | -0.8%
Class B | 0.0% | -0.2% | -0.3% | -0.3% | -0.3% | -0.5%
Class C | 0.1% | 0.0% | 0.1% | 0.1% | 0.1% | 0.0%
Class D | 0.2% | 0.4% | 0.4% | 0.6% | 0.0% | 0.2%
Class E |  |  |  |  |  | 
Overall | -0.1% | -0.2% | -0.3% | -0.4% | -0.1% | -0.3%
 | -0.1% | -0.2% | -0.3% | -0.4% | 0.0% | -0.2%
Enc Time[%] | 102% |  |  | 103% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Mult[%] | -7% |  |  | -7% |  | 
Adds[%] | -9% |  |  | -10% |  | 
Access[%] | 0% |  |  | 0% |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 9: Visual Quality Check
<number>
Slightly better relative to HM4.0
Notes: We believe RA results are lower compared with the LD as a result of the use of future pictures in B slices
<number>

## Slide 10: Visual Quality Check
<number>
Better than HM4.0 when SAO is disabled
Notes: We believe RA results are lower compared with the LD as a result of the use of future pictures in B slices
<number>

## Slide 11: Conclusion
<number>
BD-rate relative to HM 4.0
  0.65%. 0.09% and 0.22% average Y, U and V BD-rate reductions (respectively) compared to those of HM 4.0.
Complexity relative to HM 4.0
  Multiplications: -7 % and -5% for average case and worst case (respectively)
  Additions: -10% and -6% for average case and worst case (respectively)
  Access: almost same as HM4.0
Visual quality relative to HM 4.0
  Slightly better than HM4.0
  Better than HM4.0 when SAO is disabled