## Slide 1
<number>
<number>
RIM, Samsung and Sony
November 25, 2011
A Combined Proposal from JCTVC-G366, JCTVC-G657, and JCTVC-G768 on Context Reduction of Significance Map with CABAC
JCTVC-G1015
Notes: <number>

## Slide 2: Summary
Three non-CE contributions on significance map context reductions with commonality:
  JCTC-G366 (Sony)
  JCTVC-G657 (RIM)
  JCTC-G768 (Samsung)
Propose to combine the best of the three significance map contributions.
Show how that could work with level context reductions from JCTVC-G121 in CE11 and with JCTVC-G718
  40 significance map context reductions.
  36 level context reductions from JCTVC-G121.
  56 level context reductions from JCTVC-G718.
<number>

## Slide 3: Context Reduction of 4x4
HM4 has 15 luma and 15 chroma 4x4 significance map contexts.
Proposed has 9 luma and 6 chroma 4x4 significance map contexts.
  Reduction of 15 contexts.
<number>
0
1
1
1
4
4
3
3
2
3
2
3
5
5
5
4x4 Chroma SigMap
Context Grouping
0
1
4
5
6
6
8
8
2
3
2
3
7
7
7
4x4 Luma SigMap
Context Grouping
0
1
4
5
8
9
12
13
2
3
6
7
10
11
14
HM4 4x4 Luma and Chroma
SigMap Context Grouping

## Slide 4: Context Reduction of 8x8
HM4 has 16 luma and 16 chroma 8x8 significance map contexts.
Proposed has 11 luma and 11 chroma 8x8 significance map contexts.
  Reduction of 10 contexts.
<number>
Proposed 8x8 Luma and Chroma
SigMap Context Grouping
15*
1
4
5
8
10
12
12
2
3
10
3
10
11
11
11
0
1
4
5
8
10
12
12
2
3
10
3
10
11
11
11
0
1
4
5
8
10
12
12
2
3
10
3
10
11
11
11
0
1
4
5
8
10
12
12
2
3
10
3
10
11
11
HM4 8x8 Luma and Chroma
SigMap Context Grouping
0
1
4
5
8
9
12
13
2
3
6
7
10
11
14
15
0
1
4
5
8
9
12
13
2
3
6
7
10
11
14
15
0
1
4
5
8
9
12
13
2
3
6
7
10
11
14
15
0
1
4
5
8
9
12
13
2
3
6
7
10
11
14

## Slide 5: Context Reduction of 16x16/32x32
HM4 has 13 luma and 13 chroma 16x16/32x32 significance map contexts.
Proposed has 7 luma and 4 chroma 16x16/32x32 significance map contexts.
  Reduction of 15 contexts.
<number>

## Slide 6: Average Luminance BDR Results
BDR without level coding
 | I_HE | RA_HE | LB_HE | LP_HE
QP(22,27,32,37) | 0.05 | -0.02 | 0.03 | 0.04
LQP(12,17,22,27) | 0.09 | 0.00 | 0.02 | 0.02
RDOQ-OFF | 0.02 | -0.02 | -0.02 | 0.01

## Slide 7: Integration with level coding
BDR with JCTVC-G121
  40 significance map context reductions and 36 level context reductions from JCTVC-G121.
BDR with JCTVC- G718
  40 significance map context reductions and 56 level context reductions from JCTVC-G718 (test still running)
<number>
 | I_HE | RA_HE | LB_HE | LP_HE
QP(22,27,32,37) | 0.10 | 0.02 | 0.03 | 0.05
LQP(12,17,22,27) | 0.17 | 0.04 | 0.04 | 0.04
RDOQ-OFF | 0.06 | -0.01 | 0.00 | 0.01
 | I_HE | RA_HE | LB_HE | LP_HE
QP(22,27,32,37) | 0.05 |  |  | 
LQP(12,17,22,27) | 0.09 |  |  | 
RDOQ-OFF | 0.02 |  |  | 

## Slide 8: Conclusions
The best of JCTVC-G366, JCTVC-G657, and JCTVC-G768 were combined to achieve 40 context reductions in significance map coding with CABAC.
  Average BDR is 0.0% for all test cases except I_HE at low QP with 0.1% BDR.
Propose to be adopted in HM5.
<number>

## Slide 9: Appendix
<number>

## Slide 10: BDR without JCTVC-G121
<number>
 | All Intra HE |  |  | All Intra (Low QP) |  |  | All Intra (RDOQ off) |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.05% | 0.28% | 0.40% | 0.10% | 0.11% | 0.11% | 0.10% | 0.28% | 0.18%
Class B | 0.04% | 0.17% | 0.14% | 0.15% | 0.15% | 0.16% | 0.01% | 0.16% | 0.21%
Class C | 0.03% | 0.07% | 0.08% | 0.05% | 0.05% | 0.09% | -0.02% | 0.06% | 0.07%
Class D | 0.03% | 0.10% | 0.10% | 0.01% | 0.07% | 0.07% | -0.04% | 0.05% | 0.05%
Class E | 0.09% | 0.06% | 0.10% | 0.13% | 0.13% | 0.21% | 0.05% | 0.36% | 0.30%
Class F |  |  |  |  |  |  |  |  | 
Overall | 0.05% | 0.14% | 0.17% | 0.09% | 0.10% | 0.12% | 0.02% | 0.17% | 0.16%
 | 0.05% | 0.13% | 0.14% | 0.10% | 0.08% | 0.11% | 0.02% | 0.17% | 0.15%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 102% |  |  | 101% |  |  | 100% |  | 
 | Random Access HE |  |  | Random Access (Low QP) |  |  | Random Access(RDOQ off) |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.06% | 0.38% | 0.56% | 0.01% | 0.21% | 0.30% | 0.05% | -0.04% | 0.08%
Class B | -0.01% | 0.07% | 0.00% | 0.05% | 0.07% | -0.05% | -0.01% | -0.02% | 0.04%
Class C | 0.03% | -0.01% | 0.03% | -0.01% | 0.03% | 0.03% | 0.02% | -0.04% | 0.03%
Class D | -0.02% | 0.31% | -0.13% | -0.05% | -0.03% | -0.22% | 0.04% | -0.04% | -0.31%
Class E |  |  |  |  |  |  |  |  | 
Class F |  |  |  |  |  |  |  |  | 
Overall | -0.02% | 0.18% | 0.11% | 0.00% | 0.07% | 0.01% | -0.02% | 0.04% | 0.04%
 | 0.00% | 0.13% | 0.09% | 0.00% | 0.07% | -0.01% | -0.01% | 0.02% | 0.04%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  |  | 97% |  | 
 | Low delay B HE |  |  | Low delay B (Low QP) |  |  | Low delay B (RDOQ off) |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.00% | -0.08% | -0.25% | 0.05% | 0.03% | -0.07% | -0.03% | -0.25% | -0.29%
Class C | 0.09% | -0.10% | -0.15% | 0.03% | 0.01% | -0.10% | 0.02% | 0.08% | -0.21%
Class D | 0.03% | 0.45% | -0.33% | -0.01% | -0.11% | -0.18% | -0.02% | -1.11% | -0.31%
Class E | 0.02% | -0.35% | 0.08% | 0.02% | -0.26% | -0.09% | -0.04% | -0.25% | 0.27%
Class F |  |  |  |  |  |  |  |  | 
Overall | 0.03% | 0.00% | -0.18% | 0.02% | -0.06% | -0.11% | -0.02% | -0.38% | -0.17%
 | 0.03% | 0.00% | -0.26% | 0.02% | -0.07% | -0.15% | -0.02% | -0.39% | -0.19%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  |  | 101% |  | 
 | Low delay P HE |  |  | Low delay P (Low QP) |  |  | Low delay P (RDOQ off) |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | -0.02% | -0.13% | 0.29% | 0.05% | 0.05% | -0.06% | 0.01% | -0.31% | -0.44%
Class C | 0.06% | -0.07% | -0.21% | 0.02% | 0.02% | -0.10% | 0.02% | -0.15% | -0.13%
Class D | 0.09% | -0.32% | -0.57% | -0.01% | -0.11% | -0.32% | -0.01% | -0.95% | -0.64%
Class E | 0.01% | -0.07% | -0.81% | 0.03% | -0.34% | -0.25% | 0.04% | -1.04% | -0.52%
Class F |  |  |  |  |  |  |  |  | 
Overall | 0.04% | -0.15% | -0.26% | 0.02% | -0.07% | -0.17% | 0.01% | -0.57% | -0.43%
 | 0.03% | -0.15% | -0.36% | 0.02% | -0.07% | -0.17% | 0.01% | -0.49% | -0.47%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 101% |  | 

## Slide 11: BDR with JCTVC-G121
<number>
 | All Intra HE |  |  | All Intra (Low QP) |  |  | All Intra (RDOQ off) |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.09% | 0.34% | 0.44% | 0.16% | 0.19% | 0.15% | 0.12% | 0.29% | 0.26%
Class B | 0.11% | 0.22% | 0.22% | 0.22% | 0.21% | 0.25% | 0.06% | 0.22% | 0.24%
Class C | 0.09% | 0.16% | 0.15% | 0.15% | 0.14% | 0.18% | 0.03% | 0.08% | 0.14%
Class D | 0.10% | 0.21% | 0.20% | 0.12% | 0.20% | 0.18% | 0.03% | 0.07% | 0.10%
Class E | 0.11% | 0.12% | 0.17% | 0.21% | 0.19% | 0.27% | 0.08% | 0.44% | 0.34%
Class F |  |  |  |  |  |  |  |  | 
Overall | 0.10% | 0.21% | 0.24% | 0.17% | 0.19% | 0.20% | 0.06% | 0.21% | 0.21%
 | 0.10% | 0.21% | 0.22% | 0.18% | 0.16% | 0.19% | 0.06% | 0.20% | 0.21%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  |  | 100% |  | 
 | Random Access HE |  |  | Random Access (Low QP) |  |  | Random Access(RDOQ off) |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.05% | 0.44% | 0.34% | 0.03% | 0.24% | 0.33% | 0.04% | -0.09% | 0.05%
Class B | 0.02% | 0.11% | 0.19% | 0.08% | 0.07% | 0.00% | -0.05% | 0.05% | -0.02%
Class C | 0.05% | -0.08% | 0.07% | 0.03% | 0.04% | 0.10% | 0.00% | -0.04% | -0.08%
Class D | 0.07% | -0.01% | -0.25% | 0.02% | 0.03% | -0.30% | 0.08% | -0.20% | -0.13%
Class E |  |  |  |  |  |  |  |  | 
Class F |  |  |  |  |  |  |  |  | 
Overall | 0.02% | 0.11% | 0.10% | 0.04% | 0.09% | 0.03% | -0.01% | 0.06% | 0.05%
 | 0.04% | 0.07% | 0.08% | 0.04% | 0.11% | 0.00% | 0.00% | 0.05% | 0.07%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 97% |  | 
 | Low delay B HE |  |  | Low delay B (Low QP) |  |  | Low delay B (RDOQ off) |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.00% | -0.21% | -0.31% | 0.07% | 0.09% | -0.06% | 0.00% | -0.06% | -0.35%
Class C | 0.08% | -0.25% | -0.15% | 0.05% | -0.07% | -0.07% | 0.05% | 0.00% | -0.21%
Class D | 0.00% | -0.09% | -0.49% | 0.00% | -0.14% | -0.12% | 0.00% | -0.72% | -0.68%
Class E | 0.07% | -0.55% | 0.14% | 0.02% | -0.51% | -0.15% | -0.08% | -0.96% | -0.13%
Class F |  |  |  |  |  |  |  |  | 
Overall | 0.03% | -0.25% | -0.23% | 0.04% | -0.12% | -0.10% | 0.00% | -0.38% | -0.36%
 | 0.03% | -0.23% | -0.22% | 0.04% | -0.15% | -0.14% | 0.00% | -0.38% | -0.34%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  |  | 100% |  | 
 | Low delay P HE |  |  | Low delay P (Low QP) |  |  | Low delay P (RDOQ off) |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | -0.04% | -0.04% | -0.31% | 0.06% | 0.09% | -0.10% | 0.00% | -0.31% | -0.45%
Class C | 0.04% | 0.06% | -0.03% | 0.01% | 0.05% | -0.04% | 0.02% | -0.31% | -0.25%
Class D | 0.09% | -0.13% | -0.57% | -0.01% | -0.09% | -0.24% | -0.01% | -0.76% | -1.08%
Class E | 0.16% | -0.08% | -0.13% | 0.09% | 0.04% | 0.27% | 0.02% | -1.34% | 0.43%
Class F |  |  |  |  |  |  |  |  | 
Overall | 0.05% | -0.04% | -0.27% | 0.04% | 0.03% | -0.05% | 0.01% | -0.62% | -0.39%
 | 0.05% | 0.00% | -0.30% | 0.04% | 0.03% | -0.05% | 0.01% | -0.48% | -0.38%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  |  | 101% |  | 

## Slide 12: BDR with JCTVC-G718
<number>
 | All Intra HE |  | 
 | Y | U | V
Class A | 0.05% | 0.28% | 0.47%
Class B | 0.05% | 0.18% | 0.18%
Class C | 0.03% | 0.12% | 0.12%
Class D | 0.03% | 0.11% | 0.10%
Class E | 0.10% | 0.07% | 0.12%
Overall | 0.05% | 0.16% | 0.20%
 | 0.05% | 0.15% | 0.18%
All Intra HE (low QP) |  | 
Y | U | V
0.10% | 0.12% | 0.11%
0.15% | 0.14% | 0.18%
0.05% | 0.05% | 0.09%
0.01% | 0.09% | 0.06%
0.14% | 0.12% | 0.21%
0.09% | 0.10% | 0.13%
0.10% | 0.09% | 0.12%
 | Random Access HE |  | 
 | Y | U | V
Class A | #VALUE! | #VALUE! | #VALUE!
Class B | -0.01% | 0.24% | 0.09%
Class C | 0.00% | -0.08% | 0.01%
Class D | 0.01% | 0.05% | -0.24%
Class E |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE!
 | #VALUE! | #VALUE! | #VALUE!
 | Low Delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE!
Class C | 0.08% | -0.06% | -0.04%
Class D | -0.01% | 0.20% | 0.24%
Class E | 0.11% | -0.03% | 0.83%
Overall | #VALUE! | #VALUE! | #VALUE!
 | #VALUE! | #VALUE! | #VALUE!
Random Access HE (low QP) |  | 
Y | U | V
#VALUE! | #VALUE! | #VALUE!
#VALUE! | #VALUE! | #VALUE!
-0.02% | 0.02% | -0.02%
-0.04% | 0.04% | -0.29%
#VALUE! | #VALUE! | #VALUE!
#VALUE! | #VALUE! | #VALUE!
Low Delay B (low QP) |  | 
Y | U | V
#VALUE! | #VALUE! | #VALUE!
0.03% | -0.10% | -0.10%
-0.03% | -0.18% | -0.19%
0.03% | -0.61% | 0.04%
#VALUE! | #VALUE! | #VALUE!
#VALUE! | #VALUE! | #VALUE!
All Intra HE (RDOQ Off) |  | 
Y | U | V
0.10% | 0.27% | 0.20%
0.03% | 0.17% | 0.22%
-0.02% | 0.03% | 0.08%
-0.03% | 0.04% | 0.01%
0.05% | 0.37% | 0.31%
0.02% | 0.17% | 0.16%
0.02% | 0.16% | 0.16%
Random Access (RDOQ off) |  | 
Y | U | V
#VALUE! | #VALUE! | #VALUE!
#VALUE! | #VALUE! | #VALUE!
0.02% | 0.08% | -0.03%
-0.06% | -0.29% | -0.10%
#VALUE! | #VALUE! | #VALUE!
#VALUE! | #VALUE! | #VALUE!
Low Delay B HE |  | 
Y | U | V
#VALUE! | #VALUE! | #VALUE!
0.04% | -0.04% | 0.08%
0.02% | -0.71% | -0.39%
-0.01% | -0.55% | -1.24%
#VALUE! | #VALUE! | #VALUE!
#VALUE! | #VALUE! | #VALUE!