## Slide 1: VLC for high level syntax (ALF and SAO parameters) (JCTVC-G122)
Vivienne Sze
Texas Instruments
Joint Collaborative Team on Video Coding (JCT-VC)
of ITU-T SG16 WP3 and ISO/IEC JTb1/SC29/WG11
7th Meeting: Geneva, CH, 21-30 Nov, 2011

## Slide 2: CABAC used for high level syntax
High level syntax is typically handled by firmware, which traditionally don’t have CABAC acceleration (JCTVC-F377).
For reduced system implementation complexity it is desirable for all syntax elements found in slice header, APS, PPS, and SPS be coded with simple VLC.
CABAC coded high level syntax elements in HM-4.0 include
  alf_cu_control_flag, alf_cu_control_max_depth, alf_length_cu_control_info, alf_cu_flag, sao_split_flag, sao_flag_cb, sao_flag_cr, sao_type_idx, sao_offset.

## Slide 3: Proposed Approach
Propose always using VLC for high level syntax elements even when CABAC is selected as the entropy coder. These parameters include
Byte alignment moved from before transmitting SAO parameters in the slice header to after the slice header.

## Slide 4: Experiment Results
HM-4.0 under common conditions
Simulation platform is LSF equipped with Intel(R) Xeon(R) CPU X5570@2.93GHz 64 bits Linux machines
Results cross-checked by HHI
Intra | Random Access | Low Delay
0.0 | 0.1 | 0.1

## Slide 5: Conclusions
Only use VLC for high level syntax elements
Negligible impact on coding efficiency (up to 0.1%)
Recommend for adoption into HEVC test model
  Draft text available in contribution