## Slide 1: JCTVC-G139: Non-CE6.d: Intra Prediction With Selective Secondary Boundary
Geert Van der Auwera, Xianglin Wang, Marta Karczewicz
Qualcomm Inc.

## Slide 2: Summary
Improvement of harmonized intra prediction with secondary boundary solution studied in CE6.d (JCTVC-G280)
Proposed to selectively apply prediction from secondary boundary to improve class F results
BD-rate improvement from 0.2% to -0.2% for class F

## Slide 3: Selective Secondary Boundary Intra Prediction
Analyze secondary boundary samples (2 locations only):
  IF (horizontal directional mode) THEN
    Value = MAX( | TR[N-2] -2*TR[N-1] + TR[N] |,
    | TR[N-3] -2*TR[N-2] + TR[N-1] | )
  IF ( Value < Threshold )
  THEN { Enable prediction} ELSE { Disable }
  Similar for vertical directional mode; independent of block size
TR[N-2]
TR[N-1]
TR[N-3]
(0,0)
(N,0)
(i,j)
(0,N)
(N,N)
TR[N-1]
TR[N]
TR[N-2]

## Slide 4: Selective Secondary Boundary Intra Prediction
Thresholding: values
  24 (VER+4…VER+7, VER-4…VER-8, HOR+4…HOR+7, HOR-4…HOR-7)
  128 (multi line VER, HOR, VER+8, HOR+8)
  256 (VER+8, HOR+8)

## Slide 5: Results
CE6.d harmonized solution (with class F)
Selective secondary boundary: improved class F
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.9% | -0.8% | -0.8% | -0.8% | -1.0% | -1.1%
Class B | -0.6% | -0.6% | -0.6% | -0.6% | -0.8% | -0.7%
Class C | -0.6% | -0.6% | -0.6% | -0.7% | -0.8% | -0.7%
Class D | -0.6% | -0.6% | -0.6% | -0.7% | -0.6% | -0.7%
Class E | -0.8% | -0.7% | -0.7% | -0.7% | -0.9% | -1.0%
Class F | -0.2% | -0.4% | -0.3% | 0.0% | -0.2% | -0.3%
Overall | -0.6% | -0.6% | -0.6% | -0.6% | -0.7% | -0.7%
 | -0.6% | -0.6% | -0.6% | -0.6% | -0.7% | -0.8%
Enc Time[%] | 101% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.9% | -0.8% | -0.9% | -0.8% | -1.0% | -1.1%
Class B | -0.6% | -0.6% | -0.6% | -0.6% | -0.8% | -0.8%
Class C | -0.6% | -0.6% | -0.7% | -0.7% | -0.8% | -0.7%
Class D | -0.7% | -0.6% | -0.7% | -0.7% | -0.7% | -0.7%
Class E | -0.8% | -0.7% | -0.9% | -0.7% | -0.9% | -0.9%
Class F | 0.2% | 0.1% | 0.1% | 0.2% | -0.1% | -0.2%
Overall | -0.6% | -0.6% | -0.6% | -0.5% | -0.7% | -0.7%
 | -0.6% | -0.6% | -0.6% | -0.5% | -0.7% | -0.7%
Class F Sequence | Y | U | V
BasketballDrillText | -0.5% | -0.5% | -0.6%
ChinaSpeed | 0.2% | 0.1% | 0.0%
SlideEditing | 0.0% | -0.2% | -0.1%
SlideShow | -0.5% | -1.0% | -0.7%
 | -0.2% | -0.4% | -0.3%
Class F Sequence | Y | U | V
BasketballDrillText | -0.5% | -0.6% | -0.7%
ChinaSpeed | 0.5% | 0.5% | 0.3%
SlideEditing | 1.1% | 0.8% | 0.8%
SlideShow | -0.2% | -0.3% | 0.1%
 | 0.2% | 0.1% | 0.1%
All Intra HE
All Intra HE

## Slide 6: Results
CE6.d harmonized solution results without class F
Selective secondary boundary: similar to CE6.d solution
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.9% | -0.8% | -0.9% | -0.8% | -1.0% | -1.1%
Class B | -0.6% | -0.6% | -0.6% | -0.6% | -0.8% | -0.8%
Class C | -0.6% | -0.6% | -0.7% | -0.7% | -0.8% | -0.7%
Class D | -0.7% | -0.6% | -0.7% | -0.7% | -0.7% | -0.7%
Class E | -0.8% | -0.7% | -0.9% | -0.7% | -0.9% | -0.9%
Overall | -0.7% | -0.7% | -0.7% | -0.7% | -0.8% | -0.8%
 | -0.7% | -0.7% | -0.7% | -0.7% | -0.8% | -0.9%
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.9% | -0.8% | -0.8% | -0.8% | -1.0% | -1.1%
Class B | -0.6% | -0.6% | -0.6% | -0.6% | -0.8% | -0.7%
Class C | -0.6% | -0.6% | -0.6% | -0.7% | -0.8% | -0.7%
Class D | -0.6% | -0.6% | -0.6% | -0.7% | -0.6% | -0.7%
Class E | -0.8% | -0.7% | -0.7% | -0.7% | -0.9% | -1.0%
Overall | -0.7% | -0.6% | -0.6% | -0.7% | -0.8% | -0.8%
 | -0.7% | -0.6% | -0.7% | -0.7% | -0.8% | -0.8%
Enc Time[%] | 101% |  |  | 99% |  | 
Dec Time[%] | 99% |  |  | 101% |  | 

## Slide 7: Conclusion
Method was presented to selectively apply intra prediction from secondary boundary
Improved BD-rate results for class F sequences
Similar execution times
Thanks to Sharp for cross checking! (JCTVC-G960)