## Slide 1: Non-CE6: Reducing Line Buffers for intra mode
Jaehyun Lim
LG Electronics
JCTVC-G145

## Slide 2: Introduction
Line buffer for intra mode
  The intra modes of 4x4 blocks are required to be stored in line buffers for determining the above MPM of a next LCU row
  The size of the line buffers is proportional to the picture width.
current
above
neighbor
left
neighbor
When this line indicates LCU boundary,
line-buffer is required for storing intra mode
[ MPM candidates ]

## Slide 3: Proposed method I
0
1
2
3
8x8 block boundary
4
5
…
…
Intra modes of these blue blocks are stored in the line buffer
Share the same intra mode
Method I: line buffer 2:1 compression
  Only half of intra modes in bottom 4x4 PUs for upper LCU are stored in line buffer.
  Right intra mode in every 8x8 block boundary is remained.

## Slide 4: Proposed method II
Method II: line buffer removal
  Whole line buffer for intra mode is removed.
  Planar mode is used if above MPM candidate is beyond the LCU boundary.
current
10
5
Left MPM candidate = 10
LCU boundary
above MPM candidate = 0 (planar mode)

## Slide 5: Experimental Results
Results on the proposed line buffer 2:1 compression vs HM4 anchor
 | All Intra HE |  |  | All Intra LC |  |  | Random Access HE |  |  | Random Access LC |  |  | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  |  |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | -0.1% | 0.1% | 0.0% | -0.1% | -0.2% | 0.0% | -0.1% | 0.1%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.3% | -0.1%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | -0.4% | 0.0% | 0.1% | 0.1% | 0.4% | 0.0% | -0.2% | -0.5%
Class E | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  |  |  |  |  | 0.1% | 0.6% | 1.3% | 0.0% | 0.3% | 0.6%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.1% | 0.3% | 0.0% | 0.1% | 0.0%
Enc Time | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time | 99% |  |  | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  | 

## Slide 6: Experimental Results
Results on the proposed line buffer removal vs HM4 anchor
 | All Intra HE |  |  | All Intra LC |  |  | Random Access HE |  |  | Random Access LC |  |  | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.2% | 0.0% | 0.0% | 0.1% | -0.1% |  |  |  |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | -0.3% | 0.0% | 0.0% | 0.0%
Class C | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | -0.1% | -0.1% | 0.0% | 0.2% | -0.1%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | -0.3% | 0.0% | 0.0% | 0.1% | 0.0% | 0.2% | -0.3% | 0.0% | 0.1% | 0.2%
Class E | 0.1% | 0.1% | 0.2% | 0.1% | 0.0% | 0.1% |  |  |  |  |  |  | 0.0% | 0.0% | 0.6% | 0.0% | -1.1% | 0.1%
Overall | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | 0.0%
Enc Time | 99% |  |  | 99% |  |  | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time | 100% |  |  | 99% |  |  | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  | 

## Slide 7: Conclusion
Line buffer reduction/removal for intra mode is proposed.
Almost no bitrate increase is observed without any encoding/decoding
time changes.
It is recommended to adopt the proposed line buffer removal scheme
to save the memory for storing intra mode.

## Slide 8: Proposed changes to WD text: method I
from
If intraPredModeN is greater than or equal to intraPredModeNum
  If intraPredModeNum is equal to 4 then candIntraPredModeN is set equal to mapIntraPredMode4[ intraPredModeN ]
  Otherwise candIntraPredModeN is set equal to mapIntraPredMode10[ intraPredModeN ]
Otherwise, candIntraPredModeN is set equal to intraPredModeN
to
If intraPredModeN is greater than or equal to intraPredModeNum
  If intraPredModeNum is equal to 4 then candIntraPredModeN is set equal to mapIntraPredMode4[ intraPredModeN - intraPredModeNum ]
  Otherwise candIntraPredModeN is set equal to mapIntraPredMode10[ intraPredModeN - intraPredModeNum ].
Otherwise, candIntraPredModeN is set equal to intraPredModeN

## Slide 9: Proposed changes to WD text: method II
from
If intraPredModeN is greater than or equal to intraPredModeNum
  If intraPredModeNum is equal to 4 then candIntraPredModeN is set equal to mapIntraPredMode4[ intraPredModeN ]
  Otherwise candIntraPredModeN is set equal to mapIntraPredMode10[ intraPredModeN ]
Otherwise, candIntraPredModeN is set equal to intraPredModeN
to
If intraPredModeN is greater than or equal to intraPredModeNum, candIntraPredModeN is set equal to 0 ( Intra_Planar )
Otherwise, candIntraPredModeN is set equal to intraPredModeN