## Slide 1: Non-CE8: Information on CU-based ALF control re-design process
Jaehyun Lim, Seungwook Park
LG Electronics
JCTVC-G146

## Slide 2: Introduction & proposed
ALF filter on/off control in each CU depth
  3 additional re-design loops exist after determining initial ALF on/off map
  The effect of these re-design loop is investigated in terms of performance and complexity (encoding time).
ALF coefficient
Decision
[ ALF encoding process ]
CU-based ALF filter on/off control
re-design loop 2
re-design loop 1
re-design loop 3
Effect of
3 more re-design
process
In
each CU depth?
Initial design loop

## Slide 3: Experimental Results
Results in case of reducing the number of re-design to 2 vs HM4 anchor
Test Case I : re-design loop 2
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.3% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | -0.3% | -0.4%
Class E | 0.0% | 0.0% | 0.0% |  |  |  | 0.1% | 0.2% | 0.6%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 92% |  |  | 98% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 

## Slide 4: Experimental Results
Results in case of reducing the number of re-design to 1 vs HM4 anchor
Test Case II : re-design loop 1
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.1% | -0.1% | -0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | -0.2%
Class C | 0.0% | 0.0% | 0.0% | 0.1% | -0.1% | 0.0% | 0.2% | -0.1% | -0.1%
Class D | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.1% | -0.2% | -0.2%
Class E | 0.0% | 0.0% | 0.0% |  |  |  | 0.3% | 0.3% | 0.6%
Overall | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.2% | 0.0% | 0.0%
Enc Time[%] | 83% |  |  | 96% |  |  | 97% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 

## Slide 5: Experimental Results
Results in case of reducing the number of re-design to 0 vs HM4 anchor
Test Case III : re-design loop 0
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.2% | -0.1% | -0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.2% | -0.1% | -0.1% | 0.4% | -0.3% | -0.3%
Class C | 0.1% | -0.1% | -0.1% | 0.3% | -0.1% | 0.0% | 0.4% | -0.2% | -0.1%
Class D | 0.0% | 0.0% | 0.0% | 0.2% | 0.0% | 0.1% | 0.2% | 0.6% | 0.1%
Class E | 0.0% | 0.0% | 0.0% |  |  |  | 0.9% | 0.2% | 0.3%
Overall | 0.0% | 0.0% | 0.0% | 0.2% | -0.1% | 0.0% | 0.4% | 0.0% | -0.1%
Enc Time[%] | 74% |  |  | 93% |  |  | 95% |  | 
Dec Time[%] | 99% |  |  | 100% |  |  | 101% |  | 

## Slide 6: Experimental Results
Summary
re-design loop | performance |  |  |  |  |  |  |  |  | Enc Time |  | 
 | AIHE |  |  | RAHE |  |  | LBHE |  |  | AIHE | RAHE | LBHE
 | Y | U | V | Y | U | V | Y | U | V |  |  | 
2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 92% | 98% | 99%
1 | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.2% | 0.0% | 0.0% | 83% | 96% | 97%
0 | 0.0% | 0.0% | 0.0% | 0.2% | -0.1% | 0.0% | 0.4% | 0.0% | -0.1% | 74% | 93% | 95%

## Slide 7: Conclusion
The effects by reducing the number of CU-based ALF on/off control re-design are investigated in terms of coding performance and encoding time.
By reducing this number, significant encoding time decrease with marginal loss in coding performance is observed.
Therefore, it is recommended to adopt the proposed reduction of numbers on re-design process.