## Slide 1: Non-CE8: Information on CU-based ALF control re-design process
Jaehyun Lim
LG Electronics
JCTVC-G146

## Slide 2: Introduction & proposed
Line buffer for intra mode
  In current HM 4, 3 more re-design process on CU-based filter ALF on/off
  control decision is performed in each CU depth.
  The effect of this re-design loop is investigated by reducing the number of
  re-design to 0~2 .
Adaptive in-loop
Wiener filtering
[ ALF process ]
CU-based ALF filter on/off control
re-design loop 2
re-design loop 1
re-design loop 3
Effect of
3 more re-design
process
In
each CU depth?

## Slide 3: Experimental Results
Results in case of reducing the number of re-design to 2 vs HM4 anchor
Test Case I : re-design loop 2
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.3% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | -0.3% | -0.4%
Class E | 0.0% | 0.0% | 0.0% |  |  |  | 0.1% | 0.2% | 0.6%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 92% |  |  | 98% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 

## Slide 4: Experimental Results
Results in case of reducing the number of re-design to 1 vs HM4 anchor
Test Case II : re-design loop 1
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.1% | -0.1% | -0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | -0.2%
Class C | 0.0% | 0.0% | 0.0% | 0.1% | -0.1% | 0.0% | 0.2% | -0.1% | -0.1%
Class D | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.1% | -0.2% | -0.2%
Class E | 0.0% | 0.0% | 0.0% |  |  |  | 0.3% | 0.3% | 0.6%
Overall | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.2% | 0.0% | 0.0%
Enc Time[%] | 83% |  |  | 96% |  |  | 97% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 

## Slide 5: Experimental Results
Results in case of reducing the number of re-design to 0 vs HM4 anchor
Test Case III : re-design loop 0
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.2% | -0.1% | -0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.2% | -0.1% | -0.1% | 0.4% | -0.3% | -0.3%
Class C | 0.1% | -0.1% | -0.1% | 0.3% | -0.1% | 0.0% | 0.4% | -0.2% | -0.1%
Class D | 0.0% | 0.0% | 0.0% | 0.2% | 0.0% | 0.1% | 0.2% | 0.6% | 0.1%
Class E | 0.0% | 0.0% | 0.0% |  |  |  | 0.9% | 0.2% | 0.3%
Overall | 0.0% | 0.0% | 0.0% | 0.2% | -0.1% | 0.0% | 0.4% | 0.0% | -0.1%
Enc Time[%] | 74% |  |  | 93% |  |  | 95% |  | 
Dec Time[%] | 99% |  |  | 100% |  |  | 101% |  | 

## Slide 6: Experimental Results
Summary
re-design loop | performance |  |  |  |  |  |  |  |  | Enc Time |  | 
 | AIHE |  |  | RAHE |  |  | LBHE |  |  | AIHE | RAHE | LBHE
 | Y | U | V | Y | U | V | Y | U | V |  |  | 
2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 92% | 98% | 99%
1 | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.2% | 0.0% | 0.0% | 83% | 96% | 97%
0 | 0.0% | 0.0% | 0.0% | 0.2% | -0.1% | 0.0% | 0.4% | 0.0% | -0.1% | 74% | 93% | 95%

## Slide 7: Conclusion
The effects by reducing the number of CU-based ALF on/off control re-design are investigated in terms of coding performance and encoding time.
By reducing this number, significant encoding time decrease with marginal loss in coding performance is observed.
Therefore, it is recommended to adopt the proposed reduction of numbers on re-design process.