## Slide 1: Proposed Error Patterns for JCT-VC JCT-VC G150
Stephan Wenger Vidyo, Inc

## Slide 2: Network Simulation Conditions
G.1050 network simulator
8 active network elements (routers) in path
Traffic injected in several categories
  VoIP (constant low bitrate)
  OTT Video (TCP, high bitrate)
  P2P (TCP, multiple connections, high bitrate)
  HTTP (TCP, variable bitrate)
  All those were live-captured by G.1050 people
Test signal is VBR, 1.5 Mbit/s average, with 1 second bursts up to 2 Mbit/s, captured as an “HD” feed (G.1050 contains a vague description)

## Slide 3: Results
Four error pattern files: 1%, 3%, 5%, and 10% average loss rates
Both bursty and non-bursty loss characteristics
  For example, the 1% loss file contains a long burst of more than 16 packets (with two successfully transmitted packets in the burst) around timestamp 0.93 sec)
Jitter low at low and high loss rates, highly variable at medium loss rates
  Low jitter because queues are mostly empty/full at low/high loss rates
  High jitter, because queues are oscillating
Some pumping observable (indication of insufficient randomization)
Files contain long bursts of unimpaired transmission

## Slide 4: Example: File format
Source:,"TIA TR30.3: TIA-921B"
Creation Date:,10/22/2011
Description:, out/5/HD_vbr
Content-Encoding :, ASCII
Delay Unit:,ms
Time, Delay, Drop
0.000000000,81.918020000,0
0.030424000,79.411300000,0
0.061512000,79.411300000,0
0.077098000,79.411300000,0
0.092701000,79.411300000,0
0.123900000,79.411300000,0
0.139608000,79.411300000,0
0.155107000,79.411300000,0
0.170722000,79.411300000,0
0.186294000,79.411300000,0
0.201897000,79.411300000,0
0.217533000,79.411300000,0

## Slide 5: Example: Statistics