## Slide 1: Test result of low delay tile (JCTVC-G183, m21740)
Copyright 2011 FUJITSU LIMITED
7th JCT-VC meeting, Geneva/Switzerland
2011/11/21-30
K.Kazui, S.Shimada, J.Koyama, and A.Nakagawa
FUJITSU LABORATORIES LTD.
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 2: Summary
Copyright 2011 FUJITSU LIMITED
Test result of low delay tile proposal (JCTVC-E140) is presented.
  The purpose is to provide very low delay functionality with higher picture quality in HEVC , which is requested from major broadcasters (e.g. CBS and ABC, as referred in JCTVC-F147).
Proposed scheme in JCTVC-E140
  Additional low delay mode in which the order of entropy coding is the raster scan within a picture.
    The processing order of entropy coding and source coding can be set differently.
  New syntax for restricting reference across tile boundary in a flexible manner.
    A tile with lower index is treated as “not available”.
Experiment
  Scenario: very low delay coding using vertical intra line refresh
  Coding gain of the proposed scheme over two existing schemes are measured.
  Software is implemented onto HM-4.0-dev-tiles-wpp (v1418)
Result
  Improvement of BD-Rate from -4.6% to -5.8% in low delay configurations.
  We would like to thank Sharp for cross-checking (JCTVC-G968).
We suggest to promote the proposed scheme to WD.
<number>
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 3: Background (1/3)
Very low delay coding with high picture quality
  Request from industries such as broadcasting (JCTVC-E147)
Vertical intra line refresh
  One type of gradual decoding refresh schemes
  Coding delay due to the bitstream buffer can be reduced to 1 Treeblock line time.
  Proper control for guaranteeing correct reconstruction within one refresh cycle is necessary. (Similar discussion is found in JCTVC-G317 (Qualcomm))
    The control should prevent contamination of refreshed pixels from non-refreshed pixels.
Copyright 2011 FUJITSU LIMITED
Vertical intra line refresh
<number>

## Slide 4: Background (2/3)
Degradation occurs when vertical intra line refresh is applied to HEVC.
  Slice insertion in each treeblock line for disabling in-loop filtering at the area boundary leads to significant coding loss. (JCTVC-C021)
  If in-loop filtering remains enabled at the boundary, significant degradation occurs long after 1 refresh cycle. (JCTVC-E061)
We have proposed high-level syntax/semantics for this problem. (JCTVC-B031, JCTVC-C021, JCTVC-D053)
  Picture partitioning in source coding
  (Asymmetric) restriction on reference among partitions
Copyright 2011 FUJITSU LIMITED
Conventional scheme
(Multiple slices insertion)
Degradation caused by in-loop filtering at area boundary
(JCTVC-E061)
Proposed high-level syntax/semantics in JCTVC-B031
<number>

## Slide 5: Background (3/3)
The tile scheme realizes sub-picture partitioning.
However, high-quality and very low delay cannot co-exists with tile in WD4.
  The order of entropy coding is the raster scan within a tile. Delay of 1-picture duration is inevitable when vertical tiles are inserted.
  If tiles are inserted in each treeblock rows, loss in coding efficiency occurs.
JCTVC-F140 proposes additional mode in which the order of entropy coding is the raster-scan within a picture.
Test result of the proposed scheme is shown in this contribution.
Copyright 2011 FUJITSU LIMITED
Entropy coding order of WD4 tile
Low delay coding with WD4 tile
Proposed Low delay tile in JCTVC-F140
<number>

## Slide 6: Experiment
Scenario
  Very low delay coding using vertical intra line refresh scheme
  refresh_cycle = Ceil( picture_width / LCU_width )
    Shifting speed of the vertical intra line is LCU_width per picture.
Comparison
  WD4 tile based scheme (Ref_1)
  The scheme without tile (Ref_2)
Software: implemented onto HM-4.0-dev-tiles-wpp (v1418)
Copyright 2011 FUJITSU LIMITED
Ref_1 WD4 tile based scheme
Ref_2 Scheme without tile
Vertical intra line is partially overlapped among pictures
<number>

## Slide 7: Detail of proposed scheme
Source coding
  restriction of reference at the tile boundary.
    Pixel reference for intra prediction and for in-loop filtering
    MV reference for MV prediction
    A tile boundary is treated as a picture boundary for in-loop filtering.
Entropy coding
  The processing order is changed to the raster-scan within a picture.
  No reset, no restriction of context reference at the tile boundary.
    Unlike source coding, entropy coding is completely independent to other pictures.
Copyright 2011 FUJITSU LIMITED
Proposed scheme
<number>

## Slide 8: Implementation note
WD4 tile based scheme (Ref_1)
  Symmetrical restriction of reference at all tile boundaries regardless the presence of slice boundary.
    HM4 tile does not support restriction of reference for ALF and SAO.
The scheme without tile (Ref_2)
  The mode of intra prediction for a PU inside the vertical intra line is restricted so that non-refreshed pixels are referred in intra prediction.
Common features among the proposed scheme and compared schemes.
  Insertion of the vertical intra line in a picture
  Restriction of the search range in ME (Encoder-only)
  Temporal MVP is not used at a recovery point.
    Provisional use of the flag corresponding to mv_competition_temporal_flag (JCTVC-F427, Sony)
Copyright 2011 FUJITSU LIMITED
<number>

## Slide 9: Result
Copyright 2011 FUJITSU LIMITED
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -3.2% | -4.9% | -3.9% | -3.3% | -4.5% | -3.5%
Class C | -4.6% | -5.4% | -5.5% | -4.7% | -5.2% | -5.1%
Class D | -6.5% | -7.5% | -7.4% | -6.6% | -7.4% | -7.2%
Class E | -8.0% | -9.9% | -9.2% | -8.6% | -9.3% | -8.9%
Overall | -5.3% | -6.6% | -6.2% | -5.5% | -6.3% | -5.8%
 | -5.3% | -6.6% | -6.2% | -5.5% | -6.3% | -5.8%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -5.9% | -9.3% | -7.8% | -4.5% | -5.7% | -5.1%
Class C | -4.7% | -8.3% | -8.9% | -4.0% | -5.5% | -5.6%
Class D | -3.3% | -6.6% | -6.8% | -2.9% | -3.7% | -3.8%
Class E | -10.4% | -16.1% | -15.6% | -7.5% | -11.3% | -10.1%
Overall | -5.8% | -9.6% | -9.3% | -4.6% | -6.2% | -5.8%
 | -5.8% | -9.7% | -9.3% | -4.6% | -6.2% | -5.8%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 95% |  |  | 92% |  | 
Proposal vs. WD4 Tile (Ref_1)
Proposal vs. w/o Tile (Ref_2)
<number>

## Slide 10: Conclusion
Proposed low delay tile scheme is implemented onto HM4 and tested.
  Cross-checked by Sharp
BD-Rate reduction of -4.6%～-5.8% is achieved in the very low delay scenario.
We suggest to adopt the additional mode in which the order of entropy coding is the raster scan within a picture into WD.
  The proposed scheme enables that source coding and entropy coding have different setting of the processing order and restriction at tile boundary.
Copyright 2011 FUJITSU LIMITED
<number>

## Slide 11
<number>
Copyright 2010 FUJITSU LIMITED