## Slide 1: Enhancement on operation of coded picture buffer (JCTVC-G188, m21745)
Copyright 2011 FUJITSU LIMITED
7th JCT-VC meeting, Geneva/Switzerland
2011/11/21-30
K.Kazui, S.Shimada, J.Koyama and A.Nakagawa
FUJITSU LABORATORIES LTD.
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 2: Summary
Copyright 2011 FUJITSU LIMITED
We propose again new operation of CPB (coded picture buffer) in order to realize interoperable very low delay coding less than 1 frame period.
  Former proposals in JCTVC-C021 and JCTVC-D053
We request to start discussion on HRD specification in HEVC.
<number>
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 3: Background
Interoperable very low delay coding less than 1 frame period
  Request from broadcasting industry (JCTVC-F147)
Enhancement of HRD specification is necessary
  HRD in AVC only specifies the removal time of a picture. Minimum delay exceeds 1 picture period.
  AVC-based video transmission apparatus in the market utilize vendors’ proprietary protocols so that the encoder and the decoder work jointly for lowering codec delay.
  No interoperability in AVC-based apparatus
We have proposed the enhancement of CPB operation.
  JCTVC-C021, JCTVC-D053
  Summarized in this presentation
We should accelerate the discussion on HRD for the publish of CD at 2012/02 meeting.
Copyright 2011 FUJITSU LIMITED
<number>

## Slide 4: Problem in AVC’s HRD specification
Removal time of each picture is defined.
Coding delay exceeds 1 frame period.
  In the worst case, the last bit of the first treeblock arrives at the removal time of the picture.
  In the real world, a decoder decodes a picture within dt (~= 1 frame period).
  Display timing should be delayed dt .
Copyright 2011 FUJITSU LIMITED
Buffer model in AVC
<number>

## Slide 5: Proposal
A picture is conceptually divided into M groups of treeblocks.
  Each group contains equal number of treeblocks.
  Example：1 Treeblock line
  The variable M is signaled in Buffering period SEI.
  Amount of bits of each group can be averaged by existing schemes such as the vertical intra line refresh schemes.
tr( n, i ): removal time of i-th group in picture n.
  tr( n, i ) = tr ( n - 1 ) + ( tr ( n ) - tr ( n - 1 ) ) * i / M
Copyright 2011 FUJITSU LIMITED
New buffer model
Decoding delay can be reduced to 1ms.
1920x1080/60Hz
1 group per 1 treeblock line
<number>

## Slide 6: Detail
Syntax and semantics
  num_groups_in_picture_minus1 in Buffering period SEI message
  (PicWidthInLCUs * PicHeightInLCUs)%(num_groups_in_picture_minus1 + 1) = 0
Definition of last bit of coded group of treeblocks
  The last bit of a coded group of treeblock is explicitly specified.
  CABAC case:
  When bin X, which corresponds to the last end_of_slice_flag in the coded group of treeblocks, is reconstructed through the arithmetic decoding process of bit A in a bitstream, then bit A is the last bit in a bitstream.
Copyright 2011 FUJITSU LIMITED
<number>

## Slide 7: Conclusion
We propose again new operation of CPB (coded picture buffer) in order to realize interoperable very low delay coding less than 1 frame period.
We request to start discussion on HRD specification in HEVC.
Copyright 2011 FUJITSU LIMITED
<number>

## Slide 8
<number>
Copyright 2010 FUJITSU LIMITED