## Slide 1
Modification of derivation process of motion vector information for interlace format (JCTVC-G196, m21753)
J.Koyama, A. Yamori, K.Kazui, S.Shimada and A.Nakagawa
FUJITSU LABORATORIES LTD.
Copyright 2011 FUJITSU LIMITED
Notes: I’m …
I’d like to talk about …
<number>

## Slide 2: Summary
Two inconsistencies exist between the current derivation process of MV information and the nature of interlace format
Adjustments of vertical component according to field parity
  Chroma MV for 4:2:0 (same as in AVC)
  MV predictor
Shifting only. No syntax change.
BD-PSNR for chroma is drastically improved by chroma MV adjustment
  0.48 dB (RA_HE) to 0.23 dB (LB_LC)
  Up to +1 dB for “Mobile and calendar”
BD-Rate for luma is improved by MV predictor adjustment
  0.8 % (RA_HE, RA_LC) to 2.0 % (LD_LC)
We propose to consider dealing with interlace format in HEVC and discuss in JCT-VC meetings.
Improved RD-curve of chroma
by chroma MV adjustment
<number>
Notes: We point out there are two consistencies between the current derivation process of MV information and the nature of interlace format.
# nature of interlace format is disparity in vertical direction between top field and bottom field.
Proposed modification adjusts of vertical component in chroma motion vector in 4:2:0 sequences and motion vector predictor in Merge and AMVP mode.
The proposed modification applies shifting only without syntax change.
We see 0.48 to 0.23 dB coding gain performance by modification on chroma MV modification and UP to 1dB gain for particular sequence, like this ->
And we also see 0.8 to 2.0 % gain by motion vector predictor.
<number>

## Slide 3: Introduction
Industry’s need
  M21411 “Joint proposal of HEVC requirements on the support of interlace format” advocates the importance of interlace support
  M21411 also states interlace support shall not delay the schedule
Problem in supporting interlace
  Two Inconsistencies exist between the current derivation process of MV information and the nature of interlace format.
    Derivation of chroma MV
    Derivation of MV predictor
We introduce modifications to remove the inconsistencies
  Possible with small changes in the derivation process of MV information
  Significant improvement in coding efficiency
  No danger to delay the schedule
<number>
Notes:   As mentioned in M21411, there are strong industry’s need for supporting interlaced format. And it also says that adoption for interlaced format shall not delay the schedule.
  We point out that two inconsistencies exist between the current HM design and the nature of interlace format
  First one is derivation of chroma MV, the other is derivation of MV predictor.
  We propose to remove the inconsistencies for support interlaced format.
  It is realized with small changes, and achieves significant performance, and there is no danger to delay the hevc schedule, I believe.
  ここでProposeなのかがいまいち…、だってInterlaceはまだやると決まっていない
  段階を踏んでいない、Inconsistencyの紹介にとどめるべきでは？
<number>

## Slide 4: Inconsistency on chroma MV in 4:2:0
Top
Top
Bottom
Bottom
Luma
Chroma
Correct position
mvLX[ 1 ]= 1.0
mvCLX[ 1 ]= 1.0
(in units
of chroma line)
Derived chroma MV does not point to the correct position
Y
<number>
Notes: This figure shows the inconsistency on chroma MV in 4:2:0 sources.
In case that luma vector indicates top field to bottom field, using the same vector value for chroma, chroma vector doesn’t indicate correct position.
<number>

## Slide 5: Proposed modification on chroma MV derivation
Top
Top
Bottom
Bottom
Luma
Chroma
Y
Correct position
mvLX[ 1 ]= 1.0
shift
The same chroma MV adjustment of AVC
mvCLX[ 1 ] −= 2 ( from top to bottom )
mvCLX[ 1 ] += 2 ( from bottom to top )
in units of 1/8 chroma line
mvCLX[ 1 ]= 0.75
(in units of chroma line)
<number>
Notes: So, shift chroma vector to be parallel to luma motion vector, to indicate correct position, same as AVC. Equations are showed here.
もうちょっといい説明を
<number>

## Slide 6: Inconsistency on MV prediction
y
Luma
Top
Bottom
Top
Bottom
mvCol[ 1 ] = −1.0
mvLXCol[ 1 ] = −1/3
CREF
Ref-pic of mvCol
Correct position
Derived MV predictor does not point to the correct position
PREF
Ref-pic
PORG
Curr-pic
CORG
Org-pic of mvCol
<number>
Notes: In case of derivation of MV predictor, it has the same kind of inconsistency.
If motion mvCol indicates from bottom field to top field, derived motion vector predictor, mvLXCol indicates the wrong position.
<number>

## Slide 7: Proposed modification on MV prediction
mvLXCol[ 1 ] = −1.0
[Shift 1] mvCol[ 1 ] += 2 * ( parity(CREF) − parity(CORG) )
mvCol => <scaling> => mvLXCol
[Shift 2] mvLXCol[ 1 ] += 2*(parity(PORG) − parity(PREF) )
y
Luma
mvCol[ 1 ] = −1.0
mvLXCol[ 1 ] = −0.5
CREF
Ref-pic of mvCol
PREF
Ref-pic
PORG
Curr-pic
CORG
Org-pic of mvCol
shift2
shift1
mvCol[ 1 ] = −1.5
Note: This modification is applicable to both spatial MVP candidates and temporal MVP candidates
<number>
Notes: So, to correct motion vector, shifting processes are done.
First, shift 1, shift the mvCol to convert the vector value based on Bottom field.
Second, scale the vector, same as HEVC
Finally, shift 2, shift the mvLXCol to convert the value based on top field.
The processes make the motion vector predictor is parallel to mvCol.
もうちょっといい話し方を
<number>

## Slide 8: Experiment
Two experiments
  Experiment 1: Only chroma motion vector modification
  Experiment 2: Both chroma motion vector and motion vector predictor modifications
Test sequences (interlace, 4:2:0/8-bit)
  4 HD sequences and 4 SD sequences in ITU-R BT.1120.
    HD: "Walk through the square", "Church", "Whale show" and "Marching"
    SD: "Flower garden", "Table tennis“, "Mobile and calendar" and "Football"
Software
  Implemented onto HM-4.0 software
    One field picture is considered as one frame
    An interlaced sequence is encoded with the half height and the doubled frame rate of the original interlaced sequence.
    A field parity is automatically derived by POC, an even POC number represents a top field and an odd POC number represents a bottom field
<number>
Notes: Experimental condition
Test sequences are 4:2:0/8-bit sequences (in itu-r BT.1120) showed here.
And software, the proposed modifications are implemented on HM-4.0.
One field picture is considered as one frame,
So an interlaced sequences are encoded with the half height and the doubled frame rate of the original seq.
And even POC number represent a top field, and odd POC number represent a bottom field.
<number>

## Slide 9: Results on experiment 1 (chroma motion vector modification vs HM-4.0)
Random Access HE |  | BD-PSNR (dB) |  | 
 |  | Y | U | V
1920x1080 | Church | 0.00 | 0.09 | 0.06
 | Marching | 0.00 | 0.33 | 0.52
 | Walk | 0.00 | 0.46 | 0.48
 | WhaleShow | 0.00 | 0.23 | 0.29
832x480 | Flower | 0.02 | 1.01 | 0.38
 | Football | 0.00 | 0.38 | 0.18
 | Mobile | 0.06 | 1.05 | 1.16
 | TableTennis | −0.01 | 0.24 | 0.35
Overall 1920x1080 |  | 0.00 | 0.28 | 0.34
Overall 832x480 |  | 0.02 | 0.67 | 0.52
Overall |  | 0.01 | 0.48 | 0.43
Results of BD-PSNR comparing Proposal to HM4.0
  Average coding gain in Chroma U is 0.48dB (RA_HE) 0.43dB (RA_LC) 0.27dB (LD_HE) 0.23dB (LD_LC) (see attached excel sheet for details)
  Up to 1dB coding gain in chroma components on RA_HE condition
    “Flower garden”
    “Mobile and calendar”
Data is shown in BD-PSNR
since evaluation of chroma performance in
BD-bitrate may cause misleading
<number>
Notes: This is the result obtained by chroma modification.
Average coding gains are from 0.48 to 0.23 dB.
And in some sequences, up to 1 dB coding gain is achieved in chroma components.
<number>

## Slide 10: RD-Curve of experiment 1 (chroma motion vector modification vs HM-4.0)
RD-curve
RD-curve of chroma U component
Reference: HM-4.0, Tested: chroma MV modification
(class C sequence “Mobile and calendar”, RA_HE condition)
<number>
Notes: This figure is the rd-curve of the chroma U compoment in mobile and calendar in RA_HE condition.
<number>

## Slide 11: Results on experiment 2 (chroma MV and MV predictor modification vs chroma MV modification only)
BD-Bitrate (%) performance of chroma MV and MV predictor modification compared to chroma MV modification only
  Average coding gains in Luma are 0.8% (RA_HE), 0.8% (RA_LC), 1.8% (LB_HE), 2.0% (LB_LC)
  3.7% coding gain in luma component of the class C sequence “Football” on LB_LC condition
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class B | −0.6 | −0.1 | −0.2 | −0.6 | −0.1 | −0.2
Class C | −1.0 | −0.7 | −0.6 | −1.0 | −0.6 | −0.7
Overall | −0.8 | −0.4 | −0.4 | −0.8 | −0.4 | −0.5
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class B | −1.6 | −1.0 | −1.3 | −2.0 | −0.7 | −1.0
Class C | −1.9 | −1.2 | −1.2 | −2.0 | −1.0 | −1.3
Overall | −1.8 | −1.1 | −1.2 | −2.0 | −0.9 | −1.2
<number>
Notes: This is the result obtained by chroma modification and mvp modification compared to chroma modification.
Average coding gain is from 0.8% to 2.0%
3.7 % coding gain is achieved in luma component of class C seq. football on LB_LC condition.
<number>

## Slide 12: Conclusion
Two inconsistencies between WD4 and the nature of interlace format are removed by simple modifications
  Adjustment of chroma MV same as in AVC
  Adjustment of MV predictor for AMVP/Merge/Skip
Significant improvement of coding efficiency
  On average 0.23 dB (LB_LC) to 0.48 dB (RA_HE), up to +1 dB for “Mobile and calendar” in chroma component by chroma MV adjustment
  On average −0.8 % (RA_HE, RA_LC) to −2.0 % (LB_LC), up to 3.7% for “Football” in luma component by MV predictor adjustment
We support the contribution JCTVC-G912 mentioning the adjustment of interlace format in HEVC and request to establish an AHG with mandates of
  Collecting interlace sequences for further evaluation
  Analyzing proposed schemes related to interlace support at this meeting
<number>
Notes: Conclusion.
We fix the two inconsistencies between WD4 and the nature of interlaced format.
One is on chroma MV, the other is on MV predictor.
And we achieve significant coding gains.
We request to an AHG and discuss interlaced sequences for further evaluation
And analyzing proposed scheme related to interlaced support.
蝶野さんのドキュメントサポート、とする方が、足並みそろえている感じがするのでは？
<number>