## Slide 1
CE11 Report on Mode Dependent Coefficient Scanning for Inter Coding
Jin Song, Xiaozhen Zheng, Haitao Yang ,
Haoping Yu

## Slide 2: Background
A prediction unit dependent coefficient scanning order selection scheme (PDCS) for inter coding is proposed in the last meeting.
NSQT for inter coding was added into HM4.0
The harmonization of PDCS and NSQT is tested in CE11, and is reported in this document

## Slide 3: Proposal Scheme
The relationship among PU partition, TU partition and scanning pattern
 | 2NxN PU | 2NxnU PU | 2NxnD PU | Nx2N PU | nLx2N PU | nRx2N PU | 2Nx2N PU | NxN PU
Non-square TU | Vertical scan (TU is horizontal stripe) |  |  | Horizontal scan (TU is vertical stripe) |  |  | N/A | 
Square TU | Zig-zag scan |  |  |  |  |  |  | 

## Slide 4: Proposal Scheme
The proposed method is
  Horizontal scan for the “vertical stripe” TU
  Vertical scan for the “horizontal stripe” TU

## Slide 5: Simulations & Results
 | Random Access LC |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.2% | 0.2% |  |  | 
Class B | -0.1% | -0.5% | -0.3% | -0.1% | -0.7% | -0.5%
Class C | 0.0% | -0.2% | -0.1% | 0.0% | -0.3% | -0.5%
Class D | 0.0% | -0.2% | -0.1% | -0.1% | -0.2% | -0.3%
Class E |  |  |  | -0.3% | -0.1% | -0.2%
Overall | 0.0% | -0.2% | -0.1% | -0.1% | -0.4% | -0.4%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
Thanks Samsung for the crosschecking efforts

## Slide 6: WD modifications
Inverse scanning process The variable scanIdx, indicating wich scan is used to scan the transform coefficients (zigzag, horizontal or vertical), is derived as follows.
  If PredMode is equal to MODE_INTRA, the following applies.
    If cIdx is equal to 0, scanIdx is set to ScanType[ Log2( nS >> 2 ) ][ IntraPredMode ].
    Otherwise (cIdx is equal to 1 or 2), scanIdx is set to ScanType[ Log2( nS >> 2 ) ][ IntraPredModeC ]
  Otherwise (PredMode is not equal to MODE_INTRA), when nW is equal to nH, scanIdx is set to 0,when nW is larger than nH, scanIdx is set to 2,else scanIdx is set to 1.

## Slide 7: Conclusions
Mode dependent coefficient scanning method for inter coding is proposed in this contribution.
It is harmonized with NSQT
Coding gain, no complexity
We recommend adopting this method in next version of HEVC Test Model.

## Slide 8
Thank You
www.huawei.com