## Slide 1: Progressive Motion Vector Resolution (PMVR)
Jicheng An, Xiang Li, Xun Guo and Shawmin Lei
JCTVC-G277
Copyright © MediaTek Inc. All rights reserved.
Presented by X. Li
7th JCT-VC Meeting in Geneva
21-30, Nov., 2011
Notes: <number>

## Slide 2: Overall Summary
Use the higher MV resolution when MV is close to MVP and lower MV resolution when MV is far away from MVP.
  Variant A: PMVR w/o 1/8-pixel
    Highest MV resolution is 1/4-pixel, lowest is 1/2-pixel
  Variant B: PMVR with 1/8-pixel
    Highest MV resolution is 1/8-pixel, lowest is 1/2-pixel
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 3: PMVR without 1/8-pixel
Simplification for HM4.0
Both BD-rate gain and complexity reduction can be achieved.
Set TH=2 for B slice and TH=4 for P slice in SPS
Suggested to be adopted by HEVC.
Copyright © MediaTek Inc. All rights reserved.
<number>
 | RA and LB config. | LP config.
BD-rate gain | 0.20% | 0.05%
Enc. time reduction | 9% | 4%
Dec. Interpolation counts reduction | 5~8% | 4%
Dec. Memory access reduction | 3~4% | 2%
Dec. Memory bandwidth reduction | 1% | 1%

## Slide 4: PMVR with 1/8-pixel
Add1/8-pixel interpolation filters
Larger gain for LP configurations. (2.6% BD-rate gain)
Complexity reduction or increase for different configurations.
Set THq=4, THe=0 for B slice and THq=4, THe=2 for P slice in SPS.
Suggested to be tested in CE.
Copyright © MediaTek Inc. All rights reserved.
<number>
 | RA config. | LB config. | LP config.
BD-rate gain | 0.55% | 0.35% | 2.58%
Enc. time | -7% | -8% | 6~7%
Dec. Interpolation counts | 8% | -3% | 9~10%
Dec. Memory access | 4% | -1% | 3%
Dec. Memory bandwidth | 2~3% | 0% | 0~1%

## Slide 5
Copyright © MediaTek Inc. All rights reserved.
Thank you
Notes: <number>

## Slide 6: Threshold transmission
Set TH=2 for B slice and TH=4 for P slice as default.
In order to enable more flexibility, send the TH index for B and P slice respectively in SPS from the four candidates shown in this table.
  TH=+∞: uniform 1/4-pixel resolution same as HM4.0
  TH=0: 1/4-pixel resolution for merge/skip modes and 1/2-pixel resolution for other inter modes.
Copyright © MediaTek Inc. All rights reserved.
<number>
TH index | TH
0 | 0
1 | 2
2 | 4
3 | +∞

## Slide 7: Threshold transmission
Set (THq, THe)=(4, 0) for B slices and (4, 2) for P slices as default.
In order to enable more flexibility, send the TH pair (THq, THe) index for B and P slice respectively in SPS from the four candidates shown in this table.
  (THq, THe)=(+∞, +∞): 1/8-pixel MV resolution is always used.
  (THq, THe)=(0, 0): 1/8-pixel resolution is used for skip/merge and 1/2-pixel resolution is used for other inter modes.
Copyright © MediaTek Inc. All rights reserved.
<number>
TH pair index | (THq, THe)
0 | (0, 0)
1 | (4, 0)
2 | (4, 2)
3 | (+∞, +∞)

## Slide 8: Outline
PMVR without 1/8-pixel MV resolution
  Limited 1/4-pixel MV positions
  Modification of MVD derivation
  Experimental Results
  Threshold transmission
PMVR with 1/8-pixel MV resolution
  1/8-pixel interpolation filters
  Limited 1/4-pixel and 1/8-pixel MV positions
  Modification of MVD derivation
  Experimental Results
  Threshold transmission
Conclusions
Copyright © MediaTek Inc. All rights reserved.
<number>
Notes: <number>

## Slide 9: Outline
PMVR without 1/8-pixel MV resolution
  Limited 1/4-pixel MV positions
  Modification of MVD derivation
  Experimental Results
  Threshold transmission
PMVR with 1/8-pixel MV resolution
  1/8-pixel interpolation filters
  Limited 1/4-pixel and 1/8-pixel MV positions
  Modification of MVD derivation
  Experimental Results
  Threshold transmission
Conclusions
Copyright © MediaTek Inc. All rights reserved.
<number>
Notes: <number>

## Slide 10: Limited 1/4-pixel MV positions (1/2)
Limited 1/4-pixel MV positions (the red square around CTR):
  MV_x ∈ [CTR_x-TH, CTR_x+TH]
  MV_y ∈ [CTR_y-TH, CTR_y+TH]
CTR is derived as:
  CTR_x = MVP_x>>1<<1;
  CTR_y = MVP_y>>1<<1;
When MVP is in half or integer pixel position, MVP and CTR coincide as shown in this figure.
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 11: Limited 1/4-pixel MV positions (2/2)
Benefits
  Simplified Motion Estimation
    1/4-pixel MV positions out of range don’t need to be searched.
  Reduced interpolation operations
    Reduced interpolation counts (Mult and Adds)
    Reduced memory access
  Reduced MVD coding bits->BD-rate gain
    Since not all the 1/4 pixel MV positions are needed  more efficient MVD derivation.
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 12: MVD derivation
Given MVP and MV, the MVD is derived as follows
  If |MV_x-CTR_x| >TH
    MVD_x = (MV_x + CTR_x + sign(MV_x-CTR_x)*TH) /2 – MVP_x
    MVD_y = (MV_y – CTR_y) / 2
  Elseif |MV_y-CTR_y| >TH
    MVD_x = (MV_x – CTR_x) / 2
    MVD_y = (MV_y + CTR_y + sign(MV_y-CTR_y)*TH) /2 – MVP_y
  Else // same as HM4.0
    MVD_x = MV_x – MVP_x
    MVD_y = MV_y – MVP_y
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 13: Examples of MVD derivation
The MVD values of position A, B, and C are shown as follows:
In HM4.0:
  A: (2, 0)
  B: (4, -2)
  C: (4, -4)
In PMVR:
  A: (2, 0)
  B: (3, -1)
  C: (3, -2)
In PMVR, the MVD coding bits are reduced.
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 14: RA and LB Performance when TH=2
Copyright © MediaTek Inc. All rights reserved.
<number>
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.4% | -1.1% | -1.0% | -0.4% | -0.8% | -0.7%
Class B | -0.2% | -0.5% | -0.4% | -0.3% | -0.5% | -0.3%
Class C | -0.2% | -0.6% | -0.6% | -0.3% | -0.4% | -0.5%
Class D | 0.0% | -0.5% | -0.4% | -0.1% | -0.3% | -0.3%
Class E |  |  |  |  |  | 
Overall | -0.2% | -0.7% | -0.6% | -0.3% | -0.5% | -0.4%
 | -0.2% | -0.6% | -0.6% | -0.3% | -0.5% | -0.4%
Enc Time[%] | 92% |  |  | 91% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Mult[%] | -5% |  |  | -5% |  | 
Adds[%] | -5% |  |  | -5% |  | 
Access[%] | -3% |  |  | -3% |  | 
MemBand(2D) Ave.[%] | -1% |  |  | -1% |  | 
MemBand(2D) Max.[%] | 4% |  |  | 7% |  | 
MemBand(1D) Ave.[%] | -1% |  |  | -1% |  | 
MemBand(1D) Max.[%] | 5% |  |  | 7% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.2% | -0.4% | -0.4% | -0.2% | -0.1% | -0.1%
Class C | -0.2% | -0.3% | -0.4% | -0.3% | -0.1% | -0.4%
Class D | 0.0% | -0.1% | -0.5% | 0.0% | -0.1% | 0.0%
Class E | -0.2% | -0.3% | 0.4% | -0.2% | 0.7% | 0.2%
Overall | -0.1% | -0.3% | -0.3% | -0.2% | 0.1% | -0.1%
 | -0.1% | -0.3% | -0.3% | -0.2% | 0.0% | -0.1%
Enc Time[%] | 90% |  |  | 89% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Mult[%] | -7% |  |  | -8% |  | 
Adds[%] | -7% |  |  | -8% |  | 
Access[%] | -4% |  |  | -4% |  | 
MemBand(2D) Ave.[%] | -1% |  |  | -1% |  | 
MemBand(2D) Max.[%] | 5% |  |  | 5% |  | 
MemBand(1D) Ave.[%] | -1% |  |  | -1% |  | 
MemBand(1D) Max.[%] | 4% |  |  | 5% |  | 
BD-rate gain
  0.2% BD-rate gain.
Complexity reduction
  9% encoding time reduction
  5%~8% interpolation counts reduction.
  3%~4% memory access reduction.
  1% memory bandwidth reduction.

## Slide 15: LP Performance when TH=4
Copyright © MediaTek Inc. All rights reserved.
<number>
BD-rate gain
  0.05% BD-rate gain.
Complexity reduction
  4% encoding time reduction
  4% interpolation counts reduction.
  2% memory access reduction.
  1% memory bandwidth reduction.
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | -0.2% | -0.4% | -0.1% | -0.1% | 0.0%
Class C | -0.1% | -0.2% | -0.3% | -0.1% | -0.2% | -0.2%
Class D | 0.0% | -0.5% | -0.4% | 0.0% | -0.2% | -0.4%
Class E | 0.0% | 0.4% | -0.1% | 0.0% | -0.2% | -1.1%
Overall | -0.1% | -0.2% | -0.3% | 0.0% | -0.2% | -0.3%
 | 0.0% | -0.2% | -0.3% | 0.0% | -0.2% | -0.4%
Enc Time[%] | 96% |  |  | 96% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
Mult[%] | -4% |  |  | -4% |  | 
Adds[%] | -4% |  |  | -4% |  | 
Access[%] | -2% |  |  | -2% |  | 
MemBand(2D) Ave.[%] | -1% |  |  | -1% |  | 
MemBand(2D) Max.[%] | 2% |  |  | 6% |  | 
MemBand(1D) Ave.[%] | -1% |  |  | -1% |  | 
MemBand(1D) Max.[%] | 2% |  |  | 7% |  | 

## Slide 16: Outline
PMVR without 1/8-pixel MV resolution
  Limited 1/4-pixel MV positions
  Modification of MVD derivation
  Experimental Results
  Threshold transmission
PMVR with 1/8-pixel MV resolution
  1/8-pixel interpolation filters
  Limited 1/4-pixel and 1/8-pixel MV positions
  Modification of MVD derivation
  Experimental Results
  Threshold transmission
Conclusions
Copyright © MediaTek Inc. All rights reserved.
<number>
Notes: <number>

## Slide 17: Interpolation for 1/8-pixel resolution
8-tap 6-bit DCT-IF for 1/8-pixel luma interpolation
4-tap 6-bit DCT-IF for 1/16-pixel chroma interpolation
Copyright © MediaTek Inc. All rights reserved.
<number>
Position | Filter Coefficients |  |  |  |  |  |  | 
1/8 | {-1, | 3, | -6, | 62, | 9, | -4, | 2, | -1}
3/8 | {-2, | 5, | -12, | 50, | 30, | -10, | 4, | -1}
Position | Filter Coefficients |  |  | 
1/16 | {-2, | 63, | 4 | -1}
3/16 | {-5, | 59, | 13 | -3}
5/16 | {-6, | 52, | 23, | -5}
7/16 | {-7, | 43, | 34, | -6}

## Slide 18: Limited 1/4- and 1/8-pixel MV positions
Limited 1/4-pixel MV positions:
  MV_x/y ∈ [CTRq_x/y - THq, CTRq_x/y + THq]
Limited 1/8-pixel MV positions:
  MV_x/y ∈ [CTRe_x/y - THe, CTRe_x/y + THe]
CTRe is derived as
  CTRe_x/y = MVP_x/y>>1<<1
CTRq is derived as
  CTRq_x/y = (MVP_x/y+1)>>2<<2
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 19: MVD derivation
  Given MVP and MV, the MVD is derived as follows
    If |MV_x-CTRq_x| >THq
      S = sign(MV_x-CTRq_x)
      MVD_x = (MV_x + 2(CTRe_x+S*THe) + CTRq_x + S*THq)/4 - MVP_x
      MVD_y = (MV_y – CTRq_y)/4
    Elseif |MV_y-CTRq_y| >THq
      S = sign(MV_y-CTRq_y)
      MVD_x = (MV_x – CTRq_x)/4
      MVD_y = (MV_y + 2(CTRe_y+S*THe) + CTRq_y + S*THq)/4 – MVP_y
    Elseif |MV_x-CTRe_x| > THe
      MVD_x = (MV_x + CTRe_x + sign(MV_x-CTRe_x)*THe)/2 – MVP_x
      MVD_y = (MV_y – CTRe_y)/2
    Elseif |MV_y-CTRe_y| > THe
      MVD_x = (MV_x – CTRe_x)/2
      MVD_y = (MV_y + CTRe_y + sign(MV_y-CTRe_y)*THe)/2 – MVP_y
    Else
      MVD_x = MV_x – MVP_x
      MVD_y = MV_y – MVP_y
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 20: Examples of MVD derivation
The MVD values of position A, B, and C are shown as follows:
In uniform 1/8-pixel resolution:
  A: (1, 0)
  B: (3, -2)
  C: (7, -6)
In PMVR:
  A: (1, 0)
  B: (2, -1)
  C: (3, -2)
In PMVR, the MVD coding bits are reduced.
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 21: RA and LB performance, THq=4, THe=0
R-D performance
  0.55% gain for RA
  0.35% gain for LD
Complexity
  Enc. time
    8% reduction
  Interpolation counts
    8% increase for RA
    3% reduction for LD
  Memory access
    4% increase for RA
    1% reduction for LD
  Memory bandwidth
    2～3% increase for RA
Copyright © MediaTek Inc. All rights reserved.
<number>
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.4% | -1.2% | -1.1% | -0.6% | -0.9% | -0.9%
Class B | -0.3% | -0.7% | -0.6% | -0.6% | -0.9% | -0.8%
Class C | -0.5% | -0.8% | -0.8% | -0.7% | -1.2% | -1.2%
Class D | -0.5% | -0.9% | -0.9% | -0.9% | -1.5% | -1.6%
Class E |  |  |  |  |  | 
Overall | -0.4% | -0.9% | -0.8% | -0.7% | -1.1% | -1.1%
 | -0.4% | -0.9% | -0.8% | -0.7% | -1.1% | -1.1%
Enc Time[%] | 93% |  |  | 92% |  | 
Dec Time[%] | 102% |  |  | 103% |  | 
Mult[%] | 8% |  |  | 8% |  | 
Adds[%] | 8% |  |  | 8% |  | 
Access[%] | 4% |  |  | 4% |  | 
MemBand(2D) Ave.[%] | 2% |  |  | 3% |  | 
MemBand(2D) Max.[%] | 10% |  |  | 11% |  | 
MemBand(1D) Ave.[%] | 2% |  |  | 2% |  | 
MemBand(1D) Max.[%] | 9% |  |  | 9% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.2% | -0.5% | -0.8% | -0.3% | -0.6% | -0.3%
Class C | -0.4% | -0.8% | -0.7% | -0.5% | -0.5% | -0.8%
Class D | -0.4% | -1.1% | -1.3% | -0.5% | -0.9% | -1.3%
Class E | -0.1% | -0.1% | 0.7% | -0.2% | 0.3% | 0.1%
Overall | -0.3% | -0.6% | -0.6% | -0.4% | -0.5% | -0.6%
 | -0.3% | -0.6% | -0.6% | -0.4% | -0.5% | -0.6%
Enc Time[%] | 91% |  |  | 90% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
Mult[%] | -3% |  |  | -3% |  | 
Adds[%] | -3% |  |  | -3% |  | 
Access[%] | -1% |  |  | -1% |  | 
MemBand(2D) Ave.[%] | 0% |  |  | 0% |  | 
MemBand(2D) Max.[%] | 5% |  |  | 6% |  | 
MemBand(1D) Ave.[%] | 0% |  |  | 0% |  | 
MemBand(1D) Max.[%] | 5% |  |  | 6% |  | 

## Slide 22: LP performance, THq=4, THe=2
R-D performance
  2.6% BD-rate gain
Complexity
  6~7% encoding time increase
  9~10% interpolation counts increase
  3% memory access increase
  0~1% memory bandwidth increase
Copyright © MediaTek Inc. All rights reserved.
<number>
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -1.6% | -1.7% | -2.1% | -1.4% | -2.0% | -1.9%
Class C | -3.1% | -2.7% | -2.9% | -2.7% | -3.3% | -3.5%
Class D | -4.8% | -4.5% | -5.3% | -4.6% | -5.3% | -6.0%
Class E | -1.6% | -1.4% | -0.5% | -0.7% | -1.2% | -0.8%
Overall | -2.8% | -2.6% | -2.8% | -2.4% | -3.0% | -3.1%
 | -2.8% | -2.6% | -2.8% | -2.4% | -3.0% | -3.1%
Enc Time[%] | 106% |  |  | 107% |  | 
Dec Time[%] | 102% |  |  | 102% |  | 
Mult[%] | 10% |  |  | 9% |  | 
Adds[%] | 10% |  |  | 9% |  | 
Access[%] | 3% |  |  | 3% |  | 
MemBand(2D) Ave.[%] | 0% |  |  | 1% |  | 
MemBand(2D) Max.[%] | 9% |  |  | 9% |  | 
MemBand(1D) Ave.[%] | 0% |  |  | 1% |  | 
MemBand(1D) Max.[%] | 9% |  |  | 9% |  | 

## Slide 23: Outline
PMVR without 1/8-pixel MV resolution
  Limited 1/4-pixel MV positions
  Modification of MVD derivation
  Experimental Results
  Threshold transmission
PMVR with 1/8-pixel MV resolution
  1/8-pixel interpolation filters
  Limited 1/4-pixel and 1/8-pixel MV positions
  Modification of MVD derivation
  Experimental Results
  Threshold transmission
Conclusions
Copyright © MediaTek Inc. All rights reserved.
<number>
Notes: <number>