## Slide 1: CE6 Subtest d: Direction based Angular Intra Prediction
JCTVC-G279
Presented by Xun Guo
7th JCT-VC Meeting in Geneva
21-30 Nov., 2011
Mei Guo, Xin Zhao, Xun Guo, and Shawmin Lei
MediaTek Inc.

## Slide 2: Summary
Report the results of F122 in CE6.d
Exploited direction-related information of angular intra prediction
  Gradient based prediction (VH:blue)
    Gradient along the direction
  Bi-boundary prediction (DGL:green)
    Reference samples
    at both ends of direction
Experimental Results
  BD-rate reduction of 0.7% for both HE-AI and LC-AI
  Similar running time to HM4.0

## Slide 3: Outline
Summary
Algorithm description
Harmonization in CE6.d
Experimental results
Conclusions

## Slide 4: Gradient based Prediction (1/2)
Vertical direction
0 ≤ j ≤ 2
Horizontal direction
0 ≤ i ≤ 2

## Slide 5: Gradient based Prediction (2/2)
v+1~v+3 (j=0)
h+1~h+3 (i=0)
RLi/RAj
  Reference of Li/Aj along the direction
  The same Interpolation as intra prediction is required for non-integer positions

## Slide 6: Bi-directional Prediction (1/2)
v+4~v+8
h+4~h+8

## Slide 7: Bi-directional Prediction (2/2)
Fij
  Reference at the other end of the direction
  Interpolation required for non-integer pixels
  Approximate positions used in interpolation
v+8/h+8: α(0)=1/2, α(1)=1/4, α(2)=1/8, α(3)=1/16, α(4…k)=0
v+7/h+7: α(0)=1/2, α(1…k)=0
v+4~v+6/h+4~h+6: α(0)=1/4, α(1…k)=0
  Decreased α due to decreased correlation
 | v+4 /h+4 | v+5 /h+5 | v+6 /h+6 | v+7 /h+7 | v+8 /h+8
d= | 32/13 | 32/17 | 32/21 | 32/26 | 1
d≈ | 9/4 | 7/4 | 3/2 | 5/4 | 1

## Slide 8: Experimental Results
Anchor – HM4.0
Test conditions – JCTVC-F900
Thank Sony and Toshiba for cross verifying our results (G361,G436, G565).
Category 1 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.58% | -0.57% | -0.60% | -0.52% | -0.60% | -0.64%
Class B | -0.41% | -0.39% | -0.38% | -0.41% | -0.48% | -0.47%
Class C | -0.37% | -0.36% | -0.38% | -0.40% | -0.43% | -0.41%
Class D | -0.35% | -0.33% | -0.40% | -0.40% | -0.37% | -0.38%
Class E | -0.55% | -0.58% | -0.64% | -0.50% | -0.64% | -0.68%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Overall | -0.44% | -0.44% | -0.47% | -0.44% | -0.50% | -0.51%
 | -0.44% | -0.44% | -0.48% | -0.44% | -0.50% | -0.52%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 

## Slide 9
Category 2 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.36% | -0.32% | -0.30% | -0.33% | -0.36% | -0.42%
Class B | -0.27% | -0.20% | -0.12% | -0.28% | -0.31% | -0.26%
Class C | -0.31% | -0.23% | -0.23% | -0.31% | -0.32% | -0.29%
Class D | -0.34% | -0.24% | -0.24% | -0.35% | -0.29% | -0.31%
Class E | -0.33% | -0.30% | -0.36% | -0.32% | -0.35% | -0.32%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Overall | -0.32% | -0.25% | -0.24% | -0.31% | -0.33% | -0.31%
 | -0.32% | -0.25% | -0.25% | -0.31% | -0.32% | -0.32%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
Category 1 and | All Intra HE |  |  | All Intra LC |  | 
Category 2 | Y | U | V | Y | U | V
Class A | -0.83% | -0.79% | -0.73% | -0.75% | -0.85% | -0.97%
Class B | -0.61% | -0.53% | -0.47% | -0.60% | -0.69% | -0.68%
Class C | -0.59% | -0.57% | -0.55% | -0.64% | -0.69% | -0.62%
Class D | -0.61% | -0.54% | -0.53% | -0.64% | -0.58% | -0.60%
Class E | -0.76% | -0.74% | -0.89% | -0.70% | -0.83% | -0.86%
Class F | #VALUE | #VALUE | #VALUE! | #VALUE! | #VALUE | #VALUE
Overall | -0.67% | -0.62% | -0.61% | -0.66% | -0.72% | -0.74%
 | -0.67% | -0.63% | -0.62% | -0.66% | -0.72% | -0.74%
Enc Time[%] | 101% |  |  | 102% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 10: Harmonization in CE6.d
Category 1
  v~v+2, h~h+2
  vertical and horizontal modes: 2 lines
Category 2
  Green:F122; red: F358/F456; blue:F456
Category 4
  Category 1 + Category 2 + Filtering of planar prediction (F358)

## Slide 11: Experimental Results
Anchor – HM4.0
Test conditions – JCTVC-F900
Thank Qualcomm and HiSilicon for cross verifying our harmonization results (G293,G790).

## Slide 12: Category 1
Three lines | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.54% | -0.52% | -0.52% | -0.49% | -0.52% | -0.59%
Class B | -0.40% | -0.40% | -0.33% | -0.40% | -0.45% | -0.45%
Class C | -0.36% | -0.33% | -0.34% | -0.39% | -0.42% | -0.38%
Class D | -0.35% | -0.32% | -0.36% | -0.38% | -0.36% | -0.34%
Class E | -0.52% | -0.50% | -0.61% | -0.48% | -0.59% | -0.60%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Overall | -0.43% | -0.41% | -0.42% | -0.42% | -0.46% | -0.46%
 | -0.43% | -0.42% | -0.43% | -0.42% | -0.46% | -0.47%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 102% |  | 
Two lines | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.52% | -0.45% | -0.46% | -0.47% | -0.48% | -0.57%
Class B | -0.34% | -0.33% | -0.31% | -0.35% | -0.42% | -0.40%
Class C | -0.35% | -0.30% | -0.33% | -0.38% | -0.40% | -0.38%
Class D | -0.33% | -0.35% | -0.39% | -0.36% | -0.30% | -0.36%
Class E | -0.49% | -0.54% | -0.56% | -0.46% | -0.54% | -0.55%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Overall | -0.40% | -0.38% | -0.40% | -0.40% | -0.42% | -0.45%
 | -0.40% | -0.38% | -0.41% | -0.40% | -0.42% | -0.45%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 97% |  | 
One line | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.42% | -0.34% | -0.35% | -0.37% | -0.39% | -0.47%
Class B | -0.31% | -0.27% | -0.26% | -0.32% | -0.36% | -0.34%
Class C | -0.34% | -0.29% | -0.29% | -0.37% | -0.38% | -0.35%
Class D | -0.34% | -0.36% | -0.33% | -0.37% | -0.33% | -0.33%
Class E | -0.44% | -0.30% | -0.39% | -0.44% | -0.39% | -0.42%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Overall | -0.37% | -0.31% | -0.32% | -0.37% | -0.37% | -0.38%
 | -0.37% | -0.31% | -0.32% | -0.37% | -0.37% | -0.38%
Enc Time[%] | 100% |  |  | 101% |  | 
Dec Time[%] | 96% |  |  | 99% |  | 

## Slide 13: Category 2
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.40% | -0.46% | -0.39% | -0.38% | -0.41% | -0.47%
Class B | -0.27% | -0.19% | -0.17% | -0.28% | -0.32% | -0.30%
Class C | -0.33% | -0.26% | -0.27% | -0.34% | -0.35% | -0.31%
Class D | -0.33% | -0.28% | -0.28% | -0.34% | -0.27% | -0.27%
Class E | -0.33% | -0.33% | -0.38% | -0.33% | -0.39% | -0.38%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Overall | -0.33% | -0.29% | -0.29% | -0.33% | -0.35% | -0.34%
 | -0.33% | -0.30% | -0.29% | -0.33% | -0.35% | -0.34%
Enc Time[%] | 101% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 101% |  | 

## Slide 14: Category 4
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.93% | -0.82% | -0.86% | -0.83% | -0.98% | -1.12%
Class B | -0.63% | -0.60% | -0.59% | -0.57% | -0.78% | -0.78%
Class C | -0.64% | -0.65% | -0.66% | -0.68% | -0.77% | -0.73%
Class D | -0.66% | -0.64% | -0.65% | -0.70% | -0.69% | -0.73%
Class E | -0.80% | -0.70% | -0.87% | -0.75% | -0.88% | -0.92%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Overall | -0.72% | -0.68% | -0.71% | -0.70% | -0.82% | -0.85%
 | -0.73% | -0.69% | -0.71% | -0.70% | -0.82% | -0.85%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 

## Slide 15: Conclusions
Reported the results of F122
Harmonized with other contributions in CE6.d
Experimental Results:
  BD-rate reduction of 0.7% for both HE-AI and LC-AI
  Similar running time to HM4.0

## Slide 16
Thank you!

## Slide 17: Results of Random Access (F122 method)
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.36% | 0.05% | -0.33% | -0.29% | -0.44% | -0.10%
Class B | -0.29% | -0.23% | -0.27% | -0.27% | -0.41% | -0.23%
Class C | -0.32% | -0.33% | -0.39% | -0.29% | -0.34% | -0.31%
Class D | -0.25% | -0.17% | -0.39% | -0.26% | -0.34% | -0.22%
Class E |  |  |  |  |  | 
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Overall | -0.31% | -0.17% | -0.34% | -0.28% | -0.39% | -0.22%
 | -0.30% | -0.21% | -0.36% | -0.28% | -0.38% | -0.23%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 18: Results of Low Delay (F122 method)
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.09% | -0.34% | -0.60% | -0.11% | -0.14% | -0.25%
Class C | -0.12% | -0.44% | -0.29% | -0.19% | -0.27% | -0.29%
Class D | -0.11% | -0.41% | 0.04% | -0.13% | -0.05% | -0.44%
Class E | 0.11% | -0.77% | 0.27% | -0.10% | -0.53% | -0.92%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Overall | -0.07% | -0.46% | -0.20% | -0.13% | -0.22% | -0.43%
 | -0.06% | -0.41% | -0.19% | -0.13% | -0.20% | -0.44%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 99% |  |