## Slide 1: Boundary-Dependent Transform for Inter-Predicted Residue
Jicheng An, Xin Zhao, Xun Guo and Shawmin Lei
JCTVC-G281
Copyright © MediaTek Inc. All rights reserved.
Presented by Xiang Li
7th JCT-VC Meeting in Geneva
21-30, Nov., 2011
Notes: <number>

## Slide 2: Outline
Error distribution in a inter PU
Relation between DCT-IV and DCT-II
Boundary-dependent transform
Experimental Results
Conclusion
Copyright © MediaTek Inc. All rights reserved.
<number>
Notes: <number>

## Slide 3: Inter prediction error in a PU
Energy distribution of inter prediction error
  Energy distribution in a 4x4 inter PU
  Prediction errors are larger near the PU boundaries than in the middle of the PU
  The reason of this effect may be the different MVs between two neighboring PUs
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 4: Inter prediction error in a split PU
One PU is split into multiple TUs
  The error are larger near PU boundaries than near interior TU (non-PU) boundaries.
  The error distribution in TU at the top left corner. (basically decrease from left to right and from top to bottom)
  Prediction error is input of transform, as a result of the uneven error distribution, there is a potential for transform improvement.
    DST-VII and DCT-IV can adapt this distribution better than DCT-II
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 5: Boundary-Dependent Transform
Proposed
  Table 1. 4-point transform mapping (using DST-VII ).
  Table2. 8-point and 16-point transform mapping (using DCT-IV).
  F(DST-VII): Flip the DST-VII matrix from left to right
  F(DCT-IV): Flip the DCT-IV matrix from left to right
Copyright © MediaTek Inc. All rights reserved.
<number>
TU Boundary |  | Horizontal Trans. | TU Boundary |  | Vertical Trans.
Left | Right |  | Top | Bottom | 
non-PU | PU | DST-VII | non-PU | PU | DST-VII
PU | non-PU | F(DST-VII) | PU | non-PU | F(DST-VII)
PU | PU | DCT-II | PU | PU | DCT-II
non-PU | non-PU | DCT-II | non-PU | non-PU | DCT-II
TU Boundary |  | Horizontal Trans. | TU Boundary |  | Vertical Trans.
Left | Right |  | Top | Bottom | 
non-PU | PU | F(DCT-IV) | non-PU | PU | F(DCT-IV)
PU | non-PU | DCT-IV | PU | non-PU | DCT-IV
PU | PU | DCT-II | PU | PU | DCT-II
non-PU | non-PU | DCT-II | non-PU | non-PU | DCT-II

## Slide 6: Boundary-dependent transform
0.2% gain for RAHE and RALC.
0.5% gain for LDHE and LDLC.
Similar run time.
No new transform implemented
Copyright © MediaTek Inc. All rights reserved.
<number>
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -0.1% | -0.1% | -0.3% | 0.1% | 0.1%
Class B | -0.2% | 0.2% | 0.3% | -0.2% | 0.1% | 0.1%
Class C | -0.2% | 0.0% | 0.1% | -0.2% | 0.1% | 0.1%
Class D | -0.2% | 0.0% | 0.1% | -0.2% | 0.0% | 0.0%
Class E |  |  |  |  |  | 
Overall | -0.2% | 0.0% | 0.1% | -0.2% | 0.1% | 0.1%
 | -0.2% | 0.0% | 0.1% | -0.2% | 0.1% | 0.1%
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.5% | 0.1% | 0.1% | -0.5% | 0.2% | 0.0%
Class C | -0.5% | -0.2% | 0.0% | -0.5% | 0.2% | -0.2%
Class D | -0.4% | 0.5% | 0.1% | -0.4% | 0.2% | 0.2%
Class E | -0.5% | 0.2% | 0.3% | -0.6% | 0.6% | -0.2%
Overall | -0.5% | 0.1% | 0.1% | -0.5% | 0.3% | 0.0%
 | -0.5% | 0.2% | 0.1% | -0.5% | 0.2% | 0.0%

## Slide 7: Conclusion
Suggest to adopt this boundary-dependent transform into HEVC
  4-point DST-VII, 8-point and 16-point DCT-IV
  0.2% BD-rate gain for RA, 0.5% gain for LD
  Similar run time.
  No new transform implemented.
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 8
Copyright © MediaTek Inc. All rights reserved.
Thank you
Notes: <number>

## Slide 9: DST-VII and DCT-IV
The 4-point DST-VII has been in current HEVC (for intra coding)
The 8-point and 16-point DCT-IV are actually part of 32-point DCT-II which has been in HEVC.
  N-point DCT-II
  N-point DCT-IV
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 10: Relation between DCT-II and DCT-IV
Regrouping the terms f[n] and f[N-1-n] of a DCT-II yields：
The even index coefficients of the DCT-II are thus equal to the DCT-II of N/2-pt signal f[n]+f[N-1-n].
The odd index coefficients of the DCT-II are equal to the DCT-IV of N/2-pt signal f[n]-f[N-1-n].
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 11: Relation between DCT-II and DCT-IV
Butterfly structure for N-point DCT-II
Therefore, the 8-point and 16-point DCT-IV reuse the implementation of existing 32-point DCT-II and hence new transforms need not be implemented.
In CE10, DCT-IV can be realized by full-factorized fast algorithm.
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 12: Example
For example, when a 8x8 PU is split into four 4x4 TUs, the transform should be taken as
When a 16x16 PU is split into four 8x8 TUs, the transform should be taken as
Copyright © MediaTek Inc. All rights reserved.
<number>
TU | Horizontal Trans. | Vertical Trans.
TU0 | F(DST-VII) | F(DST-VII)
TU1 | DST-VII | F(DST-VII)
TU2 | F(DST-VII) | DST-VII
TU3 | DST-VII | DST-VII
TU | Horizontal Trans. | Vertical Trans.
TU0 | DCT-IV | DCT-IV
TU1 | F(DCT-IV) | DCT-IV
TU2 | DCT-IV | F(DCT-IV)
TU3 | F(DCT-IV) | F(DCT-IV)

## Slide 13: Use Table 1 (DST-VII) for 4,8,16-pt Transform
0.2%~0.3% gain for RA.
0.5% gain for LD.
Similar run time.
High complexity
  New transforms for 8-pt and 16-pt DST-VII
  Matrix multiplication
Copyright © MediaTek Inc. All rights reserved.
<number>
 | Random Acess HE |  |  | Random Acess LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.3% | -0.1% | -0.2% | -0.4% | -0.1% | -0.2%
Class B | -0.2% | 0.1% | 0.1% | -0.3% | 0.1% | 0.2%
Class C | -0.2% | 0.0% | 0.0% | -0.2% | 0.1% | 0.0%
Class D | -0.2% | 0.1% | 0.0% | -0.3% | 0.0% | 0.1%
Class E |  |  |  |  |  | 
Overall | -0.2% | 0.0% | 0.0% | -0.3% | 0.0% | 0.0%
 | -0.2% | 0.0% | 0.0% | -0.3% | 0.0% | 0.0%
Enc Time[%] | 103% |  |  | 103% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.5% | -0.1% | -0.2% | -0.6% | 0.1% | 0.1%
Class C | -0.5% | 0.0% | -0.2% | -0.5% | 0.3% | 0.0%
Class D | -0.4% | 0.1% | 0.0% | -0.4% | 0.3% | -0.1%
Class E | -0.6% | 0.3% | 0.8% | -0.6% | 0.8% | 0.2%
Overall | -0.5% | 0.0% | 0.0% | -0.5% | 0.3% | 0.0%
 | -0.5% | 0.0% | 0.0% | -0.5% | 0.3% | 0.1%
Enc Time[%] | 102% |  |  | 102% |  | 
Dec Time[%] | 101% |  |  | 101% |  |