## Slide 1: Non-CE7: Mode-Dependent DCT/DST for Chroma
Xin Zhao, Xun Guo, Mei Guo, Shawmin Lei, Siwei Ma and Wen Gao
MediaTek Inc.
Presented by Xun Guo
7th JCT-VC Meeting in Geneva
21-30 November, 2011
Notes: <number>

## Slide 2: Overall Summary
Mode-dependent DCT/DST method is proposed to be extended to 4x4 chroma blocks
Experimental results
  Based on HM4.0 and test conditions of JCTVC-F900
  Average BD-rate reductions of 0.0%, -0.6% and -0.7% for HE-AI
  Average BD-rate reductions of 0.0%, -1.1% and -1.2% for LC-AI
Run time
  Almost the same as that of HM4.0
<number>

## Slide 3: Outline
Introduction
Proposed method
Simulation results
Conclusions
<number>
Notes: <number>

## Slide 4: Mode-dependent DCT/DST in HM4.0
For 4x4 Luma blocks only
The selection of column and row transform matrices is determined by it’s intra prediction mode
<number>
DST Matrix: 1
DCT Matrix: 0

## Slide 5: DCT/DST Selection
Vertical and horizontal transform is selected according to a look-up-table
  DST: 1 DCT: 0
  In HM4.0, DCT/DST is applied only for 4x4 luma blocks
<number>
Mode | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35
Ver | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
Hor | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0

## Slide 6: Chroma Inta mode
In HM4.0, 6 chroma intra modes
  Horizontal, Vertical, Planar, DC, DM, LM
  If one of Horizontal, Vertical, Planar, DC is equal to DM, it is replaced by Right-down diagonal
For all chroma modes, only DCT is used
<number>

## Slide 7: Outline
Introduction
Proposed method
Simulation results
Conclusions
Copyright © MediaTek Inc. All rights reserved.
<number>
Notes: <number>

## Slide 8: Solution 1
<number>
Chroma mode | Horizontal Transform | Vertical Transform
DM= Planar | DCT | DCT
DM≠Planar | DCT | DCT
LM | DCT | DCT
Planar | DCT | DCT
Horizontal | DST | DCT
Vertical | DCT | DST
DC | DCT | DCT
right-down diagonal mode | DCT | DCT

## Slide 9: Solution 2
<number>
Chroma mode | Horizontal Transform | Vertical Transform
DM= Planar | DST | DST
DM≠Planar | DCT | DCT
LM | DCT | DCT
Planar | DST | DST
Horizontal | DCT | DCT
Vertical | DCT | DCT
DC | DCT | DCT
right-down diagonal mode | DCT | DCT

## Slide 10: Solution 3
<number>
Chroma mode | Horizontal Transform | Vertical Transform
DM= Planar | DST | DST
DM≠Planar | DCT | DCT
LM | DCT | DCT
Planar | DST | DST
Horizontal | DCT | DCT
Vertical | DCT | DCT
DC | DCT | DCT
right-down diagonal mode | DCT | DST

## Slide 11: Solution 4
<number>
Chroma mode | Horizontal Transform | Vertical Transform
DM= Planar | DST | DST
DM≠Planar | DCT | DCT
LM | DCT | DCT
Planar | DST | DST
Horizontal | DST | DCT
Vertical | DCT | DST
DC | DCT | DCT
right-down diagonal mode | DCT | DST

## Slide 12: Outline
Introduction
Proposed method
Simulation results
Conclusions
<number>
Notes: <number>

## Slide 13: Simulation Results
Anchor – HM4.0
Solution 1, 2, 3 and 4
Test condition: HE-AI and LC-AI
Thank Samsung for crosschecking (JCTVC-G879)
<number>

## Slide 14: Simulation Results
Solution 1
<number>
 | Intra, HE |  |  | Intra, Loco |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.2% | -0.2% | 0.0% | -0.3% | -0.4%
Class B | 0.0% | -0.3% | -0.3% | 0.0% | -0.5% | -0.5%
Class C | 0.0% | -0.4% | -0.6% | 0.0% | -0.8% | -0.9%
Class D | 0.0% | -0.7% | -0.8% | 0.0% | -0.9% | -1.1%
Class E | 0.0% | -0.1% | -0.2% | 0.0% | -0.3% | -0.5%
All Avg | 0.0% | -0.4% | -0.4% | 0.0% | -0.6% | -0.7%

## Slide 15: Simulation Results
Solution 2
<number>
 | Intra, HE |  |  | Intra, Loco |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.3% | -0.2% | 0.0% | -0.6% | -0.5%
Class B | 0.0% | -0.5% | -0.5% | 0.0% | -0.9% | -0.8%
Class C | -0.1% | -0.7% | -0.8% | -0.1% | -1.1% | -1.2%
Class D | -0.1% | -0.9% | -1.0% | -0.1% | -1.3% | -1.4%
Class E | 0.0% | 0.0% | -0.3% | 0.0% | -0.5% | -0.9%
All Avg | 0.0% | -0.5% | -0.6% | -0.1% | -0.9% | -1.0%

## Slide 16: Simulation Results
Solution 3
<number>
 | Intra, HE |  |  | Intra, Loco |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.4% | -0.3% | 0.0% | -0.6% | -0.5%
Class B | 0.0% | -0.6% | -0.5% | 0.0% | -0.9% | -0.8%
Class C | -0.1% | -0.7% | -0.9% | -0.1% | -1.1% | -1.3%
Class D | -0.1% | -1.0% | -1.1% | -0.1% | -1.3% | -1.5%
Class E | 0.0% | -0.1% | -0.3% | 0.0% | -0.5% | -0.9%
All Avg | 0.0% | -0.6% | -0.6% | -0.1% | -0.9% | -1.0%

## Slide 17: Simulation Results
Solution 4
<number>
 | Intra, HE |  |  | Intra, Loco |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.4% | -0.3% | 0.0% | -0.7% | -0.7%
Class B | 0.0% | -0.6% | -0.6% | 0.0% | -1.1% | -1.0%
Class C | -0.1% | -0.8% | -1.1% | -0.1% | -1.4% | -1.5%
Class D | -0.1% | -1.2% | -1.3% | -0.1% | -1.6% | -1.8%
Class E | 0.0% | -0.1% | -0.3% | 0.0% | -0.5% | -1.1%
All Avg | 0.0% | -0.6% | -0.7% | 0.0% | -1.1% | -1.2%
Enc Time (%) | 99% |  |  | 100% |  | 
Dec Time (%) | 97% |  |  | 97% |  | 

## Slide 18: Simulation Results
Solution 4
<number>
 | RA, HE |  |  | RA, Loco |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | -0.6% | -0.7% | 0.0% | -0.7% | -0.9%
Class B | 0.0% | -1.0% | -1.1% | 0.0% | -1.0% | -0.9%
Class C | 0.0% | -1.0% | -1.0% | 0.0% | -1.2% | -1.2%
Class D | 0.0% | -0.9% | -1.6% | 0.0% | -1.2% | -0.9%
Class E |  |  |  |  |  | 
All Avg | 0.0% | -0.9% | -1.1% | 0.0% | -1.0% | -1.0%
Enc Time (%) | 100% |  |  | 100% |  | 
Dec Time (%) | 100% |  |  | 101% |  | 

## Slide 19: Conclusions
Mode-dependent DCT/DST is extended to 4x4 chroma
Average BD-rate reductions of
  0.0%, -0.6% and -0.7% for HE-AI
  0.0%, -1.1% and -1.2% for LC-AI
  0.0%, -0.9% and -1.1% for HE-RA
  0.0%, -1.0% and -1.0% for LC-RA
The run time is almost the same as that of HM4.0
<number>

## Slide 20
Thank you
Notes: <number>